## Slide 1: ITSS TRAINING
Router 101
And
Networking Basics

## Slide 2: You Don’t Need Internet Access to Run
Connect your devices to an Ethernet switch or Router
Enable DHCP on your router or…
Set Static IP Addresses on computers and printer if using a switch
Copy files to a thumb drive for uploads and downloads

## Slide 3: To Connect to Another Network or the Internet, You Need a Router
Your Router is ‘THE BOSS’ of
Your Network

## Slide 4: The Router Manages:
Connection to your Internet Service Provider
IP Addressing via DHCP
Usually up to 4 Clients
Security – Firewall
Wireless Access Point
And a bunch of other stuff….

## Slide 5: Router ports run at 100/1000 Mbps

## Slide 6: Router Speed Continued
For small networks, the router ports are acceptable
For larger networks, and for big data users like GIS, connect a Gigabit ethernet switch to increase internal network speed

## Slide 7: Simple Network Layout

## Slide 8: Ethernet Switch Notice – No Port to Internet

## Slide 9: Ethernet Switches
Run at 100 Mbps or 1 Gbps
Pass data packets to the destination device with no error checking
Smart enough to know what’s connected to it so cuts router traffic
Older Hubs are much slower due to 10 Mbps speed and error checking

## Slide 10: When you configure a router, be sure to:
Create a new admin password
Change the Admin Username (if possible)
Enable the Firewall
Disable Remote Management
Disable Wireless until it is needed
Set WiFi to the highest security that your devices can handle

## Slide 11: If you don’t know the router’s address…
Plug your computer into an ethernet port on your router
Make sure your computer is set to receive an IP address automatically
The computer will receive an IP address
At the command prompt:
  ipconfig
  ipconfig /release
  ipconfig /renew
  ipconfig /all

## Slide 12: ipconfig

## Slide 13: ipconfig /release

## Slide 14: ipconfig /renew

## Slide 15: ipconfig /all

## Slide 16: If All That Fails
Go to the manufacturer’s website on another device (hard to do if no internet!)
Or dig out the manual
Reset the router
Try again

## Slide 17: Don’t know the router password?

## Slide 18: Use a web browser to access the router setup
This is the default gateway

## Slide 19: Basic Setup

## Slide 21: Enable DHCP and choose an IP address Scheme

## Slide 22: IP Addresses
10.6.3.X (10.REGION.TEAM.X)
192.168.2.X
Best NOT to use 192.168.1.X -- this can conflict with ISP address handed to your router

## Slide 23: Enabling WiFi

## Slide 24: Wireless Security Settings

## Slide 25: Wireless Speed Settings

## Slide 26: Check the Client Table Often

## Slide 27: Simple Network Layout

## Slide 31: Questions?