## Slide 1
Making and Testing Ethernet Cables

## Slide 2: EIA/TIA-568A and 568B Cables
EIA/TIA-568 Commercial Building Telecommunications Wiring Standard
Telecommunications Industry Association (TIA) http://www.tiaonline.org.

## Slide 3
CATx CABLE QUICK FACTS

## Slide 4
Cable - you can buy a 1000 feet roll of Cat 5/6 cable at computer stores or datacomm supply companies. Get the good stuff.
Solid wire - each one of the 8 wires inside the cable consists of one solid wire. It has better conductivity than stranded cable, which means you can run ethernet over farther distances.
Stranded wire - each one of the 8 wires inside the cable consists of a few dozen very fine hair-like strands that bend and flex very easily.

## Slide 5: We’ll Go Through These Steps
Measure
Strip
Untwist
Order
Trim
Punch
Repeat
Test

## Slide 6
RJ-45 connectors usually come in bags of 50, 100 etc.
Two different kind of RJ-45 connectors – for solid or stranded wire cables
Using the wrong kind will likely result in a bad connection

## Slide 7
8 wire – STRANDED (wire) = 2 “Teeth”
8 wire – SOLID (wire) = 1 “Tooth”
RJ Connectors
RJ = Registered Jack
2 “TEETH”
Stranded (or Solid)
Versus

## Slide 8
Ratcheting Crimping tool - the crimpers will pay for themselves after you make a few cables.
A good crimping tool has a pair of wire cutters built in, as well as a blade to strip insulation.

## Slide 9
Cut a piece of Cat 5 as long as you need. Remember: Measure twice, cut once. Don’t be afraid to leave some slack
Make sure the cut on each end is clean and straight.

## Slide 10
Strip about an inch of the insulation off the cable. Cut it back square. Some crimping tools come with a built-in wire stripper
It is extremely important that you only cut the plastic insulation/jacket and not the wire.
Damaging one of the 8 wires, even if you just nick it or partially cut it, will ruin your cable.

## Slide 11
Untwist the wires. You'll notice that there are 4 pairs of multi-colored wires inside. Sort the pairs by color.
You should see wires color coded as follows: blue/blue-stripe, orange/orange-stripe, green/green-stripe, brown/brown-stripe.

## Slide 12
Align the wires in the following order
orange stripe
orange
green stripe
blue
blue stripe
green
brown stripe
brown

## Slide 13
Clip off the tops so that the wires are all the same length and stick out about ¾ of an inch from the insulation.
orange stripe
orange
green stripe
blue
blue stripe
green
brown stripe
brown

## Slide 14
Hold an RJ-45 connector clip down
Insert the sorted and aligned wires carefully into the RJ-45 connector
Verify that the wires are still in the correct order.
Make sure that the wires have gone all the way into and are touching the end of the RJ-45 connector. Now push the jacket as far as it will go into the connector.

## Slide 15: RIGHT!

## Slide 16: WRONG!

## Slide 17
Insert the RJ-45 connector into the crimping tool.
Squeeze the handle.
You will know you’re done when the tool releases.

## Slide 18: You’re ½ Way There!
Repeat this procedure to put a 568B connector on the other end of the cable.
Use the same wire order as on the first end
This will make a straight-through cable.

## Slide 19: EIA/TIA 568A 568B

## Slide 20: Test Your Cables
Test all cables before you install them. It saves hours of data chasing later.
Find a bad cable? Repair it or cut it and toss in the trash. You don’t want broken cables in your kit.

## Slide 21: Follow These Easy Steps
Measure
Strip
Untwist
Order
Trim
Punch
Repeat
Test
http://www.pcnineoneone.com/howto/cat5diy1.html
TEST
Never Install A Cable
You Have Not Tested