## Slide 1: Incident Hardware

## Slide 2: We Do Not Endorse or Recommend Any Vendor

## Slide 3: Overview
Equipment We Use
Document
BPA’s
Routers
Switches
Network Layout
Workstations
Printers and Plotters
GPS Devices

## Slide 4: Equipment We Use
Routers
Switches
Servers
Workstations
Network Attached Storage (NAS)
Printers and Print Servers
Plotters
GPS Devices
Satellite Transceivers
Mobile Devices

## Slide 5: Document It
Record any and all bits of information regarding your
network
Get in the habit of doing it now
IP addresses, passwords, property location, phone
numbers
Transition documentation

## Slide 6: BPA’s
Nationwide or Regional Rental Agreements
Negotiated With Hartford, Smart Source, and Spectrum
Fire, GIS, FBAN and e-ISuite server Computer
Configurations, iPad, networking equipment, Peripherals
(new National Standard being developed)
Check With Your Finance Chief for the latest
Agreements

## Slide 7: Let’s Start With the Router
A router is a device that forwards traffic between networks and subnetworks --- yours and the Internet, for instance.
It is the _______ of your network
One per network/subnetwork
Can provide wired or wireless access to networkable devices
Provides DHCP

## Slide 8: Router Configuration
Set the admin id and password
Configure WAN Port (the connection to your ISP)
Enable DHCP
Disable wireless access until/unless needed
Reserve a block of static IP addresses for printers, servers,
etc.
Set the DHCP range
Document ad nauseum

## Slide 9: Switches
A Switch is a device that connects networkable devices
Star topology
Uplink or auto-sensing
Last port link or uplink -- careful

## Slide 10: Star Topology
Switch
Home Runs
From Central
Server Location
To Individual
“Yurts/Trailers”
Switches w/in
“Yurts” To Connect
PCs w/in “Yurt”

## Slide 11: Tree or Daisy-Chain

## Slide 12: Typical Network Setup in an ICP

## Slide 13
Typical Network Setup in a
Type 3 to Type 2 to Type 1
Fire Camp
DON’T DO THIS TO THE INCOMING ITSS

## Slide 14
DO THIS

## Slide 15: What Kind of Workstations?
Rentals
Agency Imaged
Agency Non-imaged
DO NOT LET Personal Equipment ON YOUR
NETWORK

## Slide 16: Keep Your Network Virus Free
Check for Antivirus currency
Don’t put your network at risk
NIMDA at Lakeview Complex
LUVSAN at B & B

## Slide 17: Configure Workstations
DHCP enabled router: set TCP/IP to automatically obtain an IP address and DNS server addresses
Join the appropriate workgroup or domain
Do not UNJOIN Agency PCs
from Their Domain

## Slide 18: Workgroup or Domain

## Slide 19: Not Networked?
Check Connections
Start  Run  cmd
Ipconfig {/all /release /renew}
Check NIC Configuration
      Enabled?
      DHCP Enabled?

## Slide 20: Printers and Plotters
Avoid “Sharing” Printers
Use print servers like JetDirect or D-Link
Use the latest Drivers and BIOS
Static or Reserved IPs
Only set up plotters for users that need them – plotters are a precious commodity

## Slide 21: Summary
Equipment We Use
Document
BPA
Router Setup
Switches
Network Layout
Workstations
Printers and Plotters
GPS Devices
Mobile Devices