## Slide 1: Wireless Networks
                2017 ITSS Course

## Slide 2: Equipment
Wireless Router
Access Point
Wireless Bridge
LAN Switch (higher port density)
Wireless Client

## Slide 3: OSI Model
Notes: Lower levels:
L1 – copper for glass cable or RF
L2 – MAC address broadcast
L3 – Routing to different LAN and WAN
Upper Layers (L4-L7)
  TCP UDP IP

## Slide 4: Wireless Router
WAN port
Gateway to Internet Service Provider (ISP)
DSL modem provided by ISP
Dynamic Host Configuration Protocol (DHCP)
Limited LAN ports (4 ports is common)
Firewall capability

## Slide 5: Access Point
One LAN port connection
No WAN port (can not connect to ISP)
Extends your LAN through the radio spectrum
Power over Ethernet (PoE)
IEEE 802.11(a, b, g, n, ac) standard

## Slide 6: Wireless Bridge
Point to Point implementation that extends one LAN segment to another LAN segment
Instead of using cables, Radio waves are used as a conduit
  Consist of more than one wireless station
Layer 2 of the OSI model using MAC addresses
Does not see IP addresses, therefore not routable
Ex: Connects two adjacent building in a campus

## Slide 7: Wireless Clients
Laptops
Tablets
Mobile Phone
Printers
and Internet-of-Things (refrigerators, cars, home security system)

## Slide 8: Bridge Pair

## Slide 9: McClellan Dorms APs

## Slide 10: McClellan Dorms Bridges

## Slide 11: 802.11a
Operates in the 5.15GHz to 5.35GHz radio spectrum.
Speed: Up to 54Mbps (actual throughput is closer to 22Mbps)
Range: 115 feet indoor
Less prone to interference.
More expensive.
Because 802.11b and 802.11a use different radio technologies and portions of the spectrum, they are incompatible with one another.

## Slide 12: 802.11b
Operates in the 2.4GHz radio spectrum
Speed: Up to 11Mbps
Range: 115 feet indoor
Prone to interference (it shares airspace with cell phones, Bluetooth, security radios, and other devices).
Least expensive wireless LAN specification

## Slide 13: 802.11g
Operates in the 2.4GHz radio spectrum.
Speed: Up to 54Mbps
Range: 125 feet indoor
Prone to interference (it shares airspace with cell phones, Bluetooth, security radios, and other devices).

## Slide 14: 802.11n
Operates in the 2.4 or 5GHz radio spectrum
Speed: Up to 700Mbs
Range: 230 feet indoor
Because 802.11b and 802.11g use the same radio technologies and portions of the spectrum, they are compatible with one another.

## Slide 15: 802.11ac
Bandwidth: Up to 1000 Mb/s (multi-station) or 500 Mb/s (single-station)
Range: 115 feet indoor
Beamforming (targets clients)
Frequency range: 5.0 GHz
Multi-user MIMO
Spatial Streams
Notes: Bandwidth: Up to 1000 Mb/s (multi-station) or 500 Mb/s (single-station).
Beamforming: A signal processing technique used in antenna arrays for directional signal transmission or reception is now standard.
Multi-user MIMO: A technology that directs independent data streams to multiple devices is employed in 802.11ac devices.
Spatial Streams: A transmission technique used by MIMO to transmit independent data signals from each of the multiple transmit antennas. 802.11ac devices can use eight streams versus four streams for 802.11n.

## Slide 16: 802.11ac
 | IEEE 802.11n | IEEE 802.11ac
Frequency Band | 2.4 Ghz and 5 Ghz | 5 GHz only
Channel Widths | 20, 40 Mhz | 20, 40, 80 Mhz 160 Mhz optional
Spatial Streams | 1 to 4 | 1 to 8 total Up to 4 per client
Multi-user MIMO | No | Yes
Single Stream (1x1) Maximum Client Data Rate | 150 Mbps | 450 Mbps
Three Stream (3x3) Maximum Data Rate | 450 Mbps | 1.3 Gbps

## Slide 17: Exercise 1 - AP Bridge
PicoStation2 setup in bridge mode
  Extend your Cat5 LAN with WLAN
  IP addresses of your WLAN is in the same broadcast domain as your wired LAN
  ISP router will provide DHCP and DNS services
  Try using open network and WEP key for encryption
  Test all your clients for connectivity

## Slide 18: Exercise 2 - AP as Router
PicoStation2 setup in router mode
  Extend your Cat5 LAN with WLAN but this time create another LAN just for WiFi
  IP addresses of your WLAN is in a different broadcast domain than your wired LAN
  Your AP will provide DHCP and DNS services inherited from ISP’s router
  Use WPA2 / AES
  Test all your clients for connectivity