## Slide 1: System Access Needed by an ITSS System Access Needed by an ITSS
System Access Needed by an ITSS
Wireless Networks
2018 ITSS Course

## Slide 2: Equipment
Wireless Router
Access Point
Wireless Bridge
LAN Switch (higher port density)
Wireless Client (endpoints)

## Slide 3: OSI Model

## Slide 4
Wireless Router
One WAN port
Gateway to Internet Service Provider (ISP)
DSL modem provided by ISP
Dynamic Host Configuration Protocol (DHCP)
Limited LAN ports (4 ports is common)
Firewall capability

## Slide 5: Access Point
One LAN port connection
No WAN port (can not connect to ISP)
Extends your LAN through the radio spectrum
Power over Ethernet (PoE)
IEEE 802.11(a, b, g, n, ac) standard

## Slide 6
Wireless Bridge
Point to Point implementation that extends one LAN segment to another LAN segment
Instead of using cables, Radio waves are used as
a conduit
  Consist of more than one wireless station
Layer 2 of the OSI model using MAC addresses
Does not see IP addresses, therefore not routable
Ex: Connects two adjacent building in a campus

## Slide 7: Wireless Clients
Laptops
Tablets
Mobile Phone
Printers
and Internet-of-Things (TVs, Refrigerators, Cars, Home Security System, smart speakers)

## Slide 8
Bridge Pair

## Slide 9: McClellan Dorms APs

## Slide 10: McClellan Dorms Bridges

## Slide 11: 802.11a
Operates in the 5.15GHz to 5.35GHz radio spectrum.
Speed: Up to 54Mbps (actual throughput is closer to 22Mbps)
Range: 115 feet indoor
Less prone to interference.
More expensive.
Because 802.11b/g/n and 802.11a use different radio technologies and portions of the spectrum, they are incompatible with one another.

## Slide 12: 802.11b
Operates in the 2.4GHz radio spectrum
Speed: Up to 11Mbps
Range: 115 feet indoor
Prone to interference (it shares airspace with cell phones, Bluetooth, security radios, and other devices).
Least expensive wireless LAN specification

## Slide 13: 802.11g
Operates in the 2.4GHz radio spectrum.
Speed: Up to 54Mbps
Range: 125 feet indoor
Prone to interference (it shares airspace with cell phones, Bluetooth, security radios, and other devices).

## Slide 14: 802.11n
Operates in the 2.4 or 5GHz radio spectrum
Speed: Up to 700Mbs
Range: 230 feet indoor
Because 802.11b and 802.11g use the same radio technologies and portions of the spectrum, they are compatible with one another.

## Slide 15: 802.11ac
Bandwidth: Up to 1000 Mb/s (multi-station) or 500 Mb/s (single-station)
Range: 115 feet indoor
Beamforming (targets clients)
Frequency range: 5.0 GHz
Multi-user MIMO
Up to 8 Spatial Streams
4 Emerging Wireless Standards

## Slide 16: 802.11ac

## Slide 17: Exercise 1 - UniFi AC MESH
UniFi AC setup as Access Point
  Extend your Cat5 LAN with WLAN
  IP addresses of your WLAN is in the same broadcast domain as your wired LAN
  ISP router will provide DHCP and DNS services
  Setup your UniFi Controller software
  Test all your clients for connectivity

## Slide 18: Exercise 2 - Bridge
UniFi Mesh AP as Bridge
  Team up with another group
  One Team will be Base Camp and other Team will be Remote Camp
  Reverse Team roles