| INCIDENT RADIO COMMUNICATIONS PLAN | Incident Name ANGORA INCIDENT | Date/Time Prepared 6/27/07 2100 | Operational Period Date/Time 6/28/2007 06:00 to 18:00 |
| --- | --- | --- | --- |
| Ch # | Function | Channel Name/Trunked Radio System Talkgroup | Assignment | RX Freq N or W | RX Tone/NAC | TX Freq N or W | Tx Tone/NAC | Mode | Remarks |
| 1 | NIRSC | NIFC TAC-1 | DIV A/B | 168.0500 N |  | 168.0500 N |  | A |  |
| 2 | NIRSC | NIFC TAC-3 | DIV D | 168.6000 N |  | 168.6000 N |  | A |  |
| 3 | NIRSC | R5 TAC-4 | DIV C / S | 173.9125 N |  | 173.9125 N |  | A |  |
| 4 | NIRSC | R5 TAC-5 | DIV V/Y | 173.9625 N |  | 173.9625 N |  | A |  |
| 5 | NIRSC | R5 TAC-6 | DIV E | 173.9875 N |  | 173.9875 N |  | A |  |
| 6 | NIRSC | AIR GND | All DIVS | 166.3375 N |  | 166.3375 N |  | A | NO AIR TO GROUND FOR ALL DIVISIONS |
| 7 | NIRSC | NIFC C-1 | COMMAND | 168.7000 N |  | 170.9750 N |  | A | BRANCH II COMMAND |
| 8 | NIRSC | NIFC C-2 | COMMAND | 168.1000 N |  | 170.4500 N |  | A | BRANCH I COMMAND |
| 9 | NIRSC | WHITE 2 | STRUCTURE | 154.2650 W |  | 154.2650 W |  | A |  |
| 10 | NIRSC | WHITE 3 | STAGING | 154.2950 W |  | 154.2950 W |  | A |  |
| 11 | NIRSC | BLM T1 | All DIVS | 166.7250 N |  | 166.7250 N |  | A |  |
| 12 | NIRSC | ELDORADO S.O. | ALL DIVS | 159.6900 W |  | 161.5650 W |  | A | CONTACT FOR L.E. BRANCH TONE 3 |
| 13 | NIRSC | TMU LOCAL | LOCAL I/A | 172.3750 N |  | 171.5750 N |  | A | TONE 1 OR 6 |
| 14 | Emergency Use Only | AIR GUARD | Air Ops & Ops | 168.6250 N | None | Same | 110.9 | A | Emergency Use Only |
| 15 |  |  |  |  |  |  |  |  |  |
| 16 | Emergency Use Only | AIR GUARD | Air Ops & Ops | 168.6250 N | None | Same | 110.9 | A | Emergency Use Only |
| 5. Prepared by (Communications Unit) Kody Kerwin CAIIMT #1 | Incident Location Lake Tahoe Basin County Eldorado State CA Latitude 37-44-7 N Longitude 121-53-30 W |

The convention calls for frequency lists to show four digits after the decimal place, followed by either an “N” or a “W”, depending on whether

the frequency is narrow or wide band.   Mode refers to either “A” or “D” indicating analog or digital (Project 25)