| FIRE BEHAVIOR FORECAST |
| --- |
| FORECAST NUMBER: 4 07-18-07 | TYPE OF FIRE: Wildland Vegetation |
| FIRE NAME: Fletcher | OPERATIONAL PERIOD: Wednesday Day Shift 06:00 –18:00 |
| DATE ISSUED: 07-17-07 | TIME ISSUED: 19:00 hrs |
| UNIT: CA-MDF | SIGNED: Craig Carter, FBAN |
| INPUTS |
| WEATHER SUMMARY: Temperatures lower 70’s with min RH’s 38 to 41%. Winds SW 10 – 20 G 27 (20’), cwr 0%, and LAL’s 1 and a Haines index of 4 (low) then to a 2 (very low). For specifics, see the attached Spot Forecast number 4. |
| OUTPUTS FIRE BEHAVIOR |
| GENERAL: Fire will continue decrease in activity. Expect increased activity in the afternoon period but the fire will be more closely aligned with existing control lines so spotting should not be as great an issue. Expect moderate to extreme fire behavior should the fire become established outside the perimeter. FIRE GROWTH LAST 24 HOURS: 5,500 acres |
| SPECIFIC: Fletcher: Continued potential fire growth to the northeast and southwest due primarily to topography and wind and very dry fuels. Projections: No additional perimeter growth is anticipated because of suppression activities. Conditions will remain favorable on all Divisions for holding operations because of alignment of wind with containment lines. Due to the very dry fuels, resistance to control will remain high. Spotting will remain an issue of concern. TERM EVENT: Not calculated. Tomorrow’s forecast indices: ERC 75 (80th percentile), SC 17, BI 81 IC 26 (Timber Mountain NFDRS RAWS). |
| AIR OPERATIONS: Not applicable. Sunrise: 05:44 Sunset: 20:32 for Alturas, CA (14 hours and 48 minutes from the horizon) |
| SAFETY Do not become complacent. Winds and spotting continue to be significant safety hazards on this fire. Fuels remain critically dry. The hazard of falling snags is a significant problem for mop up operations. Do not violate LCES. |