| FIRE BEHAVIOR FORECAST |
| --- |
| FORECAST NUMBER 29 | TYPE OF FIRE SURFACE |
| FIRE NAME BTU LIGHTNING COMPLEX | OPERATIONAL PERIOD JULY 26, 2008 |
| DATE ISSUED JULY 25, 2008 | TIME ISSUED 1900 |
| UNIT BUTTE UNIT, PLUMAS NATIONAL FOREST | SIGNED Jim Turner |
| INPUTS |
| WEATHER SUMMARY SEE INCIDENT METEOROLOGIST FORECAST |
| OUTPUTS FIRE BEHAVIOR |
| GENERAL INPUTS HAZARD TREES, ROLLING MATERIAL, STUMP HOLES AND SCORCHED CANOPY ARE AN ISSUE ALL OVER THIS FIRE IN ALL DIVISIONS AND BRANCHES. PAY SPECIAL ATTENTION TO AREAS WITH POTENTIAL FOR REBURN. FINE DEAD FUEL MOISTURE = 4-9%. 1000 HR FUEL MOISTURE @ CARPENTER RIDGE= 6% PROBABILITY OF IGNITION= 30-80% MAXIMUM SPOTTING DISTANCE 0.4 MILES. CRITICAL WIND SPEED FOR CROWN TRANSITION 17 MPH AT TREE TOP LEVEL. HAINES INDEX 5 = MODERATE POTENTIAL FOR LARGE FIRE GROWTH |
| SPECIFIC CONCOW BRANCH THERE IS POTENTIAL FOR FIRE ACTIVITY IN THE MID MORNING TO LATE AFTERNOON HOURS, SMOLDERING SNAGS AND ROLL OUT PRESENT A HAZARD TO THE LINE WITH THE POSSIBILITY OF OCCASIONAL SCORCHED CROWN REBURN. INTERIOR ISLANDS WILL REMAIN ACTIVE WITH OCCASIONAL SURFACE FUELS BURNING INTO THE LADDER AND AERIAL FUELS. LIVE FUEL MOISTURES: MANZANITA = 110% @ 2970’ Elev./ 98% @ 4222’ Elev. CHINKAPIN = 77% @ 4222’ Elev. MAPLE = 175% @ 3800’ Elev. LONG BRANCH INTERIOR FIRES IN THE STRINGERS OF TREES WILL STAY ACTIVE THROUGHOUT THE DAY AND INTO EARLY EVENING. SNAGS REPRESENT THE LARGEST HAZARD OF SENDING EMBERS ALOFT WITH THE LARGE DIAMETER DEAD FUELS BEING A POSSIBLE RECEPTIVE FUEL BED FOR EMBERS. HELICOPTER BUCKET WORK AND ROTOR WASH CLOSE TO THE CONTAINMENT LINES HAS THE POTENTIAL TO CAST BURNING MATERIAL ACROSS THE LINE INTO RECEPTIVE FUELS. SPECIAL GROUPS/DIVISIONS INTERIOR ISLANDS HAVE THE POTENTIAL FOR FIRE ACTIVITY IN THE MID MORNING TO AFTERNOON HOURS. SMOLDERING SNAGS AND ROLL OUT PRESENT A HAZARD TO THE LINE WITH THE POSSIBILITY OF OCCASIONAL SCORCHED CROWN REBURN. FREY FIRE NORTH OF THE FALL RIVER SMOLDERING HEAVY FUELS WITH THE POSSIBILITY OF OCCASIONAL FLARE UPS. |
| AIR OPERATIONS BETTER VISIBILITY FROM MID-MORNING TO AFTERNOON. |
| SAFETY wEAKENED SNAGS MAY FALL ACROSS CONTAINMENT LINES. DOWNED HEAVY FUELS MAY CONTAIN HIDDEN POCKETS OF BURNING MATERIAL. SEVERE FIRE BEHAVIOR POTENTIAL FUEL MOISTURE GUIDE – PG 76 (INCIDENT RESPONSE POCKET GUIDE) HELICOPTER BUCKET WORK AND ROTOR WASH CLOSE TO THE CONTAINMENT LINES HAS THE POTENTIAL TO CAST BURNING MATERIAL ACROSS THE LINE INTO RECEPTIVE FUELS. |