| FIRE BEHAVIOR FORECAST |
| --- |
| FORECAST NUMBER: | TYPE OF FIRE: Wildland |
| FIRE NAME: Lockheed | OPERATIONAL PERIOD: 0700-0700 |
| DATE ISSUED: August 18, 2009 | TIME ISSUED: 0700 |
| UNIT: Santa Cruz (CZU) | SIGNED: Typed/printed: Don Boursier, FBTS |
| INPUTS |
| WEATHER SUMMARY: Night and morning low clouds and fog. Prevailing N/NW winds should surface by afternoon and a similar weather pattern should continue through the mid-week. Daytime: Max Temps 73-82, Min RH 40-50%, Winds N/NW 4-8 mph, Gust to 12mph along ridge tops with valley bottoms upslope/up canyon 2-6mph, Gust to 10mph. Nighttime: Min Temps 48-56, Max RH 60-75% above 1500 feet and 85-100% in canyon bottoms, Winds N 2-6 mph and light down canyon winds in canyon bottoms. |
| OUTPUTS FIRE BEHAVIOR |
| GENERAL: Today’s fire behavior will be very similar to yesterday. As a result of prevailing weather conditions, fuel moistures have increased moderately. As inversion and smoke conditions lift a warmer and drier condition will result in an overall increase in fire activity, especially in the 1 and 10 hour fuels. Fire activity will be primarily fuels/slope driven particularly in deep draws. Fuel Models 1, 2, 4, and 10 are present and mixed throughout the incident geographical area. Flame lengths from surface fuels may be up to 6 feet with rates of spread up to 12 chains per hour on slopes in full alignment. Higher live fuel moistures are contributing to reduced fire behavior. Backing fire flame lengths are generally under 2 feet. A moderate potential for spotting will exist. The POI is 30% for all areas. Spotting distances should not exceed ¼ mile. The greatest concern for spotting exists anytime torching trees are observed. Moderate night time RH recovery is expected on upper slopes and excellent on lower slopes. |
| SPECIFIC: Branch I: Little fire growth in expected. Branch II: Little fire growth in expected. Branch III: Upslope/Up canyon winds in drainages that are above Swanton Road could create wind assisted ignition in areas due to rolling debris in areas of unburned fuel. Bucket Firing Group: Conditions within this general forecast are representative of the burn project area. |
| AIR OPERATIONS: The weak inversion should dissipate by 1100 hours. Minimal wind conditions facilitate smoke over most areas throughout the day, especially in lower valleys. |
| SAFETY Low fire activity in canyon bottoms can quickly transition into rapid runs up slopes of 50% or greater. Because the fire has now been present in timber fuels for a considerable time, watch for falling snags. |