FIRE SUPPRESSION REPAIR PLAN

General:

- Repair fences damaged resulting from fire suppression activities.

- Restore berms and barriers removed for fire control access.

- Report any damages or needs to the ICP, Rehab Unit Leader.

Staging Areas/Safety Zones:

- New construction: cross drain and abandon (if applicable).

- Existing: Repair to original condition, remove debris resulting from use.

Roads:

- Grade if necessary from suppression equipment use.

- Re-establish berms.

- Clean culverts plugged with soil resulting from fire road use.

- Breach berms to facilitate drainage.

Firelines:

- Install waterbreaks on all constructed or used dozer lines using the following criteria:

- Fireline gradient(%):	0-10		11-25		26-50		>50

100’		     75’		     50’		  50’

Handlines:

- Handlines: Install waterbreaks as needed.

Waterbreaks should be installed diagonally with a minimum cut of 6” into existing grade, with a minimum berm of 6” (total height of 12”). Waterbreaks shall be installed at all watercourse crossings. Waterbreaks shall be constructed to allow for drainage at the discharge end into non-erodible material. When no material exists and the line has adequate drainage due to topography (crowned along ridge, aligned with slope), no waterbreak is necessary.

Watercourses:

- All slash, soil, and debris deposited into watercourses resulting from fire suppression activities shall be removed and stabilized.

Archaeological or Historic Sites (if discovered):

- All potential sites shall be avoided; notify Rehab Unit Leader upon discovery.

NEEDS SUMMARY

NAME:                                       POSITION:                                           .

| LOCATION | MAP DESIGNATION: | REPAIR TYPE | DESCRIPTION OF NEEDED REPAIR |
| --- | --- | --- | --- |
| BRANCH | DIVISION | OTHER | DROP POINT or STAGING AREA | WB = InstallWaterbreak/bar CD = Install Crossdrain RB = Restore Berm RD = Remove Debris Fence = Repair Fence/Gate CC = Clean Culvert WC = Watercourse Cleanout |  |