| Incident Name: SWF-120-2010 Zigzag Fire | IR Interpreter(s): Jan Johnson | Local Dispatch Phone: n/a | Interpreted Size: 73,520 ac. Growth last period: n/a |
| --- | --- | --- | --- |
| Flight Time: 0016 MT (0616 UTC) Flight Date: July 11, 2010 | Interpreter(s) location: Salt Lake City, UT (RSAC) Interpreter(s) Phone: 801-824-5440 | Regional Coordinator: n/a Regional Coord. Phone: n/a | National Coordinator: Tom Mellin National Coord. Phone: 505-842-3845 |
| Ordered By: Alberta SRD thru CIFFC | Order Number: CIFFC-R0(060) | Aircraft/Scanner System: N149Z, Phoenix | Pilots/Techs: Johnson, Stefanski/Forsyth |
| IRIN Comments on imagery: Scanner noise (streaks) on Run #1, northern section of perimeter | Weather at time of flight: mostly clear, w/ some high clouds | Flight Objective: Map isolated heat sources inside and adjacent to perimeter |
| Date and Time Imagery Received by Interpreter: July 11, 2010 @ 0430 MT | Type of media for final product: shapefiles, PDF, .doc Electronic file sent to: ftp.nifc.gov/Incident_Specific_Data/NICC/2010_Alberta_Assist/20100711 |
| Date and Time Imagery Delivered to Incident: July 11, 2010 @ 0700 MT |  |
| Comments /notes on tonight’s mission and this interpretation: Tonight's mission was flown at the request of Alberta SRD, Fire Protection through CIFFC. Purpose of the mission was to map the fire perimeter and detect and map isolated heat sources within 100 feet of the perimeter, both interior and exterior. The northern section of the incident, Run #1, had streaks in the imagery, possibly high clouds or scanner noise. Runs #2 and #3 were clear. Based on the grayscale and color imagery, there were no detectable heat sources in or near the perimeter of the fire. Or, the heat sources were below the detection threshold of the Phoenix system. Further review of the color imagery on July 12 from Run #3 indicated a possible heat source in the southwest corner of the perimeter, approximately 464 meters inside the July 9 perimeter |