AIR OPERATIONS SUMMARY	PREPARED BY: Brad Joos 					PREPARED DATE/TIME: 07/19/07 / 20:00

| 1. INCIDENT NAME: ZACA | 2. OPERATIONAL PERIOD DATE: 7/20/07 START TIME: 07:00 END TIME: 20:00 SUNRISE: 05:56 SUNSET: 20;10 |
| --- | --- |

| 3. REMARKS (Safety Notes, Hazards, Air Operations Special Equipment, etc.): Zaca Lake will only be used for a dip site when Zaca Lake Resort is threatened. Hazards: Wires at the North end of Zaca Lake. Local air traffic and Gliders at Santa Ynez Airport, monitor Unicom 122.8 for reported traffic in area. Figueroa Helibase: Lat: 34*43.663’ Long: 120*06.789’ Nav27 Live Oak HB: Lat:34* 33.638’ Long: 119* 52.871’ IA H-530 1st H-527 2nd 309 if in Santa Barbara Co. | 4. MEDEVAC A/C: SBC 308 24/7 with hoist Contact by Command Freq or Night805-692-5723 | 5. TFR#7/9196: Radius: _12.0_ NM Altitude: ______12,000____= MSL Centerpoint: Lat: 34* 49.0’ Long: 119* 54.0’ |
| --- | --- | --- |

| 6. PERSONNEL | Phone | 7. FREQUENCIES | AM | FM |  | 8. FIXED-WING | # Avail / Type/ Make-Model / FAA N# / Base(s) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| AOBD: Brad Joos | 805-886-6970 | AIR/AIR FW: | 131.575 (Briefing) | 151.2725 |  | Airtankers | 3 Airtankers on order |
| ATGS: Mark Nunez | 805-895-6620 | AIR/AIR RW: | 135.575 |  |  |  |  |
| HLCO: Rob Sonteng (available p.m.) |  | AIR/GROUND: | 171.1375 A/G #2 | 172.8125 A/G #1 |  | Leadplanes Base FAX #: | Bravo 57 A-30 Lead 02 A-31 |
| ASGS: Al Driesbach & G. Monday | 916-204-4251 805-479-1837 | COMMAND: | See communication Plan |  |  |  |
| HEBM:Faulkner (Live Oak) | 530-356-1194 | CALCORD: (MEDICALS) | Rx:156.0750 W Tx:156.0750 W |  |  |  |
| HEBM: Kevin Murray / Kurt Warner (T)( Santa Ynez Helibase) | 805-878-1484 805-680-4001 | COMMAND RPT |  |  | ATGS Aircraft | Air-Attack 07 A-29 Air-Attack 340 A-28 |
| ATB MGR:Sheryl Woods @ Santa Maria Air Base | 805-937-5059 | DECK FREQ: | 168.350 (FIG) | 163.100 (SaYn) |  |  |  |
| HEBM: Dave Sewell Figueroa Helibase | 916-205-5916 | TOLC FREQ: |  |  |  | Other | Crash Rescue Units, Tower, PRB, Refer Units, HB Trailers, Figueroa PRB (A-1), |

9. HELICOPTERS (Use Additional Sheets As Necessary)

| FAA N# | TY | MAKE/MODEL | BASE | AVAIL | START | REMARKS | FAA N# | TY | MAKE/MOD | BASE | AVAIL | START | REMARKS |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 811KA (527) | 2 | Bell 212-tank | SaYn | 0700 | 0730 | A-23 | 612RM (762) | 1 | S-61 | FIG | 0700 0700 | 0730 | A-14 |
| 9121Z | 2 | Bell 212-tank | SaYn | 0700 | 0730 | A-20 | 831 | 1 | UH-60 | SaYn | 0700 | 0730 | A-16 |
| 213SJ | 2 | Bell 212bucket | FIG | 0700 | 0730 | A-24 | 4037S (780) | 1 | Skycrane | FIG | 0700 | 0730 | A-32 |
| SBC-308 | 2 | Bell 205bucket | SaYn | 0700 | 0730 | A-21 | 216PJ | 1 | Bell 214 | FIG | 0700 | 0730 | A-12 |
| 911FS H-535 | 3 | Bell 407 | SaYn | 0700 | 0730 | A-56 | 22EA | 3 | Bell 206B3 | SaYn | 0700 | 0730 | A-57 IR Ship |
| 383SH | 3 | Bell L3 | LiveOa | 0700 | 0730 | A-43 | 45917 | 1 | S-61 | FIG | 0700 | 0730 | A-13 |
| 198HM | 2 | Bell UH-1B | SaYn | 0700 | 0730 | A-18 Restricted | 184CH | 1 | Vertol | FIG | 0700 | 0730 | A-11 |
| 212AH | 2 | Bell 212 | Sa Yn | 0700 | 0730 | A-19 | 820 | 1 | UH-60 | SaYn | 0700 | 0730 | A-15 |
| 345LA525 | 3 | A-Star | LiveOak | 0700 | 0730 | A-26 | 43T | 1 | S-61 | FIG | 0700 | 0730 | A-17 |
| 911HW | 2 | Bell 212 tank | SaYn s | 0700 | 0730 | A-34 | 65PJ | 3 | Bell L3 | SaYn | 0700 | 0730 | A-25 |

ICS-220

2/99

| 10. TASK/MISSION/ASSIGNMENT (Type/Function includes: Air Tactical, Retardant, Recon, Personnel Transport, Water Dropping, S&R, etc.) |
| --- |
| TYPE/FUNCTION | NAME OF PERSONNEL OR CARGO (if applic) OR INSTRUCTIONS FOR TACTICAL AIRCRAFT | MISSION START | FLY FROM | FLY TO |
| Retardant Drops w/ Air Tankers and Helicopters Priority 2 | Portable retardant dip site located at Figueroa Helibase. Water sources: Zaca Lake , Cachuma Lake Vineyard Pond Dip Site (Type II) located at Lat: 34’45.875 Long: 120’07.133 Mesa Dip Site (Type I) located at Lat: 34’44.218 Long: 120’07.152 Sisquoc Pond Dip Site (Type I) located at Lat: 34’50.455 Long: 120’10.726D Sisquoc Dip Tank (Type II) located at Lat: 34’50.539 Long: 120’01.498 | Per ATGS Request (0800) | Div “H” to So. Fork |  |
| Recons | Helicopter (H-383SH) operating out of ICP for OSC recon missions. H-525 is backup ship. Contact Air Operations or Operations for recon approval. H-383SH to RON at Live Oak HB. | 0800 |  |  |
| Logistic Support Priority 3 | Food and supplies to potential spike camp in Div. “H” Service repeaters | 0800 |  |  |
| Shuttles Priority 1 | 2 crews into Division “H” Reposition AG Crew 3 further east. | 0800 | Santa Ynez |  |
| Helispot Const. | Finish H-18 Lat 34* 46.09’ Long 119* 49.82’ | 0800 |  |  |
|  | Helispot 1 Lat 34’47.835 Long 120’05.679 Helispot 2 Lat 34’48.518 Long 120’04.825 |  |  |  |
|  | Helispot 3 Lat 34’49.405 Long 120’06.234 Elevation: 2500 ft Helispot 4 Lat 34’50.89 Long 120’03.11 Elevation: 1500 ft |  |  |  |
|  | Helispot 5 Lat 34’50.426 Long 120’01.286 Elevation: 1500 ft Helispot 6 Lat 34’49.643 Long 119’59.383 Elevation: 1500 ft |  |  |  |
|  | Helispot 7 Lat 34’49.53 Long 120’05.733 Elevation: 2500 ft Helispot 8 Lat 34’50.09 Long 119’55.06 Elevation: 1500 ft |  |  |  |
|  | Helispot 10 Lat 34’48.31 Long 119’56.803 Hlelispot 11 Lat 34’48.31 Long 119’55.44 Helispot10 Lat 34’48.430 Long 119’56.809 |  |  |  |
|  | Helispot 12 Lat 34’47.864 Long 119’59.843 Helispot 13 Lat 34’48.198 Long 119’58.243 |  |  |  |
|  | Helispot 14 Lat 34 47.457’ Long 119 52.518’ Elevation 3800’ HOGE Helispot 15 Lat 34 43.484 Long 119 54.783’ Elevation: 3300’ HIGE Cachuma Saddle |  |  |  |
|  | Helispot 16 Lat 34* 46.570’ Long 119* 52.220’ Helispot 17 Lat 34* 46.250’ Long 119* 50.830’ |  |  |  |
|  | TFR in place over ICP & Live Oak Helibase: Radius: 2.0 NM, 2000 MSL, Centerpoint: 34’33.441 Long:119’52.969 |  |  |  |

ICS-220

2/99