| FIRE BEHAVIOR FORECAST |
| --- |
| FORECAST NUMBER: 20 | TYPE OF FIRE: SURFACE |
| FIRE NAME: ZACA 2 | OPERATIONAL PERIOD: 7/23/2007 |
| DATE ISSUED: 7/22/07 | TIME ISSUED: 1930 |
| UNIT: SANTA BARBARA COUNTY /LOS PADRES NF | SIGNED: Corky Conover, FBAN |
| INPUTS |
| WEATHER SUMMARY: Some clouds will creep into the area from the east, giving us a gradual cooling trend the next couple of days, with another warming and drying trend the second half of the week. SEE ATTACHED INCIDENT METEOROLOGIST WEATHER FORECAST. PROBABILITY OF IGNITION = 90% (calculated) Down 10 from July 22 Live Fuel Moistures are 57% at Upper Oso (Los Prietos). |
| FIRE BEHAVIOR |
| GENERAL: Expect interior islands to continue to burn out during the peak burning period, with no real threats to the line. The heavy north aspect fuels continue to hold heat and the fire will continue to eat is way up slope on the south and east areas of the fire and make short runs upslope in afternoon. The Marre fire continues to act as a partial barrier to fire spread even during times of active burning. This fire scar extends as far east as Santa Cruz Peak on the south east portion of the fire. |
| SPECIFIC BRANCH I: No significant fire activity is anticipated. BRANCH II: No significant fire activity is anticipated. BRANCH III & BRANCH V: Divisions U/V - The fire will continue to challenge the dozer line with short runs in the afternoon between McKinley Mountain and San Rafael Peak and possibly out as far as San Rafael Ridge to Mission Pine Springs. Conifers and heavier loading of dead fuels influence the fire area with the elevation gain, this creates high intensity fire when it burns, but does not support rapid spread. The critical time period for enhanced burning in these divisions is between 1400 to 2000 hrs. Fuels on the back side of the ridge are not as continuous, and crews should be able to pick up any fire that slops over the ridge. BRANCH IV: Division H – Little residual heat remains on the division today and the area is looking good from the work of the crews the last couple of days. Divisions I – With the spot fire late yesterday afternoon near H-18, it will be critical to secure any critical sections of line as the afternoon winds from the west would align with White Ledge Canyon and could push the fire down toward the Sisquoc river drainage. As the division progresses south from White Ledge, crews will encounter more heat and a greater potential for lateral spread particularly in the upper ¼ of the division. |
| AIR OPERATIONS: The marine influence in the Santa Ynez Valley should be clearing over the helibase/airport by 0830 hours. |
| SAFETY Higher fuel loads at the higher elevations release more energy from the fire, but rates of spread are expected to be moderate until the fire comes into alignment with a slope All fuelbeds can be expected to carry fire. Don’t plan on drainages/riparian vegetation to check any fire spread Spotting “potential” today remains high with the increasing temps and decreasing humidity. |