AIR OPERATIONS SUMMARY	PREPARED BY: Brad Joos 					PREPARED DATE/TIME: 07/22/07 / 20:00

| 1. INCIDENT NAME: ZACA | 2. OPERATIONAL PERIOD DATE: 7/23/07 START TIME: 07:00 END TIME: 20:00 SUNRISE: 06:00 SUNSET: 20:11 |
| --- | --- |

| 3. REMARKS (Safety Notes, Hazards, Air Operations Special Equipment, etc.): Zaca Lake will only be used for a dip site when Zaca Lake Resort is threatened. Hazards: Wires at the North end of Zaca Lake. Local air traffic and Gliders at Santa Ynez Airport, monitor Unicom 122.8 for reported traffic in area. Figueroa Helibase: Lat: 34*43.663’ Long: 120*06.789’ Nav27 Live Oak HB: Lat:34* 33.638’ Long: 119* 52.871’ IA H-309 if in Santa Barbara Co. Review Zaca Tomahawk Missile Plan | 4. MEDEVAC A/C: SBC 308 24/7 with hoist Contact by Command Freq or Night805-692-5723 | 5. Fire TFR: Radius: 12.0NM Altitude:12,000’ MSL CP: Lat: 34* 49.0’ Long: 119* 54.0’ Live Oak TFR: Radius: 2.0 NM Altitude: 2000’ MSL CP: Lat: 34* 33.441’ Long:119* 52.969’ |
| --- | --- | --- |

| 6. PERSONNEL | Phone | 7. FREQUENCIES | AM | FM |  | 8. FIXED-WING | # Avail / Type/ Make-Model / FAA N# / Base(s) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| AOBD: Brad Joos / Pete Kubiak (Dpt) | 805-886-6970 404-661-4819 | AIR/AIR FW: | 131.575 (Briefing) | 151.2725 |  | Airtankers | 3 Airtankers on order |
| ATGS: Mark Nunez | 805-895-6620 | AIR/AIR RW: | 135.575 |  |  |  |  |
| HLCO: Rob Sonteng/Rick Vallejo |  | AIR/GROUND: | 171.1375 Div.”U & V” | 172.8125 Div. “H & I” |  | Leadplanes Base FAX #: | Bravo 02 A-77 |
| ASGS: Al Driesbach & G. Monday | 916-204-4251 805-479-1837 | COMMAND: | See communication Plan |  |  |  |
| HEBM:Faulkner (Live Oak) | 530-356-1194 | CALCORD: (MEDICALS) | Rx:156.0750 W Tx:156.0750 W |  |  |  |
| HEBM: Kevin Murray / Kurt Warner (T)( Santa Ynez Helibase) | 805-878-1484 805-680-4001 | COMMAND RPT |  |  | ATGS Aircraft | Air-Attack 07 A-29 Air-Attack 340 A-28 |
| ATB MGR:Sheryl Woods @ Santa Maria Air Base | 805-937-5059 | DECK FREQ: | 168.350 (FIG) | 163.100 (SaYn) |  |  |  |
| HEBM: Dave Sewell Figueroa Helibase | 916-205-5916 | TOLC FREQ: |  |  |  | Other | Crash Rescue Units, Tower, PRB, Refer Units, HB Trailers, Figueroa PRB (A-1), WTs |

9. HELICOPTERS (Use Additional Sheets As Necessary)

| FAA N# | TY | MAKE/MODEL | BASE | AVAIL | START | REMARKS | FAA N# | TY | MAKE/MOD | BASE | AVAIL | START | REMARKS |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 811KA (527) | 2 | Bell 212-tank | SaYn | 0600 | 0630 | A-23 excl | 612RM (762) | 1 | S-61 | FIG | 0700 0700 | 0730 | A-14 excl |
| 9121Z (531) | 2 | Bell 212-tank | SaYn | 0700 | 0730 | A-20 excl | 831 | 1 | UH-60 | SaYn | 0700 | 0730 | A-16 CA NG |
| 213SJ (530) | 2 | Bell 212bucket | FIG | 0600 | 0630 | A-24 excl (Early) | 4037S (780) | 1 | Skycrane | FIG | 0700 | 0730 | A-32 cwn (Repairs) |
| SBC-308 | 2 | Bell 205bucket | SaYn | 0700 | 0730 | A-21 County | 216PJ | 1 | Bell 214 | FIG | 0700 | 0730 | A-12 excl |
| 911FS (H-535) | 3 | Bell 407 | SaYn | 0700 | 0730 | A-56 excl | 22EA | 3 | Bell 206B3 | SaYn | 0700 | 0730 | A-57 cwn IR Ship |
| 383SH | 3 | Bell L3 | LiveOa | 0600 | 0630 | A-43 cwn (Early) | 45917 | 1 | S-61 | FIG | 0700 | 0730 | A-13 cwn |
| 198HM | 2 | Bell UH-1B | SaYn | 0700 | 0730 | A-18 cwn Restricted | 184CH | 1 | Vertol | FIG | 0600 | 0630 | A-11 excl (EARLY) |
| 212AH | 2 | Bell 212 | Sa Yn | 0700 | 0730 | A-19 cwn | 820 | 1 | UH-60 | SaYn | 0700 | 0730 | A-15 CA NG |
| 345LA (525) | 3 | A-Star | LiveOak | 0700 | 0730 | A-26 excl | 43T | 1 | S-61 | FIG | 0700 | 0730 | A-17 excl |
| 911HW (528) | 2 | Bell 212 tank | SaYn s | 0700 | 0730 | A-34 excl (Repairs) | 65PJ | 3 | Bell L3 | SaYn | 0700 | 0730 | A-25 cwn |

ICS-220

2/99

| 10. TASK/MISSION/ASSIGNMENT (Type/Function includes: Air Tactical, Retardant, Recon, Personnel Transport, Water Dropping, S&R, etc.) |
| --- |
| TYPE/FUNCTION | NAME OF PERSONNEL OR CARGO (if applic) OR INSTRUCTIONS FOR TACTICAL AIRCRAFT | MISSION START | FLY FROM | FLY TO |
| Retardant Drops w/ Air Tankers and Helicopters | Portable retardant dip site located at Figueroa Helibase. Water sources: Zaca Lake , Cachuma Lake Vineyard Pond Dip Site (Type II) located at Lat: 34’45.875 Long: 120’07.133 Mesa Dip Site (Type I) located at Lat: 34’44.218 Long: 120’07.152 Sisquoc Pond Dip Site (Type I) located at Lat: 34’50.455 Long: 120’10.726D South Fork Dip Site located at Lat:34* 45.92 Long: 119* 46.84 | Per ATGS Request | Div “I”, “V” and “U” |  |
| Recons | Helicopter (H-383SH) operating out of ICP for OSC recon missions. H-525 is backup ship. Contact Air Operations or Operations for recon approval. H-383SH to RON at Live Oak HB. |  |  |  |
| Logistic Support | IR Flights for Situation Unit, Be prepared for late minute supply orders of food and water. FOBS to line and return. |  |  |  |
| Shuttles | Into Div “I” and “U” with crew extractions in evening |  | Santa Ynez |  |
| Helispot Const. and Garbage haul back | Locate and construct helispots in Div “I” and “U”. Check helispots (ie H-8) in cold sections for haul back (Potential work for Type IIIs) |  |  |  |
|  | Helispot 20 Lat 34* 43.769’ Long 119*49.034’ |  |  |  |
|  | Helispot 3 Lat 34* 49.405’ Long 120* 06.234’ Elevation: 2500 ft Helispot 4 Lat 34* 50.89’ Long 120* 03.11’ Elevation: 1500 ft |  |  |  |
|  | Helispot 5 Lat 34* 50.426’ Long 120* 01.286’ Elevation: 1500 ft Helispot 6 Lat 34* 49.643’ Long 119* 59.383’ Elevation: 1500 ft |  |  |  |
|  | Helispot 7 Lat 34*49.53’ Long 120* 05.733’ Elevation: 2500 ft Helispot 8 Lat 34* 50.09’ Long 119* 55.06’ Elevation: 1500 ft |  |  |  |
|  | Helispot 10 Lat 34* 48.31’ Long 119* 56.803’ Hlelispot 11 Lat 34* 48.31’ Long 119* 55.44’ Helispot10 Lat 34* 48.430’ Long 119* 56.809’ |  |  |  |
|  | Helispot 12 Lat 34* 47.864’ Long 119* 59.843’ Helispot 13 Lat 34* 48.198’ Long 119* 58.243’ |  |  |  |
|  | Helispot 14 Lat 34* 47.457’ Long 119* 52.518’ Elevation 3800’ HOGE Helispot 15 Lat 34* 43.484’ Long 119* 54.783’ Elevation: 3300’ HIGE Cachuma Saddle |  |  |  |
|  | Helispot 16 Lat 34* 46.570’ Long 119* 52.220’ Helispot 17 Lat 34* 46.250’ Long 119* 50.830’ |  |  |  |
|  | Helispot 18 Lat 34* 45.288’ Long 119* 48.820’ Elevation 4000’ Helispot 19 Lat 34* 44.560’ Long 119* 48.883’ Elevation 4,000’ HOGE Type II and Blackhawks |  |  |  |

ICS-220

2/99