# The Five-D System for Effective Fireline Waterbars

Michael J. Furniss

USDA Forest Service

Pacific Northwest Research Station

Corvallis, Oregon

To make effective waterbars on firelines, just remember the 5-D System. The five D’s are:
Distance, Diagonal, Divert, Discharge, and Dissipate.

Most forest values depend on healthy soils; clean water, streams full of fish, diverse wildlife habitats, productive timberlands, beautiful places, and so on. Firefighters strive to protect our soils by suppressing the wildfires that can damage them.

Methods used to fight fires, especially firelines, can cause erosion and soil degradation, and need to be treated to properly maintain forest values. Fireline surfaces usually cause runoff during heavy rainfall and snowmelt. Without waterbars, excessive runoff will concentrate and cause rills and gullies to form. Effective waterbars can prevent this from happening.

Distance: To be effective, waterbars must break up drainage areas and runoff on the fireline so that there’s not enough erosive energy available in runoff to erode the soil. To ensure that excess runoff cannot accumulate, waterbars must be placed the proper distance apart, based on the slope of the fireline. This breaks up the area that accumulates runoff, keeping it small enough to prevent damage. Erosion potential depends on slope and a table is provided on the next page that gives the maximum distance between waterbars, or between a waterbar and the next upslope drainage break.

Diagonal: After deciding where you will put each waterbar, the next decision is how to build them. An important principle in working with flowing water is: don't bully the flow, lead it. Waterbars built directly across a fireline oppose the water's energy and tend to fail. Waterbars built diagonal to the fireline lead the water off and work much better. A diagonal waterbar has a gentle slope along its base that leads the water off. A simple rule is to add 5 to the slope of the road, in percent, and build the waterbar at that many degrees from perpendicular. Or simpler yet, just build them at 30 degrees off perpendicular (see the illustration on the next page).

Divert: A good waterbar will divert the water off the fireline. To do this the waterbar must be sufficiently deep to handle all the flow for as long as it's needed. Excavation is much more effective than fill in making a durable and effective waterbar (a ditch or a dip beats a dike).

Discharge: Another feature of a good waterbar is that it will discharge the flow. A good waterbar is not a dam – it must have an open outlet.

Dissipate: Finally, a good waterbar should dissipate the flow just below the outlet to exhaust its eroding power and cause it to filter into the soil. This may require placing slash, rock, or debris below the outlet, or fudging a bit on distance to take advantage of natural features that will dissipate the water's erosive energy.

So remember, when locating and building waterbars, place them the right distance apart, at a diagonal to the fireline, so that they divert, then discharge, then dissipate the energy of the flowing water. Be sure to make them deep enough so they'll be durable.

Fireline slope	Maximum Distance Apart

%	(feet)

1-6	300

7-9	200

10-14	150

15-20	90

21-40	50

41-60	25

# Text boxes

Recommended spacing for waterbars on firelines. Waterbars should be no further apart than this, but they may be closer. When in doubt, put in more. From: UDSA-Forest Service, “Sale Administrator's Handbook”

Illustration by

Kathryn Ronnenberg