| FIRE BEHAVIOR FORECAST |
| --- |
| FORECAST NUMBER: 25 | TYPE OF FIRE: SURFACE |
| FIRE NAME: ZACA | OPERATIONAL PERIOD: 7/23/2007 |
| DATE ISSUED: 7/28/07 | TIME ISSUED: 2200 |
| UNIT: SANTA BARBARA COUNTY /LOS PADRES NF | SIGNED: David Kerr |
| INPUTS |
| WEATHER SUMMARY: Another day of drier and warmer conditions as high pressure continues to build over the area. Single digit humidity today with poor recovery at night. NW/N winds will persist over the area. SEE ATTACHED INCIDENT METEOROLOGIST WEATHER FORECAST. PROBABILITY OF IGNITION = 100% (calculated) Live Fuel Moistures are 51% at Upper Oso (Los Prietos). Sample date July 15, 2007 |
| FIRE BEHAVIOR |
| GENERAL: Yesterdays run has repositioned the fire into a SW facing drainage and has set the stage for the fire to react to upslope runs out of the drainage bottom. These upslope runs are possible towards the San Rafael Ridge near Mission Pine Camp and McKinley Mountain. North to northwest flow over the fire area will continue to push the fire into continuous older fuels than we have been dealing with in the recent shifts. Expect significant fire spread today, both wind driven to the south and east, and upslope runs as the fire repositions in new drainages |
| SPECIFIC BRANCH III: Division V – The slop-over from yesterday has the potential to become more active today. The fire is aligned with the general ridgetop winds and will react to the continuing low RHs. The fire is out of alignment with the slope providing some mitigation of the spread potential BRANCH IV: Divisions I & J – The fire remains in a generally northerly aspect and is oriented parallel with the general wind expected for today. Both of these factors will help to limit spread from these divisions. Expect the general fire behavior to increase as early as 1000 as the poor humidity recovery from last night allows more heat to be carried forward increasing the potential of early morning fireline activity. BRANCH V: Divisions U & T – The fire is now burning on a southwest facing slope and will be more reactivity than we have seen previous shifts. NW to N winds will try to push the fire downslope, while the topography wants to grab active portions of the fireline and spread the fire NE to San Rafael Ridge or Southwest to the series of dozer lines south of the McKinley Peak ridge. The gradient between these two forces will determine the overall direction of spread. However, active fire is to be expected regardless of the driving force. Expect active fire by 1000hrs. . |
| AIR OPERATIONS: Much the same fog situation at Santa Ynez this morning as yesterday. Expect burn-off at the airport by 0900. The ICP helibase should be clear. Smoke from today’s fire activity will impact visibility on the most southeast positions of the fire |
| SAFETY Low humidity in the fire area are near Red Flag conditions. The fire will develop rapidly as the sun begins to warm the exposed fuels Expected enhanced spotting potential today as the drying trend continues to effect the flammability of the smaller size class fuels Fire has moved into a SW facing drainage. This is different than we have seen in many shifts. Expect rapid develop of any fire on these brush dominated slopes |