| FIRE BEHAVIOR FORECAST |
| --- |
| FORECAST NUMBER: 24 | TYPE OF FIRE: SURFACE |
| FIRE NAME: ZACA 2 | OPERATIONAL PERIOD: 7/27/2007 |
| DATE ISSUED: 7/26/07 | TIME ISSUED: 2000 |
| UNIT: SANTA BARBARA COUNTY /LOS PADRES NF | SIGNED: Corky Conover, FBAN |
| INPUTS |
| WEATHER SUMMARY: The monsoonal moisture will continue to move eastward the next few days. High pressure is rebuilding over the Incident and the air mass is more stable. A warming and drying trend will continue over the fire area through the weekend. SEE ATTACHED SPOT WEATHER FORECAST. PROBABILITY OF IGNITION = 50% (6500 feet in elevation) 70% (4500 feet in elevation) Live Fuel Moistures are 57% at Upper Oso (Los Prietos). |
| FIRE BEHAVIOR |
| GENERAL: With the warming and drying trend we should expect the fire activity to pick up a little earlier each day. The heavy north aspect fuels continue to hold heat and the fire will continue to eat is way up slope on the south-east area of the fire and short runs upslope in afternoon are still possible. The Marre fire continues to act as a partial barrier to fire spread even during times of active burning. This fire scar extends as far east as Santa Cruz Peak on the south east portion of the fire. |
| SPECIFIC All DIVISIONS EXCEPT U: No significant fire activity is anticipated. Division U - The fire will continue to work its way laterally and slowly up toward the ridge between McKinley Mountain and San Rafael Peak. Conifers and heavier loading of dead fuels influence the fire area with the elevation gain, this creates high intensity fire when it burns, but does not support rapid spread. The critical time period for enhanced burning in these divisions is between 1200 to 2000 hrs. Fuels on the back side of the ridge are not as continuous, and crews should be able to pick up any fire that slops or spots over the ridge. Any burn out operations should proceed cautiously when the RH drops below 25%, and should be reconsidered if the RH drops to ≤ 20%. Divisions I – The entire division is looking good with all the good work from the crews that last few days. As the division progresses south into Division U, crews will encounter more heat and a greater potential for spread. See Division U. |
| AIR OPERATIONS: The marine influence in the Santa Ynez Valley, and the airport/helibase should be clear for air operations by 0930 hours. |
| SAFETY Higher fuel loads at the higher elevations release more energy from the fire, but rates of spread are expected to be moderate until the fire comes into alignment with the slope. All fuel beds can be expected to carry fire. Don’t plan on drainages/riparian vegetation to check any fire spread. |