Appendix B

Design Flow Runoff Response

Basin-Indian Complex Fire on Los Padres National Forest

August, 2008

Joshua Courter and K. Andy Stone

.

Wildfires result in increased runoff with soil burn severity. Burn Area Emergency Response (BAER) teams use soil burn severity to estimate runoff resulting from fires. The increases are calculated as adjusted design flow. Adjusted design flow is the flow increase expected to occur as a result of decreased infiltration and interception following a wildfire. The values also provide an estimate of flooding potential to near-by communities.

Design Flow Runoff Response

Before an adjusted design flow can be determined, pre-fire design flow must be calculated.  This is the flow expected to occur prior to the fire.  This is the flow responsible for forming present day channel conditions and flows used to estimate proper performance of culverts and other drainage structures.  Design flow estimates have been based on existing gage station information and streams surveyed within or adjacent to the immediate fire area.  These estimates assume pre-fire ground infiltration and ground cover conditions.

Adjusted design flow is calculated using the same relationships as design flow however runoff response is estimated by assuming an increased runoff commensurate with soil burn severity in terms of recurrence interval.  This recurrence interval estimates the response of the newly burnt landscape to an average annual storm.  Pre-fire, an average rainfall event is associated with the bankfull discharge, which has a recurrence interval of 1.2-1.3 years.  The Basin-Indian Complex Fire is expected to respond to an average rainfall event differently for the low, moderate, and high severity soil burned areas.  It is expected the landscape would respond as if the discharge were associated with a 5, 10, and 25-year event on the coastal side while the inland side of the fire would be a 2, 5, and 10-year event.  The unburned lands within the fire would respond as the unburned lands outside the fire and would have a discharge associated with the average bankfull storm.   Increases in discharge associated with predicted recurrence intervals are prorated across watersheds by soil burn severity to yield post-fire discharge or the adjusted design flow.  The fire has been analyzed at a watershed level of the 6th field watershed (HUC 6).  The watersheds are 180600060202 Big Creek Frontal,

180600060104 Big Sur River, 180600120101 Cachagua Creek, 180600120102 Danish Creek-Carmel River, 180600051104	Horse Creek-Arroyo Seco, 180600060102 Las Piedras Canyon Frontal, 180600060103 Little Sur River, 180600051101 Lost Valley Creek-Arroyo Seco, 180600060201 Partington Creek Frontal, 180600051103 Piney Creek, 180600051106	 Reliz Creek-Arroyo Seco, 180600050602 San Antonio River/Mission Creek, 180600120103	San Clemente Creek-Carmel River, 180600051102 Tassajara Creek-Arroyo Seco, 180600050601 Upper San Antonio River, and 180600051105 Vaqueros Creek-Arroyo Seco. Table 1 displays the amount of burned lands by severity for the affected watersheds.

Table 1 – Approximate Acres in Watersheds Affected by the Basin-Indian Complex Fire

| Watershed Names | Soil burn severity (acres) | Total Watershed (acres) |
| --- | --- | --- |
|  | High | Moderate | Low | Unburned |  |
| Big Creek Frontal |  |  |  |  |  |
| Big Sur River | 6553 | 15847 | 6497 | 8507 | 37406 |
| Cachagua Creek | 678 | 1052 | 814 | 27395 | 29940 |
| Danish Creek-Carmel River | 3090 | 10642 | 5077 | 10417 | 29227 |
| Horse Creek-Arroyo Seco | 2301 | 4217 | 2719 | 21346 | 35227 |
| Las Piedras Canyon Frontal | 53 | 346 | 65 | 23080 | 23544 |
| Little Sur River | 3950 | 8715 | 4760 | 8225 | 24650 |
| Lost Valley Creek-Arroyo Seco | 10588 | 10345 | 2847 | 6350 | 30130 |
| Partington Creek Frontal | 1539 | 6021 | 5337 | 8393 | 21290 |
| Piney Creek | 3577 | 2914 | 931 | 29675 | 37098 |
| Reliz Creek-Arroyo Seco | 889 | 1052 | 815 | 35287 | 37221 |
| San Antonio River/Mission Creek | 7274 | 7857 | 2053 | 23353 | 40538 |
| San Clemente Creek-Carmel River | 0.11 | 5.76 | 0.56 | 21096 | 21103 |
| Tassajara Creek-Arroyo Seco | 9793 | 12216 | 3255 | 9963 | 35227 |
| Upper San Antonio River | 3586 | 4398 | 1736 | 16191 | 25911 |
| Vaqueros Creek-Arroyo Seco | 2134 | 3959 | 1528 | 13993 | 21616 |

Stream channel geometry and flow relationships were developed using local tributary streams and USGS gage stations.  Gage stations were investigated to provide information on flow conditions following the Bankfull (BKF), 2.0, 5.0, 10, 25, 50, and 100 year events.

BAER Hydrologists collected stream data in various watersheds within the fire perimeter using techniques discussed in Harrelson (1994). Staff plate readings were taken at gage sites for bankfull discharge.  Bankfull discharges were determined from station rating curves or USGS flow records.  A protocol modified by McCandless and Evertt (2002) was utilized for field surveys at gage stations.  Modification of the protocol involved surveying only riffle habitats and bed and bank material for most sites was derived from reached-averaged pebble counts and riffle pebble counts.  Stream bank material was not analyzed in this study.

Table 2 - Gage Station Data for Watersheds Affected or Adjacent to the Basin-Indian Complex Fire, 2008

| Gage Station Location | Drainage Area in m2 | Discharge in cubic feet per second |
| --- | --- | --- |
|  |  | Q BKF | Q 2.0 | Q 5.0 | Q 10 | Q 25 | Q 50 | Q 100 |
| USGS 11143000 BIG SUR RIVER NR BIG SUR CA | 46.5 | 1110 | 2340 | 4194 | 5251 | 6649 | 9594 | 10700 |
| USGS 11142800 RAT C NR LUCIA CA | 0.82 | 4.5 | 15 | 21 | 26 | 28 | N/A | N/A |
| USGS 11151870 ARROYO SECO NR GREENFIELD CA | 113 | 4325 | 6940 | 12715 | 15451 | 19085 | 21800 | N/A |
| USGS 11149650 SULPHUR SPRINGS CYN NR JOLON CA | 5.16 | 35 | 132 | 289 | 362 | 372 | N/A | N/A |

NOTE: N/A means no flow record has been recorded that exceeded highest peak flow

Several resistance equations were used in order calculate discharge on ungaged flows. These equations were Manning’s ‘n’ for relative roughness, Manning’s ‘n’ from Jarrett, Manning’s ‘n’ by Rosgen Stream Classification types, Darcy-Weisbach with Leopold, Wolman, and Miller, Darcy-Weisbach with Hey friction factor, and Chezy C. After comparing several resistance equations to the USGS gaging station 11143000, Jarrett’s equation for Manning’s ‘n’ was the most accurate. Jarrett’s Equation for Manning’s ‘n’ is listed below.

Where n=Calculated Manning’s ‘n’, S=bankfull slope, and R=hydraulic radius

Once Mannings ‘n’ value is calculated that value can be inserted into a modified Mannings equation below. The result is a calculated velocity in feet per second.

Where V=velocity, n=Manning’s ‘n’ from Jarrett’s Equation, R=hydraulic radius, and S=stream gradient

The velocity is then multiplied by the cross sectional area measured at the bankfull stage (average yearly storm event) to calculate discharge in cubic feet per second.

Q = (V)(A)

Where Q=discharge (cfs), V=velocity, and A=cross sectional area.

Using measured values from USGS gaging stations, storm return intervals were created for the 2, 5, 10, 25, 50, and 100-year storm events. Since the fire crossed two different hydrophysiographic areas, i.e. change in climate, precipitation, vegetation, bankfull return intervals, two sets of storm return intervals were created.

Coastal Storm Return Interval Equations Where: Q=discharge in cubic feet/second, WA=watershed area in square miles

Inland Storm Return Interval Equations Where: Q=discharge in cubic feet/second, WA=watershed area in square miles

These values were then multiplied by the area of the watershed by soil burn severity, which includes unburned lands. These values were then added together to provide a predicted post-fire discharge value by each 6th field watershed. Pre-fire discharge was calculated using the bankfull discharge equation. Estimates of pre-fire conditions may be determined off the Discharge Relationship by Watershed Area and Recurrence Interval graphs.

Figure 1 – Big Sur Storm Return Intervals for coastal watersheds

Figure 2 – Arroyo Seco Storm Return Intervals inland watersheds

Regression Analysis:

Discharge can be determined from a variety of different methods, including the development of regional curves or the use of regression equations that have been developed for large hydrophysiographic areas. Regional curves are preferred because they use local measured discharge data. Although regional curves developed from a few gaging stations are useful, this analysis method is more accurate when many gaging stations are used. Because there were only four gage sites (Table 2) with records of more than 10 years in the burn area, additional analysis was conducted using regression equations established by the U.S. Geological Survey (Waananen and Crippen, 1977). The rationale is that, if a good correlation could be established between the regional curves and the regression equations, the regression equations could be used to estimate discharge from ungaged streams.

The regression equations have been developed for six hydrologic regions within the state of California. The regions include: the North Coast Region, Northeast Region, Central Coast Region, Sierra Region, South Coast Region, and the South Lahontan-Colorado Desert Region. These regions generally share the same hydrophysiography (e.g., vegetation type, climate, geology, etc.), but the equations often fail to capture the variability within these large areas. Moreover, at the higher return intervals (e.g., Q50 – Q100), there are fewer data and thus the output values can be skewed. Three of these equations were used as a comparison to the regional curves (Table 3).

Table 3: regression equations for the hydrologic regions used in the Basin Complex BAER analysis (after Waananen and Crippen, 1977). Q = discharge in cubic feet per second, A = area in square miles, p = precipitation in inches, and H = average basin elevation in feet. The number next to the Q denotes the return interval.

| Region | Equations |
| --- | --- |
| South Coast |  |
| Central Coast |  |
| North Coast |  |

Area, precipitation, and average basin elevation data were derived by using an ArcGIS tool called “Streamstats” developed by the U.S. Geological Survey (http://streamstatsags.cr.usgs.gov/). This tool allows one to quickly delineate the watershed of interest and calculate all the basin characteristics necessary for input into the regression equations.

Sixty-four watersheds ranging in scale from HUC 5 to approximately HUC 8 subwatersheds were analyzed using the equations in Table 3. The results are summarized in Appendix B and include all the discharge calculations for the Q2 to Q100 return intervals. Equations from three hydrophysiographic regions (South Coast, Central Coast, and North Coast) were used to provide a broad comparison, but the central coast equations were assumed to be the most applicable.

To validate the utility of the regression equations, the discharge results were compared to those derived from the regional curves (Table 4). There was reasonably good correlation between Q values derived for the coastal watersheds (e.g., Big Sur River), but poor correlation with Q values derived for the eastern side of the burn area through the Arroyo Seco drainage. The regression equations, on average, underestimate discharge relative to the regional curves.

Table 4. Comparison of discharge values for local regional curves vs. regression equations for the central coast.

| Gage Station Location | Method | Discharge in cubic feet per second |
| --- | --- | --- |
|  |  | Q BKF | Q 2.0 | Q 5.0 | Q 10 | Q 25 | Q 50 | Q 100 |
| USGS 11143000 BIG SUR RIVER NR BIG SUR CA | Local Regional Curve | 1110 | 2340 | 4194 | 5251 | 6649 | 9594 | 10700 |
|  | Regression | N/A | 1246 | 3245 | 4833 | 6935 | 8817 | 10618 |
| USGS 11142800 RAT C NR LUCIA CA | Local Regional Curve | 4.5 | 15 | 21 | 26 | 28 | N/A | N/A |
|  | Regression | N/A | 23.8 | 67 | 108 | 169 | 222 | 284 |
| USGS 11151870 ARROYO SECO NR GREENFIELD CA | Local Regional Curve | 4325 | 6940 | 12715 | 15451 | 19085 | 21800 | N/A |
|  | Regression | N/A | 1552 | 4628 | 7398 | 11399 | 15271 | 19049 |
| USGS 11149650 SULPHUR SPRINGS CYN NR JOLON CA | Local Regional Curve | 35 | 132 | 289 | 362 | 372 | N/A | N/A |
|  | Regression | N/A | 58 | 192 | 335 | 570 | 799 | 1063 |

Note: N/A designation in Table 4 means that there is no regression equation for a bankfull return interval or no flow record has been recorded that exceeded highest peak flow.

Due to the numerous values at risk, it was determined that a conservative estimate of discharge (i.e., higher Q) was more prudent to use for planning, early warning, and treatment objectives. Therefore, it is recommended that the regional curves developed from local gage data be used instead of the regression values. This is further supported by the favorable statistical relationship (R2) derived between bankfull cross-sectional area, discharge, and basin size (Table 5).

Table 5. R2 values for regional curve parameters measured in the field.

| Related Gage Stations | Parameters | R2 |
| --- | --- | --- |
| USGS 11143000 BIG SUR RIVER NR BIG SUR CA USGS 11142800 RAT C NR LUCIA CA | Bankfull vs. Drainage Area | 0.9872 |
|  | Discharge vs. Drainage Area | 0.9026 |
| USGS 11151870 ARROYO SECO NR GREENFIELD CA USGS 11149650 SULPHUR SPRINGS CYN NR JOLON CA | Bankfull vs. Drainage Area | 0.8347 |
|  | Discharge vs. Drainage Area | 0.8962 |

Table 6 provides estimates of predicted post burn discharges for an average rainfall event (bankfull event) in both cubic feet per second and cubic feet per second per square mile for the watershed affected by the fire. Due to the vegetation recovery and response, these predicted flow rates are expected to last up to 5 years of normal average rainfall.

Table 6 - Pre and Post Fire Discharge for HUC 6 Watersheds by Soil burn severity for the Basin-Indian Complex Fire, 2008

| Watersheds Affected by the Basin-Indian Complex Fire** | Discharge by Soil Burn Severity in cfs* | Discharge by Watershed in cfs | Discharge by Watershed in cfs/Sq.mi. |
| --- | --- | --- | --- |
| Watershed | Ws Area Sq.Mi. | High Severity Burn | Moderate Severity | Low Severity | Unburned | Pre-fire | Post Fire | Pre-fire flow in cfs/sq. mi. | Post-fire flow in cfs/sq mi |
| Big Creek Frontal | 39.76 | 0.02 | 0.014 | 0.07 | 39.53 | 897 | 893 | 23 | 22 |
| Big Sur River | 58.45 | 10.24 | 24.76 | 10.15 | 13.29 | 1516 | 3921 | 26 | 67 |
| Cachagua Creek | 46.78 | 1.06 | 1.64 | 1.27 | 42.81 | 711* | 681* | 15 | 15 |
| Danish Creek-Carmel River | 45.67 | 4.83 | 16.63 | 7.93 | 16.28 | 684 | 1214 | 15 | 27 |
| Horse Creek-Arroyo Seco | 47.79 | 3.6 | 6.59 | 4.25 | 33.35 | 736 | 808 | 15 | 17 |
| Las Piedras Canyon Frontal | 36.79 | 0.08 | 0.54 | 0.1 | 36.06 | 684 | 802 | 19 | 22 |
| Little Sur River | 40.08 | 6.17 | 13.62 | 7.44 | 12.85 | 906 | 2047 | 23 | 51 |
| Lost Valley Creek-Arroyo Seco | 47.08 | 16.54 | 16.16 | 4.45 | 9.92 | 718 | 2098 | 15 | 45 |
| Partington Creek Frontal | 33.27 | 2.4 | 9.41 | 8.34 | 13.11 | 703 | 1401 | 21 | 42 |
| Piney Creek | 57.97 | 5.59 | 4.55 | 1.45 | 46.37 | 1005 | 1135 | 17 | 20 |
| Reliz Creek-Arroyo Seco | 58.16 | 1.39 | 1.4 | 0.23 | 55.14 | 1010* | 999* | 17 | 17 |
| San Antonio River/Mission Creek | 63.34 | 11.37 | 12.28 | 3.21 | 36.49 | 1159 | 1767 | 18 | 28 |
| San Clemente Creek-Carmel River | 32.97 | 0 | 0.01 | 0 | 32.96 | 404 | 404 | 12 | 12 |
| Tassajara Creek-Arroyo Seco | 55.04 | 15.3 | 19.09 | 5.09 | 15.57 | 924 | 2243 | 17 | 41 |
| Upper San Antonio River | 40.49 | 5.6 | 6.87 | 2.71 | 25.3 | 563 | 798 | 14 | 20 |
| Vaqueros Creek-Arroyo Seco | 33.78 | 3.34 | 6.19 | 2.39 | 21.86 | 420 | 555 | 12 | 16 |
| Arroyo Seco (HUC 5) | 299.81 | 45.76 | 53.98 | 17.86 | 182.21 | 4813 | 7849 | 16 | 26 |

* Post fire is less then pre fire indicates no expected increase in water in cfs due to minimal amounts of the over all watershed burning.

Subwatersheds within the HUC 6 watersheds that have values at risk are in Table 7 below. All values are estimated flows for both pre-fire and post-fire.

Table 7 - Pre and Post Fire Discharge for subwatersheds within HUC 6 Watersheds by for the Basin-Indian Complex Fire, 2008

| Subwatersheds Affected by the Basin-Indian Complex Fire | Discharge by Watershed in cfs | Discharge by Watershed in cfs/Sq.mi. |
| --- | --- | --- |
| Subwatershed Names within HUC 6 Watersheds | Ws Area Sq.Mi. | Pre-fire | Post Fire | Pre-fire flow in cfs/sq. mi. | Post-fire flow in cfs/sq mi |
| 112 inch culvert on Roosevelt Creek | 2.28 | 5 | 50 | 2 | 22 |
| 54 inch culvert on Unnamed Tributary to Arroyo Seco | 0.59 | 1 | 6 | 1 | 10 |
| Arroyo Seco River upstream of Sportsmen Club | 7.23 | 35 | 78 | 5 | 11 |
| Arroyo Seco upstream of Arroyo Seco Resort | 113.14 | 2956 | 6296 | 26 | 56 |
| Arroyo Seco upstream of Piney Creek | 123.11 | 3388 | 6529 | 28 | 53 |
| Arroyo Seco Upstream of Sycamore Flat | 207.87 | 3383 | 6284 | 16 | 30 |
| Bear Canyon - upstream of home | 11.35 | 72 | 623 | 6 | 55 |
| Big Sur River upstream of Pfeiffer-Big Sur State Park | 46 | 1094 | 3090 | 24 | 67 |
| Castro Canyon | 0.5 | 2 | 6 | 5 | 11 |
| Church Creek upstream of Caves | 2.79 | 8 | 33 | 3 | 12 |
| Coleman Canyon - upstream of home | 4.61 | 17 | 103 | 4 | 22 |
| Danish Creek-Carmel River and Cachagua Creek | 92.45 | 1395 | 1925 | 15 | 21 |
| Finch Creek downstream of confluence with Anastasia Canyon above Hastings Reserve | 6.4 | 29 | 70 | 4 | 11 |
| Graves Canyon | 1 | 6 | 12 | 6 | 12 |
| Grimes Canyon | 0.83 | 5 | 17 | 6 | 21 |
| Hot Springs Canyon | 4.2 | 42 | 126 | 10 | 30 |
| Indians Adobe | 0.36 | 0.2 | 3 | 1 | 9 |
| Juan Hiquero Creek | 1.81 | 13 | 49 | 7 | 27 |
| Lafler Canyon | 0.6 | 3 | 11 | 5 | 18 |
| Little Sur River upstream of Boy Scout Camp | 18.18 | 308 | 842 | 17 | 46 |
| Little Sur River upstream of confluence with South Fork - Bridge | 26.5 | 516 | 1332 | 19 | 50 |
| Los Padres Reservoir - everything upstream | 43.96 | 643 | 1193 | 15 | 27 |
| McWay Canyon | 2.54 | 21 | 70 | 8 | 28 |
| Miller Fork Carmel River at Tan Bark | 1.25 | 2 | 4 | 2 | 3 |
| North Fork San Antonio River - Bridge to Avila Ranch | 9.53 | 55 | 185 | 6 | 19 |
| Partington Creek | 3.73 | 36 | 122 | 10 | 33 |
| Pfeiffer-Redwood Creek | 0.93 | 5 | 22 | 6 | 24 |
| Pheneger Creek | 0.81 | 4 | 15 | 6 | 18 |
| Piney Creek above Paloma Creek | 15.88 | 124 | 419 | 8 | 26 |
| San Antonio River-Mission Creek and Upper San Antonio River | 103.83 | 1722 | 2565 | 17 | 25 |
| Santa Lucia Creek | 18.39 | 157 | 521 | 9 | 28 |
| Sierra Creek Culvert | 0.68 | 4 | 16 | 5 | 23 |
| South Fork Little Sur River upstream of confluence with Little Sur - Bridge | 11.36 | 162 | 344 | 14 | 30 |
| Tassajara Creek at Tassajara Hot Springs | 19.92 | 179 | 698 | 9 | 35 |
| Tributary to Arroyo Seco at 19S09 | 2.85 | 8 | 82 | 3 | 29 |
| Unnamed Tributary to Arroyo Seco at Santa Lucia Memorial Park | 0.61 | 1 | 3 | 1 | 4 |
| Unnamed Tributary to Church Creek - Road Crossing | 0.88 | 1 | 10 | 1 | 11 |
| Unnamed Tributary to Tassajara Creek at Tassajara Hot Springs | 1.25 | 2 | 23 | 2 | 19 |

Conclusion/Summary

The Basin-Indian Complex Fire affected several watersheds. Each watershed has been analyzed and predicts the increased water yield for that watershed. Table 8 below summarizes each watershed’s increased water yield. Table 9 summarizes subwatersheds with values at risk.

Table 8 – Increased Water Yield for the Watersheds in the Basin-Indian Complex Fire, 2008

| Increased Water Yield by HUC 6 Watershed |
| --- |
| Watershed | Water Yield (%) |
| Big Creek Frontal | 100% |
| Big Sur River | 259% |
| Cachagua Creek | 100% |
| Danish Creek-Carmel River | 178% |
| Horse Creek-Arroyo Seco | 110% |
| Las Piedras Canyon Frontal | 117% |
| Little Sur River | 226% |
| Lost Valley Creek-Arroyo Seco | 292% |
| Partington Creek Frontal | 199% |
| Piney Creek | 113% |
| Reliz Creek-Arroyo Seco | 100% |
| San Antonio River/Mission Creek | 152% |
| San Clemente Creek-Carmel River | 100% |
| Tassajara Creek-Arroyo Seco | 243% |
| Upper San Antonio River | 142% |
| Vaqueros Creek-Arroyo Seco | 132% |
| Arroyo Seco (HUC 5) | 163% |

Table 9 – Increased Water Yield for the Subwatersheds within HUC 6 Watersheds in the Basin-Indian Complex Fire, 2008

| Increased Water Yield by Subwatershed within a HUC 6 Watershed |
| --- |
| Subwatershed Name | Water Yield (%) |
| 112 inch culvert on Roosevelt Creek | 931% |
| 54 inch culvert on Unnamed Tributary to Arroyo Seco | 908% |
| Arroyo Seco River upstream of Sportsmen Club | 223% |
| Arroyo Seco upstream of Arroyo Seco Resort | 213% |
| Arroyo Seco upstream of Piney Creek | 193% |
| Arroyo Seco Upstream of Sycamore Flat | 186% |
| Bear Canyon - upstream of home | 862% |
| Big Sur River upstream of Pfeiffer-Big Sur State Park | 282% |
| Castro Canyon | 246% |
| Church Creek upstream of Caves | 443% |
| Coleman Canyon - upstream of home | 612% |
| Danish Creek-Carmel River and Cachagua Creek | 138% |
| Finch Creek downstream of confluence with Anastasia Canyon above Hastings Reserve | 244% |
| Graves Canyon | 209% |
| Grimes Canyon | 373% |
| Hot Springs Canyon | 302% |
| Indians Adobe | 1216% |
| Juan Hiquero Creek | 371% |
| Lafler Canyon | 374% |
| Little Sur River upstream of Boy Scout Camp | 273% |
| Little Sur River upstream of confluence with South Fork - Bridge | 258% |
| Los Padres Reservoir - everything upstream | 186% |
| McWay Canyon | 333% |
| Miller Fork Carmel River at Tan Bark | 185% |
| North Fork San Antonio River - Bridge to Avila Ranch | 339% |
| Partington Creek | 343% |
| Pfeiffer-Redwood Creek | 413% |
| Pheneger Creek | 330% |
| Piney Creek above Paloma Creek | 337% |
| San Antonio River-Mission Creek and Upper San Antonio River | 149% |
| Santa Lucia Creek | 331% |
| Sierra Creek Culvert | 445% |
| South Fork Little Sur River upstream of confluence with Little Sur - Bridge | 212% |
| Tassajara Creek at Tassajara Hot Springs | 390% |
| Tributary to Arroyo Seco at 19S09 | 1056% |
| Unnamed Tributary to Arroyo Seco at Santa Lucia Memorial Park | 421% |
| Unnamed Tributary to Church Creek - Road Crossing | 855% |
| Unnamed Tributary to Tassajara Creek at Tassajara Hot Springs | 1141% |

Accelerated runoff is expected to return to normal conditions within 5 years. Each passing year should result in less runoff under normal average rain conditions and normal vegetation regrowth.

References Cited

Harrelson, C C, Rawlins, C L, and Potyondy, J P. 1994. Stream channel reference sites: an illustrated guide to field technique. Gen. Tech. Rep. RM-245. Fort Collins, CO; U.S. Department of Agriculture, Forest Service, Rocky Mountain Forest and Range Experiment Station.

Jarrett, R.D., and Costa, J.E., 1988, Evaluation of the flood hydrology in the Colorado Front Range using precipitation, streamflow, and paleoflood data for the Big Thompson River Basin: U.S. Geological Survey Water-Resources Investigations Report 87–4117, 37 p.

McCandless, T L and Everett, R A. 2003.  MARYLAND STREAM SURVEY: BANKFULL DISCHARGE AND CHANNEL CHARACTERISTICS OF STREAMS IN THE PIEDMONT HYDROLOGIC REGION, Appendix B,  U.S. Fish & Wildlife Service, Chesapeake Bay Field Office, CBFO-S02-01

U.S. Geological Survey Water-Resources Investigations Report 94-4002, 1993: Nationwide summary of U.S. Geological Survey regional regression equations for estimating magnitude and frequency of floods for ungaged sites.

U.S. Geological Survey Water-Resources, Streamstats Homepage http://water.usgs.gov/osw/streamstats/index.html

Waananen, A.O., and Crippen, J.R., 1977, Magnitude and frequency of floods in California: U.S. Geological Survey Water-Resources Investigations Report 77-21, 96 p.