| Incident Name: | Piute | Analysis Tier Level: | Tier I – Primary Assets Only |
| --- | --- | --- | --- |
| State(s): | California | FSPro Projected From: RAVAR Requested: | 2 July 2008 3 July 2008 |
| Report Date: | 3 July 2008 |  | 7-day projection |
| RAVAR Analyst: | Jeff Kaiden, RMRS Missoula – 406.542.4166 jkaiden@fs.fed.us | FSPro Analyst: | Diane Travis R5 – 661.723.2754 dhtravis@fs.fed.us |
| RAVAR Code: | T1_B_080703_jk |  |  |

NOTE: This report accompanies a RAVAR analysis map.

# All RAVAR products are intended for STRATEGIC use only. It is always advised that values analyzed and displayed on RAVAR maps be verified by local knowledge.

# FSPro Basis for Analysis:

# FSPro Analysis – 7 day starting 2 July 2008; Projected spread assumes NO further suppression

# Barriers representing completed fireline are located S of the mapped perimeter – analysis assumes that these firelines will hold subject to spotting or spread around barrier ends.

# Straight line truncations of the FSPro area to the E reflects geographic limit of data used for the analysis.

# FSPro analyst stated four LANDFIRE landscapes coalesce creating the ‘fan’ shape on the E portion of the FSPro spread, numerous attempts to ‘clean’ the landscape failed.

# NOTE: The < 1% spread probability zone is displayed on the map (pale pink zone) but assets within are not summarized. This zone represents “the rare event” – confidence in this prediction is undetermined.

# Tier I Analysis – Primary Assets Only

# General Assessment:

# The fire is located on the Sequoia National Forrest 35 miles E of Bakersfield and proximate to Moreland Mill in Kern county.

# Assuming no further suppression, the 7-day fire spread projection indicates generally omni-direction spread with growth in the ‘fan’

# Communities threatened:

# numerous communities located throughout FSPro zones:

# >80%: Burton Mill, Claraville, Inmans (historical), Moreland Mill, Piute (historical), Sageland, Shady rest (historical)

# 20-40%: Little Dixie (historical), South Lake, Squirrel Mountain Valley

# 5-20%: Armistead, Bodfish, Harts Place, Havilah, Keyesville, Lake Isabella, Miracle Hot Springs, Sand Canyon, Scovern Hot Springs (historical), South Lake, Twin Oaks

# 1-5%: Fig Orchard, Loraine, Millersville, Petersburg (historical)

# Dense clusters of structures located along Caliente Creek Rd, County Highway 483 and State Highway 178 to the S, SW, W, NW, & N within all FSPro zones; and along Kelso Creek between Sageland & Weldon 4 miles NE of the mapped perimeter.

# Major Infrastructure:

# Highways, Major Roads:

# Caliente Creek Rd is located 2 miles SW of the mapped fire perimeter running throughout all FSPro zones.

# County Highway 483 is located 7 miles W of the mapped perimeter within the 1-20% FSPro zones.

# State Highway 178 is located 8 miles N of the mapped perimeter 1-20% zones.

# State Highway 14 is located 18 miles E of the mapped perimeter within the 1-40%

# Communication Towers

# 3 towers are located 8 miles NNW of the mapped perimeter within the 20-40% FSPro zone proximate to the Cook Peak Lookout.

# 1 tower is located 20 miles E of the mapped perimeter within the 5-20% zone.

# 2 towers are located 10 miles NW of mapped perimeter within the 5-20% zone.

# 4 towers are located 14 miles NW of mapped perimeter within the 1-5% zone.

# 1 tower is located 20 miles ESE of the mapped perimeter within the 1-5% zone.

# 1 tower is located 11 miles W of the mapped perimeter within the 1-5% zone.

# Oil and Gas Pipelines: 22 miles S of mapped perimeter outside all FSPro zones.

# Powerlines

# running E/W along Caliente Rd and turning N/S along County Highway 483 through all FSPro zones.

# running N/S along State Highway 14, 17 miles E of the mapped perimeter through the 1-40% FSPro zones.

- Water Resources:

  - Power Pumping Substation located 10 miles NW of mapped perimeter within 5-20%.

  - Lake Isabelle Dam is located 8 miles NW of mapped perimeter within the 5-20% zone

  - Rio Bravo Diversion Dam is located 13 miles W of mapped perimeter outside all FSPro zones

  - Water Pipelines, Aqueducts, Canals run N/S, 15 miles E of mapped perimeter through the 1-40% FSPro zones

# Other resources threatened:

# Kelso Valley Airport located 7 miles  SE of the mapped perimeter within the 40-60% zone

# Flying S Ranch Airport located 5 miles WSW of the mapped perimeter within the 20-40%

# Kern Valley Hospital located 8 miles N of the mapped perimeter within the 20-40% zone.

# numerous Hazardous waste sites (11) scattered throughout all FSPro zones

# Wild and scenic rivers: none identified per available data

# *** Report continues on next page ***

# Values assessed in this Report:

# NOTE: Analysis of assets within the 80% Spread Probability Zone includes values-at-risk that may be within the active fire perimeter; any assets within the active perimeter are not independently analyzed.

# Primary land jurisdictions (Table )

# Subtotals of USFS jurisdictions within designated roadless or wilderness areas (Table 2)

# Building cluster points per Kern County GIS parcel layer (Table 3)

# Power transmission lines (Table 4)

# Water pipelines – aqueducts – canals (Table 5)

# Other Landmarks (Table 6)

# Jurisdictions within FSPro Spread Zones:

Table

| Jurisdiction | USFS - Total | BLM | DOD | State | Private |
| --- | --- | --- | --- | --- | --- |
| FSPro Zone | In Zone | Cum. | In Zone | Cum. | In Zone | Cum. | In Zone | Cum. | In Zone | Cum. |
| > 80% | 61,714 | 61,714 | 26,861 | 26,861 | 0 | 0 | 0 | 0 | 23,596 | 23,596 |
| 60 - 80 % | 7,926 | 69,640 | 18,701 | 45,562 | 0 | 0 | 0 | 0 | 11,832 | 35,428 |
| 40 - 60 % | 5,095 | 74,735 | 28,739 | 74,301 | 0 | 0 | 29 | 29 | 18,221 | 53,649 |
| 20 - 40 % | 3,579 | 78,314 | 52,007 | 126,308 | 0 | 0 | 468 | 497 | 35,664 | 89,313 |
| 5 - 20 %* | 16,182 | 94,496 | 82,853 | 209,161 | 494 | 494 | 4,517 | 5,013 | 76,726 | 166,039 |
| 1 - 5 %* | 53,830 | 148,326 | 62,054 | 271,214 | 93 | 587 | 4,173 | 9,187 | 120,725 | 286,764 |
| * These zones are under-represented due to limited extent of area modeled. |  |  |  |  |

# USFS Designated Roadless and Wilderness Areas: These acres are subtotals of USFS-Total jurisdiction acres

Table

| Jurisdiction | USFS - IRA | USFS - Wild | USFS - PRNA |
| --- | --- | --- | --- |
| FSPro Zone | In Zone | Cum. | In Zone | Cum. | In Zone | Cum. |
| > 80% | 31,496 | 31,496 | 0 | 0 | 354 | 354 |
| 60 - 80 % | 5,525 | 37,021 | 0 | 0 | 1,492 | 1,846 |
| 40 - 60 % | 3,001 | 40,021 | 0 | 0 | 414 | 2,260 |
| 20 - 40 % | 915 | 40,936 | 205 | 205 | 0 | 2,260 |
| 5 - 20 %* | 2,490 | 43,427 | 7,939 | 8,144 | 0 | 2,260 |
| 1 - 5 %* | 28,676 | 72,102 | 13,340 | 21,483 | 0 | 2,260 |
| * These zones are under-represented due to limited extent of area modeled. |

# *** Report continues on next page ***

# Estimates of Structure Values at Risk: Estimate is derived from analysis of Kern County GIS AND/OR Assessor data; count represents building clusters*.

# Note: Recreation residences and special use structures data are not available from USFS and are not identified or analyzed in this report.

Table

|  | Acres Threatened | Structure Value Ravalli COUNTY |
| --- | --- | --- |
| Fire Spread Probability Zone | Acres by Zone | Cumulative Acres | Count by Zone | Cumulative Count | Value by Zone | Cumulative Value |
| > 80% | 112,171 | 112,171 | 112 | 112 | $16,761,024 | $16,761,024 |
| 60 - 80 % | 38,459 | 150,630 | 74 | 186 | $11,074,248 | $27,835,272 |
| 40 - 60 % | 52,083 | 202,713 | 128 | 314 | $19,155,456 | $46,990,728 |
| 20 - 40 % | 91,718 | 294,432 | 1,482 | 1,796 | $221,784,264 | $268,774,992 |
| 5 - 20 % | 180,772 | 475,204 | 1,640 | 3,436 | $245,429,280 | $514,204,272 |
| 1 - 5 % | 240,875 | 716,078 | 696 | 4,132 | $104,157,792 | $618,362,064 |

# * Building Clusters represent the center of parcels where county assessor records indicate taxable improvements are present. One or more structures and/or other improvements may exist proximate to these point locations. Accuracy of cluster points decreases with large parcel areas.   Valuation of building clusters is based on inflation adjusted average home value of $149,652 for Kern County per U.S. Census data.  Commercial assets may be undervalued.

# Table 4

| Power Transmission Lines (mi) |
| --- |
| FSPro Zone | In Zone | Cum. |
| > 80% | 1.9 | 1.9 |
| 60 - 80 % | 1.2 | 3.1 |
| 40 - 60 % | 0.9 | 4.0 |
| 20 - 40 % | 10.6 | 14.6 |
| 5 - 20 %* | 26.6 | 41.2 |
| 1 - 5 %* | 13.5 | 54.7 |

# Table 5

| Water Pipeline - Aqueduct - Canals (mi) |
| --- |
| FSPro Zone | In Zone | Cum. |
| > 80% | 0.0 | 0.0 |
| 60 - 80 % | 0.0 | 0.0 |
| 40 - 60 % | 0.0 | 0.0 |
| 20 - 40 % | 32.8 | 32.8 |
| 5 - 20 %* | 24.1 | 56.9 |
| 1 - 5 %* | 20.0 | 76.9 |

# **** Report continues on next page ****

# Table 6

| OTHER LANDMARKS | FSPro Zone |  | OTHER LANDMARKS | FSPro Zone |
| --- | --- | --- | --- | --- |
| Camp - FS | > 80 % |  | Camp or campsite | 5 - 20 % |
| Arch Site - Ruins | > 80 % |  | Miller Ranch (historical) | 5 - 20 % |
| Scout Camp Blum | > 80 % |  | Tungsten Chief Mill (historica | 5 - 20 % |
| Gallup Camp (historical) | > 80 % |  | Arnold Ranch | 5 - 20 % |
| The George Lodge (historical) | > 80 % |  | Auxiliary Dam Campground | 5 - 20 % |
| Bob Rabbit Place | > 80 % |  | Black Hills Corral | 5 - 20 % |
| Burton Mill | > 80 % |  | Borel Powerhouse | 5 - 20 % |
| Camp Nick Williams | > 80 % |  | Camp Fifteen | 5 - 20 % |
| Faust Mill | > 80 % |  | Goff Ranch | 5 - 20 % |
| Flood Ranch | > 80 % |  | Havilah Forest Service Station | 5 - 20 % |
| Landers Meadow Guard Station | > 80 % |  | Hobo Campground | 5 - 20 % |
| Liebel Ranch | > 80 % |  | Hobo Forest Service Station | 5 - 20 % |
| Piute Lookout | > 80 % |  | Johns Ranch | 5 - 20 % |
| Russell Ranch | > 80 % |  | Kern Valley Marina | 5 - 20 % |
| Walser Ranch | > 80 % |  | Kernvale | 5 - 20 % |
| Camp - FS | 60 - 80 % |  | Kissack Cove Boat Ramp | 5 - 20 % |
| Piute Ranch | 60 - 80 % |  | Knox Ranch | 5 - 20 % |
| Camp - FS | 40 - 60 % |  | Launch Area Number Nineteen | 5 - 20 % |
| Arch Site - Ruins | 40 - 60 % |  | Lazells Ranch | 5 - 20 % |
| Dove Spring Mill (historical) | 40 - 60 % |  | Main Dam Campground | 5 - 20 % |
| Arrastre | 40 - 60 % |  | Moon Ranch | 5 - 20 % |
| Harrington Ranch | 40 - 60 % |  | Paradise Cove Boat Ramp | 5 - 20 % |
| Windmill - Generator | 20 - 40 % |  | Paradise Cove Campground | 5 - 20 % |
| Dove Spring Ranch (historical) | 20 - 40 % |  | Pioneer Point Campground | 5 - 20 % |
| Freedom Hill Ranch (historical | 20 - 40 % |  | Shead Ranch | 5 - 20 % |
| Benner Ranch | 20 - 40 % |  | Slippery Rock Picnic Area | 5 - 20 % |
| Brady Ranch | 20 - 40 % |  | South Fork Picnic Area | 5 - 20 % |
| Cannon Ranch | 20 - 40 % |  | Weldons Ranch | 5 - 20 % |
| Cook Peak Lookout | 20 - 40 % |  | Williams Ranch | 5 - 20 % |
| Double S Ranch | 20 - 40 % |  | Camp - Non-FS | 1 - 5 % |
| Juniper Hills Country Club | 20 - 40 % |  | Windmill - Generator | 1 - 5 % |
| Mills Ranch | 20 - 40 % |  | Picnic Area - Non-FS | 1 - 5 % |
| Myers Ranch | 20 - 40 % |  | Democrat Guard Station (histor | 1 - 5 % |
| Wooden Shoe Annies Ranch | 20 - 40 % |  | Gundry Ranch (historical) | 1 - 5 % |
|  |  |  | Holloway Camp (historical) | 1 - 5 % |
|  |  |  | Suburu Ranch (historical) | 1 - 5 % |
|  |  |  | Bickel Camp | 1 - 5 % |
|  |  |  | Breckenridge | 1 - 5 % |
|  |  |  | Breckenridge Campground | 1 - 5 % |
|  |  |  | Breckenridge Fire Tower | 1 - 5 % |
|  |  |  | Brown Mill | 1 - 5 % |
|  |  |  | Democrat Fire Station | 1 - 5 % |
|  |  |  | Freeman | 1 - 5 % |
|  |  |  | French Gulch Lake Patrol Station | 1 - 5 % |
|  |  |  | Hog Camp | 1 - 5 % |
|  |  |  | Hungry Gulch Campground | 1 - 5 % |
|  |  |  | Isabella Marina Number Two | 1 - 5 % |
|  |  |  | Live Oak Campground | 1 - 5 % |
|  |  |  | McIvers Cabin | 1 - 5 % |
|  |  |  | Peterson Landmark Object | 1 - 5 % |
|  |  |  | Rankin Ranch | 1 - 5 % |

# END OF REPORT