| Incident Name: | Jesusita Fire | Analysis Level: | Critical Infrastructure – Primary Assets Only |
| --- | --- | --- | --- |
| State(s): | California | FSPro Analysis Name: | 5.7.2009 AM Update, 7 Day, 1000 Fires |
| RAVAR Requested: Report Date: | 7 May 2009 7 May 2009 | FSPro Projected From: | 7 May 2009 7-day projection |
| RAVAR Analyst: | Jon Rieck, RMRS Missoula – 406.329.2121 jrieck@fs.fed.us | FSPro Analyst: | Larry Hood, R5 – 530.598.1226 lhood@fs.fed.us |
| RAVAR Code: | CI_A_090507_jr | ICS-209 Incident Number: | CA-LPF-1479 |

NOTE: This report accompanies a RAVAR analysis map.

# All RAVAR products are intended for STRATEGIC use only. It is always advised that values analyzed and displayed on RAVAR maps be verified by local knowledge.

# FSPro Information:

# Details relating to FSPro assumptions, including barrier files, can be found by choosing the ‘View Report’ tab while the FSPro analysis is selected on the WFDSS website or by contacting the FSPro Analyst listed above.

# NOTE: The < 1% spread probability zone is displayed on the map (pale pink zone), but assets within are not summarized. This zone represents “the rare event” – confidence in this prediction is undetermined.

# Critical Infrastructure Analysis – Primary Assets Only

# General Assessment:

# The Jesusita Fire is currently burning 2 mi N of Santa Barbara on the Los Padres National Forest in Santa Barbara County, California.

# Assuming no further suppression, the 7-day fire spread projection indicates omni-directional growth. – urban interface to south

# Communities threatened:

# Santa Barbara – Fire currently burns within developed urban interface north of Santa Barbara; modeled spread runs immediately proximate to substantially portions of the entire interface zone N of the city.

# Mission Canyon - <1 mi S of the mapped fire perimeter within the >80% spread zone.

# Major Infrastructure:

# Transportation Infrastructure:

# State Hwy 192 – runs E-W through all spread zones S of the mapped fire perimeter

# Gibraltar Rd – runs N-S through all spread zones E of the mapped fire perimeter

# Power Transmission lines:  240 KV Edison main transmission lines run E-W through all spread zones and is inside the mapped fire perimeter

# Oil & Gas Pipelines:  2 pipelines run E-W through all spread zones S of the mapped fire perimeter

# Communication Towers:  196 towers scattered throughout all spread zones

# *** Report continues on next page ***

Water Resources:

  - Water Supply Infrastructure:

    - Dams, Intakes, & Treatment Plants:

      - Lauro – Dam, treatment plant and intake located <1 mi SW of the mapped fire perimeter in the >80% spread zone.

      - Sheffield – Dam and treatment plant located 1 mi S of the mapped fire perimeter in the >80% spread zone.

      - Water Pipelines, Aqueducts, Canals:  2 water pipelines S of the mapped fire perimeter in the >80% spread zone.

# Other resources threatened:

# If high priority natural resource values are present, please request a Natural & Cultural Resources (NCR) report.

# Other resources identified in ICS-209 not otherwise reported: Structures within the community of Upper and Lower Mission Canyon, Santa Barbara Botanic Gardens, cultural and historic resources within Mission Canyon, communication sites, 240 KV Edison main transmission lines serving the Mission Canyon and the city of Santa Barbara.

# Values assessed in this Report:

# NOTE: Analysis of assets within the 80% Spread Probability Zone includes values-at-risk that may be within the active fire perimeter; any assets within the active perimeter are not independently analyzed.

# Jurisdictions within FSPro Spread Zones:

| Jurisdiction | USFS - Total | Private |
| --- | --- | --- |
| FSPro Zone | In Zone | Cum. | In Zone | Cum. |
| > 80% | 451 | 451 | 4,537 | 4,537 |
| 60 - 80 % | 394 | 845 | 1,338 | 5,876 |
| 40 - 60 % | 1,233 | 2,078 | 2,450 | 8,326 |
| 20 - 40 % | 2,501 | 4,579 | 4,796 | 13,122 |
| 5 - 20 % | 8,263 | 12,842 | 5,503 | 18,624 |
| 1 - 5 % | 23,059 | 35,901 | 6,698 | 25,323 |

# *** Report continues on next page ***

# USFS Designated Roadless and Wilderness Areas: These acres are subtotals of USFS-Total jurisdiction acres

| Jurisdiction | USFS - IRA | USFS - Wild |
| --- | --- | --- |
| FSPro Zone | In Zone | Cum. | In Zone | Cum. |
| > 80% | 0 | 0 | 0 | 0 |
| 60 - 80 % | 0 | 0 | 0 | 0 |
| 40 - 60 % | 0 | 0 | 0 | 0 |
| 20 - 40 % | 0 | 0 | 0 | 0 |
| 5 - 20 % | 26 | 26 | 0 | 0 |
| 1 - 5 % | 11,689 | 11,715 | 0 | 0 |

# Estimates of Structure Values at Risk: Estimate is derived from analysis of Santa Barbara County data; count represents building cluster points*.

# Note: Recreation residences and special use structures data are not available from USFS and are not identified or analyzed in this report.

|  | Acres Threatened | Structure Value Santa Barbara County |
| --- | --- | --- |
| Fire Spread Probability Zone | Acres by Zone | Cumulative Acres | Count by Zone | Cumulative Count | Value by Zone | Cumulative Value |
| > 80% | 4,988 | 4,988 | 1,676 | 1,676 | $807,138,136 | $807,138,136 |
| 60 - 80 % | 1,732 | 6,721 | 599 | 2,275 | $288,470,014 | $1,095,608,150 |
| 40 - 60 % | 3,684 | 10,404 | 635 | 2,910 | $305,807,110 | $1,401,415,260 |
| 20 - 40 % | 7,297 | 17,701 | 555 | 3,465 | $267,280,230 | $1,668,695,490 |
| 5 - 20 % | 13,765 | 31,466 | 1,237 | 4,702 | $595,721,882 | $2,264,417,372 |
| 1 - 5 % | 29,758 | 61,224 | 935 | 5,637 | $450,282,910 | $2,714,700,282 |

* Building Cluster Points approximate the location of one or more structures. Most building cluster points represent the center of parcels where county assessor records indicate taxable improvements are present, but may also represent structure point locations identified by county officials. Location accuracy of cluster points decreases with large parcel areas.  Building Clusters points are intended for STRATEGIC USE ONLY. It is always advised that specific structure location be verified by local knowledge.   Valuation of building cluster points is based on inflation adjusted average home value of $481,586  for Santa Barbara County per U.S. Census data.   Commercial assets may be undervalued.

# Expected Structures Threatened (assuming no suppression) = 2594

# (Expectation = No. of structures x prob. of fire spread within zone)

# **** Report continues on next page ****

# Oil and Gas Pipelines (mi):

| Sempra Energy Oil and Gas Pipelines (mi) |
| --- |
| FSPro Zone | In Zone | Cum. |
| > 80% | 5 | 5 |
| 60 - 80 % | 1 | 6 |
| 40 - 60 % | 0 | 6 |
| 20 - 40 % | 1 | 7 |
| 5 - 20 % | 2 | 9 |
| 1 - 5 % | 3 | 12 |

# Power Transmission Lines (mi):

| Power Transmission Lines (mi) |
| --- |
| FSPro Zone | In Zone | Cum. |
| > 80% | 13 | 13 |
| 60 - 80 % | 5 | 18 |
| 40 - 60 % | 5 | 23 |
| 20 - 40 % | 10 | 33 |
| 5 - 20 % | 12 | 45 |
| 1 - 5 % | 14 | 59 |

# **** Report continues on next page ****

# Other Landmarks:

| OTHER LANDMARKS | FSPro Zone |
| --- | --- |
| Santa Barbara Tennis Club | > 80 % |
| none identified per available data | 60 - 80 % |
| Santa Barbara County Bowl | 40 - 60 % |
| none identified per available data | 20 - 40 % |
| Campsite - FS | 5 - 20 % |
| Forbush Campground | 5 - 20 % |
| Forbush Flat Rustic Campsite | 5 - 20 % |
| Hot Springs Club | 5 - 20 % |
| Montecito Country Club | 5 - 20 % |
| San Marcos Trout Club | 5 - 20 % |
| Santa Barbara Radio Range Station | 5 - 20 % |
| USFS Facility | 1 - 5 % |
| Picnic Area - FS | 1 - 5 % |
| Live Oak Dairy Ranch (historic | 1 - 5 % |
| Romero Saddle Guard Station | 1 - 5 % |
| Blue Canyon Campground | 1 - 5 % |
| Cottam Campground | 1 - 5 % |
| Fall Recreation Site | 1 - 5 % |
| Hidden Potvero Rustic Campsite | 1 - 5 % |
| Lower Camuesa Campground | 1 - 5 % |
| Lower Oso Campground | 1 - 5 % |
| Middle Camuesa Campground | 1 - 5 % |
| Ninteen Oaks Campground | 1 - 5 % |
| Red Rock Campground | 1 - 5 % |
| Sage Hill Campground | 1 - 5 % |
| Santa Ynez Campground | 1 - 5 % |
| Upper Camuesa Campground | 1 - 5 % |
| Upper Oso Campground | 1 - 5 % |
| White Oaks Campground | 1 - 5 % |

# END OF REPORT