80 – AIRCRAFT

Table of Contents												Pages

80 – AIRCRAFT	316

81 - AIRCRAFT INVENTORY	316

81.1 LEAD PLANES/ AERIAL SUPERVISION AIRCRAFT (ASM)	316

81.2 - AIRTANKERS	317

81.3 – HELICOPTERS	318

81.3.1 FOREST SERVICE FIRE WATCH HELICOPTERS	319

81.4 - AIR ATTACK/TACTICAL AIRCRAFT	319

81.4.1 - NATIONAL AIR ATTACK COVERAGE – OFF SEASON ROTATION	320

81.5 - CALL WHEN NEEDED - TRANSPORT/RECON	321

81.5.1 AIR ATTACK AND FIRE DETECTION AIRCRAFT	321

81.5.2 OTHER PROGRAM USE OF CWN AIRCRAFT	321

81.5.3 - APPROVED CALL WHEN NEEDED AIRCRAFT AND PILOTS	321

81.5.4 - CWN HELICOPTERS	322

81.6 - SMOKEJUMPER AIRCRAFT	322

81.7 - INFRARED AIRCRAFT	322

81.8 – LARGE TRANSPORT CONTRACT AIRCRAFT	323

82 - AIRCRAFT INSPECTORS AND AIRCRAFT OPERATIONS SPECIALISTS	323

83 - AIRPORT  GUIDE	323

83.1 AIRPORT  CONDITIONS	323

84 - MAFFS OPERATING BASES	323

# 80 – AIRCRAFT

# 81 - AIRCRAFT INVENTORY

## 81.1 LEAD PLANES/ AERIAL SUPERVISION AIRCRAFT (ASM)

- All dispatching of Lead Planes/ASMs will be done by the GACCs. Requests for Lead/ASM planes will go to the respective GACC Coordinators/CALFIRE Operations Duty Officer for consideration.  Normal ordering procedures will be followed.

- There are three Forest Service Lead Planes/ASM assigned to California: One in Southern California GACC at Lancaster Fox Field, and two at the Northern California Service Center in Redding. They are staffed seven days a week during the summer months, and are available the rest of the year, pilot dependent.

- There is one BLM Lead Plane/ASM assigned to California, working out of Lancaster Fox Field.

- The GACC Federal Aircraft Coordinators will coordinate with the two Aviation Groups for the availability and assignments for all Federal Lead/ASM planes.

- GACCs/CAL FIRE Operations Coordination Center (OCC) will be responsible for the Aircraft Flight Schedules, form 9400-1a, when needed for the aircraft.

| LEAD Number | Pilot | LOCATION | STATUS |
| --- | --- | --- | --- |
| 5-1 | Mike Dietz | Redding | T |
| 5-2 | Mike Savage | Fox Field | T |
| 5-3 | VACANT | Fox Field |  |
| 5-4 | VACANT | Fox Field |  |
| 5-5 | Travis Strahan | Redding | Q/M |
| 5-6 | VACANT | Redding |  |
| 5-7 | VACANT | Fox Field |  |
| 5-8 | Dave Spliethof | Redding | Q/M/S/V |
| 5-9 | Dan Johnson | Redding | Q/M/I/C/S/V |
| B-5 | Mike Lynn - BLM | Fox Field | Q/M/C/V |
| C-1 | Robert Coward | Redding - CAL FIRE | Q/M/V |
| C-2 | Lynn Flock | Victorville - CAL FIRE | Q/M/V |
|  | Brad Richards John Litton John Blumm | Redding Fox Field Redding | S I/S S/H |
| Q = Qualified | M = MAFFS Lead | T = Trainee | C = Check Airman |
| I = Instructor | S = Smokejumper Pilot | H = Cobra Helicopter | V = VLAT Lead |

## 81.2 - AIRTANKERS

All airtanker(s) will be released daily and reordered under a new request number for the following day.

NOTE:  Due to shortage of National Airtankers their number and availability can not be determined.

| BASES | AGENCY |
| --- | --- |
| Ukiah (UKI) | CAL FIRE |
| Klamath Falls, OR (LMT) | USFS |
| Rohnerville (FOT) | CAL FIRE |
| Redding (RDD) | CAL FIRE/USFS |
| Chester (O05) | USFS |
| Chico (CIC) | CAL FIRE |
| Grass Valley (GOO) | CAL FIRE |
| Stead, NV (RTS) | BLM |
| Sonoma (STS) | CAL FIRE |
| Columbia (O22) | CAL FIRE |
| Hollister (CVH) | CAL FIRE |
| Fresno (FAT) | CAL FIRE/USFS |
| Porterville (PTV) Bishop (BIH) | BLM/USFS USFS |
| Paso Robles (PRB) | CAL FIRE |
| Lancaster (WJF) | USFS |
| Hemet/Ryan (HMT) | CAL FIRE |
| San Bernardino (SBD) | USFS |
| Ramona (RMN) | CAL FIRE/USFS |
| Victorville (VCV) | CAL FIRE |
| RELOAD BASES |  |
| McClellan (MCC) | CAL FIRE |
| Siskiyou (SIY) | USFS |
| Stockton (SCK) | USFS |
| Santa Maria (SMX) | USFS |

## 81.3 – HELICOPTERS

Aircraft are assigned numbers and are prefixed with the word "Helicopter".

FEDERAL

| HELICOPTER NUMBER | FOREST/AGENCY | BASE |
| --- | --- | --- |
| 502 R | Klamath - KNF | Scott Valley - A30 |
| 503 | Klamath - KNF | Happy Camp - 36S |
| 506 | Shasta - Trinity-SHF | Trinity - TRI |
| 510 | Lassen - LNF | Chester - 5Q2 |
| 512 | Plumas - PNF | Quincy - QCY |
| 514 | Tahoe - TNF | Grass Valley - GOO |
| 516 | Eldorado - ENF | Pacific – PAC |
| 517 | Stanislaus - STF | Bald Mt - 76CA |
| 520 | Sierra - SNF | Trimmer - TRM |
| 522 R | Sequoia - SQF | Peppermint - PMT |
| 523 | Sequoia - SQF | Kernville - L05 |
| 525 | Inyo - INF | Independence - 207 |
| 527 | Los Padres - LPF | ArroyoGrande - ARG |
| 528 | Los Padres - LPF | Santa Ynez - IZA |
| 530 | Los Padres - LPF | Chuchupate – CHU |
| 531 | Angeles - ANF | Chilao - CHI |
| 534 | San Bernardino - BDF | Heaps Peak - HPS |
| 535 | San Bernardino - BDF | Keenwild - KEN |
| 538 | Cleveland - CNF | Ramona - RMN |
| 551 | Yosemite - YNP | Crane Flat - CFL |
| 552 | Sequoia NP - KNP | Ash Mountain - AMH |
| 553 | BLM Susanville - NOD | Ravendale - RAV |
| 554 | BLM CA Desert - CDD | Apple Valley - APY |

R= Rapple

| Heavy bases | FOREST/AGENCY | BASE |
| --- | --- | --- |
| Type 1L or 2L | Angeles - ANF | Lancaster – WJF |
| Type 1L or 2L | San Bernardino - BDF | San Bernardino - SBD |
| Type 1L or 2L | Cleveland - CNF | Hemet - HMT |
| Type 1L or 2L | Sierra - SNF | Ramona - 068 |
|  | - |  |
| Type 1L or 2L | Los Padres - LPF | Casitas - CAS |
| Type 1L or 2L | Eldorado - ENF | Pacific - PAC |
| Type 1L or 2L | Lassen -LNF | Chester - 5Q2 |
| Type 1L or 2L | Klamath - KNF | Siskiyou - SIY |
| Type 1L or 2L | Tahoe - TNF | Truckee – TRK |

Type  1L or 2 L                           Sequoia – SQF			Porterville - PTV

CAL FIRE

| HELICOPTER NUMBER | AGENCY/UNIT | BASE - Identifer |
| --- | --- | --- |
| 101 | CAL FIRE Northern Ops /MEU | Howard Forest - HFS |
| 102 | CAL FIRE Northern Ops /HUU | Kneeland - O19 |
| 104 | CAL FIRE Northern Ops /LNU | Boggs Mountain - BGS |
| 106 | CAL FIRE Northern Ops /SCU | Alma – ALM |
| 202 | CAL FIRE Northern Ops /LMU | Bieber - BBR |
| 205 | CAL FIRE Northern Ops /TGU | Vina - VNA |
| 301 | CAL FIRE Southern Ops /RRU | Hemet/Ryan - HMT |
| 305 | CAL FIRE Southern Ops /BDU | Prado - PDO |
| 404 | CAL FIRE Southern Ops /TCU | Columbia - O22 |
| 406 COUNTY HELICOPTER NUMBER Varies Varies Varies | CAL FIRE Southern Ops /BEU AGENCY/UNIT Ventura County/VNC Santa Barabra County/SBC San Diego County/SDC | Bear Valley – BVH |

### 81.3.1 FOREST SERVICE FIRE WATCH HELICOPTERS

There are two Forest Service Fire Watch Cobras in Region 5. One is located at Lancaster Fox Field and the other is located at Northern California Service Center in Redding.

The Fire Watch aerial supervision/remote sensing program was designed to fulfill aerial supervision needs and enhance incident management situational awareness.

- Fire Watch Capabilities:

- Air Tactical Group Supervision / Helicopter Coordination

- Mapping

- Video and Audio data recording color and infrared imagery (Full Motion Video)

- Real time audio/video downlink to support tactical fire operations.

Using the FLIR camera/moving map combination to map the fire and then down linking the information to incident personnel in real time provides a clear view of the overall situation.

A portable microwave receiver carried on the aircraft can be delivered to personnel on the incident to view real time color or infrared video of critical areas.

The Fire Watch geo-referenced FLIR system turret is integrated with the Avalex mapping system.  Data from the turret is capable of producing ESRI shape file perimeters by tracing the fire edge from a dispatch, regardless of smoke.

## 81.4 - AIR ATTACK/TACTICAL AIRCRAFT

| Air Attack | Unit | Base/FAA ICAO | Area of Influence |
| --- | --- | --- | --- |
| 01 | ANF | Fox Field - WJF | Angeles NF |
| 05 | KNF | Siskiyou - SIY | Klamath NF |
| 06 | LNF | Chester - O05 | Chester Air Attack Zone – IR Equipped |
| 07 | LPF | Santa Marie SMX - | Los Padres – IR Equipped |
| 12 | BDF | San Bernardino-SBD | San Bernardino and Cleveland NF's |
| 507 | ONC | Redding - RDD | North Ops - IR Equipped |
| 509 | OSC | Fox Field - WJF | South Ops - IR Equipped |
| 15 | SNF | Fresno - FAT | Fresno Air Attack Zone |
| 17 | TNF | Grass Valley - GOO | Grass Valley Air Attack Zone |
| 490 | KRN | Meadows Field - BFL | Bakersfield, Kern County |
| 110 | MEU | Ukiah - UKI | CAL FIRE Northern Ops |
| 120 | HUU | Rohnerville - FOT | CAL FIRE Northern Ops |
| 140 | LNU | Sonoma - STS | CAL FIRE Northern Ops |
| 210 | BTU | Chico - CIC | CAL FIRE Northern Ops |
| 230 | NEU | Grass Valley - GOO | CAL FIRE Northern Ops |
| 240 | RDD | Redding - RDD | CAL FIRE Northern Ops |
| 310 | RRU | Hemet/Ryan - HMT | CAL FIRE Southern Ops |
| 330 | MVU | Ramona - RMN | CAL FIRE Southern Ops |
| 340 | SLU | Paso Robles - PRB | CAL FIRE Southern Ops |
| 410 | TUU | Porterville - PTV | CAL FIRE Southern Ops |
| 430 | FKU | Fresno - FAT | CAL FIRE Southern Ops |
| 440 | TCU | Columbia - O22 | CAL FIRE Southern Ops |
| 460 | BEU | Hollister - CVH | CAL FIRE Southern Ops |
| 500 | CDF | Various | CAL FIRE Headquarters |

CAL FIRE Air Tactical on Forest Service incidents will be dispatched within the Air Tanker Base Zone of Influence according to local dispatch policy.

### 81.4.1 - NATIONAL AIR ATTACK COVERAGE – OFF SEASON ROTATION

Region 5 Air Tactical Group Supervisors (ATGS) will be available for national air attack coverage from Pay Period-24 through Pay Period-11 of the following year as follows:

-One primary and one relief ATGS will be available from Pay Period-24 through Pay Period-11. The need and type of platform will be discussed at the time of the order. (Agency aircraft vs CWN)

-The ATGS chair or assistant will be the primary contact to both GACCs.

-Pat Basch (Sierra National Forest) ATGS Chair; Phil Hawkins (Shasta-Trinity National Forest)ATGS  Co-Chair

-ATGS will take an ATGS Trainee on each assignment, if feasible.

-ATGS can be ordered with IR capabilities.

-Primary ATGS will be on four hour call.

-Relief ATGS will be on eight hour call.

| Pay Period | Primary ATGS | Relief ATGS |
| --- | --- | --- |
| 24 | AA - 01 | AA - 05 |
| 25 | AA - 05 | AA - 06 |
| 26 | AA - 06 | AA - 07 |
| 01 | AA - 07 | AA - 12 |
| 02 | AA - 12 |  |
| 03 |  | AA - 17 |
| 04 | AA - 17 | AA - 14 |
| 05 | AA - 14 | AA - 15 |
| 06 | AA - 15 | AA - 01 |
| 07 | AA - 01 | AA - 05 |
| 08 | AA - 05 | AA - 06 |
| 09 | AA - 06 | AA - 07 |
| 10 | AA - 07 | AA - 12 |
| 11 | AA - 12 |  |

## 81.5 - CALL WHEN NEEDED - TRANSPORT/RECON

### 81.5.1 AIR ATTACK AND FIRE DETECTION AIRCRAFT

Forest Service requests for CWN aircraft will be placed to the appropriate GACC. The aerial observer or ATGS’s name, the date and time needed, delivery location, and Firecode must be identified prior to the request being placed up to the GACC. The GACC will process requests for Federal aircraft directly with the fixed wing vendor.

Forest Service CWN aircraft may use the forest number as its call sign when a qualified ATGS is aboard.

Example: Shasta-Trinity National Forest, Forest number is 14 , AA-14

Forest Service has pre-assigned aircraft call signs are to be used when utilizing CWN Aircraft as fire detection reconnaissance aircraft. When the aircraft are being used for activities other than for fire detection the FAA registration number will be used as the call sign.

| FOREST | RECON NUMBERS |
| --- | --- |
| Angeles | Recon 10, 11, 12 |
| Cleveland | Recon 13, 14, 15 |
| Eldorado | Recon 16, 17, 18 |
| Inyo | Recon 19, 20, 21 |
| Klamath | Recon 22, 23, 24 |
| Lassen | Recon 25, 26, 27 |
| Los Padres | Recon 28, 29, 30 |
| Mendocino | Recon 31, 32, 33 |
| Modoc | Recon 34, 35, 36 |
| Sequoia | Recon 37, 38, 39 |
| Plumas | Recon 40, 41, 42 |
| San Bernardino | Recon 43, 44, 45 |
| Six Rivers | Recon 46, 47, 48 |
| Shasta-Trinity | Recon 49, 50, 51 |
| Sierra | Recon 52, 53, 54 |
| Stanislaus | Recon 55, 56, 57 |
| Tahoe | Recon 58, 59, 60 |
| Lake Tahoe Basin | Recon 61, 62, 63 |
| Susanville BLM | Recon 64, 65, 66 |
| Bakersfield BLM | Recon 67, 68, 69 |
| California Desert District | Recon 70, 71, 72 |

### 81.5.2 OTHER PROGRAM USE OF CWN AIRCRAFT

Forest Service requests for CWN aircraft will be placed to the appropriate GACC. The Fixed Wing Manager’s name, the date and time needed, delivery location, and Firecode must be identified prior to the request being placed up to the GACC. The GACC will process requests for Federal aircraft directly with the fixed wing vendor.

When the aircraft are being used, the FAA registration number will be used as the call sign.

Example:  N1622 tail number, “Forest Health- 622”

### 81.5.3 - APPROVED CALL WHEN NEEDED AIRCRAFT AND PILOTS

A Federal listing of pilots and aircraft carded for the current year are kept at the GACC level.

(see California Mobilization Guide Section Chapter 28.9 for more ordering information)

### 81.5.4 - CWN HELICOPTERS

Forest Service requests for CWN Helicopters will be placed to the appropriate GACC.  The GACC will place requests for T1 and T2 CWN Helicopters up to the NICC.  The Helicopter Manager’s name, the date and time needed, delivery location, and Firecode/Charge Code must be identified prior to the request being placed up to the NICC.  The GACC will process requests for Federal T3 CWN Helicopters directly with the vendor.  National policy requires a manager be assigned to every helicopter prior to arriving at the incident.  The helicopter and manager will be married up at a non-fire incident location.

Department of Interior requests for CWN helicopters can be processed by the DOI unit directly (BLM, NPS, BOR, etc).  All Type 1 and 2 helicopter requests will be placed to the GACC, who will then place them up to the NICC.  All Type 3 and Type 4 CWN helicopters that are located within the administrative jurisdiction of a BLM District may be ordered by the appropriate Dispatch Center from the AMD Source List.  The ordering unit will order or provide a qualified Helicopter Manager and crew members. (see California Mobilization Guide Chapter 28.10 for more ordering information)

CAL FIRE requests can be filled at the Unit or GACC level from their approved vendor list.  Refer to CAL FIRE Handbook 8300 section 8353.  Instructions for filling requests can also be in the CAL FIRE email program, Outlook. It is located under - Public Folders, All Public Folders, Sacramento HQ Units, Fire Protection, Aircraft Call When Needed.

## 81.6 - SMOKEJUMPER AIRCRAFT

At Northern California Service Center, the Region maintains two smokejumper (para-cargo) fixed wing aircraft during the active fire season.  They use the radio call signs “Jump 5-1” and “Jump 5-2”.  Any requests for additional Smokejumper aircraft for non-initial attack assignments will be placed up by the GACC to the NICC.  Initial attack needs may be met by following Initial Attack agreements in place between GACCs.

Refer to Chapter 60 of this guide for Operational Procedures for the Regional base and any satellite bases.

## 81.7 - INFRARED AIRCRAFT

Federal Infrared Aircraft are requested through the GACC.  Agency aircraft will be committed before vendor aircraft are utilized.

Forest Service IR Aircraft

- King Air 200			NIFC		N149Z

- Citation II			NIFC		N144Z

- Bell 209 (FIREWATCH)	R5		N109Z

- Bell 209 (FIREWATCH)	R5		N107Z

- Commander 690-B		R5		N700PQ- AA-07

- Commander 680-FL		R5		N634CT- AA-06

- Beech A100 (FireMapper)	R5                         N127Z

See California Mobilization Guide Chapter 28.2.10 for information on requesting an IR mission flight.

## 81.8 – LARGE TRANSPORT CONTRACT AIRCRAFT

All requests for large transport aircraft will be processed through the GACCs.  These requests will be placed on a flight request/schedule form, (Form 9400-1a).  The GACCs will place these requests with the NICC at least 48 hours before the flight is needed.

See California Mobilization Guide Chapter 28.10 for information needed to schedule aircraft.

81.9 -- OTHER FOREST SERVICE AIRCRAFT

There are three other Forest Service owned aircraft available for non-fire or law enforcement missions: including but not limited to: Non-fire IR work, forest health surveies, personal/cargo transport, animal telemtry backcountry airfield inspections and off-airport training platforms. These aircraft can be request for use through the GACCs.

# 82 - AIRCRAFT INSPECTORS AND AIRCRAFT OPERATIONS SPECIALISTS

Annually the Regional Office Aviation and Fire Management revises FS/CAL FIRE pilot authority for inspectors in aircraft operation.

# 83 - AIRPORT  GUIDE

The Pilots Guide to California Airports will be used in California.  It is recommended that each Unit maintain their own copy(s) through the subscription process or have access to the internet site.

## 83.1 AIRPORT  CONDITIONS

When visibility starts to deteriorate to Instrument Flight Rules (IFR), notification to the GACC needs to be made over the intercom.  This will assist in the repositioning of initial attack aircraft to another base where visibility is better.

Airtanker bases need to advise their respective GACCs whenever conditions make aerial resources unavailable and when they become available again due to weather or mechanical reasons.

# 84 - MAFFS OPERATING BASES

| GACC | AIRPORT NAME | LOCATION | REMARKS |
| --- | --- | --- | --- |
| Southern California (OSCC) |
|  | San Bernardino International | San Bernardino, CA | R/H/F Portable Retardant Plant |
|  | Pt Mugu/Channel Islands | Ventura, CA | H/F Portable Retardant Plant |
|  | Fresno Air Terminal | Fresno, CA | R Limit 4 Aircraft |
|  | Paso Robles Base | Paso Roble, CA | R |
| Northern California (ONCC) |
|  | McClellan ATB | Sacramento, CA | H/F -Portable Retardant Plant. |
| Southern Oregon (NWCC) | Kingsley Field | Klamath Falls, OR | R/H/F |

R= Reload, H= Hubb, F=Full Activiation

**Four additional bases are under review at this time: CIC, WJF, VCV and SMX.

REFER TO MAFFS OPERATING PLAN for detailed information on MAFFS OPERATIONS at:

http://www.nwcg.gov/teams/ibpwt/documents/cooprelations/fs_maffs_guide.htm

THIS PAGE INTENTIONALLY LEFT FOR NOTES