FIRE BEHAVIOR FORECAST

FORECAST NO.: 7

NAME OF FIRE: Duck Lake					PREDICTED FOR: Day Shift

UNIT:  Newberry FMU						SHIFT DATE:  6/03/12

TIME AND DATE						SIGNED:___ J. Burnham_________

FORECAST ISSUED: 6/04/12 1715			             	  FIRE BEHAVIOR ANALYST

WEATHER FORECAST: Patchy fog before 8am. Otherwise, sunny, with a high near 64. Calm wind becoming north between 5 and 10 mph.

SEE ATTACHED COMPLETE FORECAST.

# FIRE BEHAVIOR

GENERAL:  With about a day of drying the probability of fire activity is already increasing.  There is a pretty good chance some of the organics will start to produce flame. If these flames are under conifer trees the low hanging branches could cause some single tree torching.

SPECIFIC:

All Divisions: This was the message from yesterday - Fine Fuel Moisture Codes (Ffmc) have been reduced to 51.6 from the heavy rains. When the fire started on May 24th, the Ffmc were around 91.7 to 92. With no heavy rain events predicted for the week and warmer temperatures this will help to keep elevating our risk once again…

…Today the Ffmc is already at 72.6 from the lack of rain and warmer temperatures. This will help to produce flame lengths of up to 2 ft in the immature jack pine(M4) and small diameter open grown type spruce stands (C2). Spread rates are also slowly increasing from nothing yesterday topping out at 2 ft/min today.

AIR OPERATIONS: Sunrise is at 5:52 a.m. and Sunset is at 9:28 p.m.

From National Wx Service:

VFR CONDITIONS WILL CONTINUE...AS HIGH PRESSURE REMAINS OVERHEAD. NNE GUSTS NEAR 20KTS AT SAW WILL QUICKLY DIMINISH WITH THE LOSS OF DAYTIME HEATING. A NEARING TROUGH FROM MN WILL NEAR IWD TOWARD DAYBREAK MONDAY. THE MAIN RESULT WILL BE MID TO HIGH CLOUDS...WHICH WILL STAY IN THE VFR CATEGORY

SAFETY:   More heat and lower humidity will allow the ground heat to start showing. Hot pockets of organics were detected using the thermo scanner where surface smoke was not present; some of these areas down 2 ft deep. Sheltered heavy fuels will have potential to flare up with improving weather.