FIRE BEHAVIOR FORECAST

FORECAST NO.: 10

NAME OF FIRE: Duck Lake					PREDICTED FOR: Day Shift

UNIT:  Newberry FMU						SHIFT DATE:  6/08/12

TIME AND DATE						SIGNED: W. Sterrett

FORECAST ISSUED: 6/07/12 1900			             	  FIRE BEHAVIOR ANALYST

WEATHER FORECAST:

Partly cloudy morning but increasing clouds and humidity with chances increasing for rain toward afternoon.  Thunderstorms possible in the evening.

SEE ATTACHED COMPLETE FORECAST.

# FIRE BEHAVIOR

GENERAL:  Today will be more humid and winds should actually decrease a little as the day goes on and a warm front with rain showers approaches.

SPECIFIC:

Models still predict moderate fire activity even with higher humidity due to the preceding days of drying. Immature jack pine(C4) and spruce(C2) are going to have the fastest ROS at 29 to 26 ft/min and (H)flame lengths of 10 to 13ft.  INTERMITENT CROWNING AT THE HEAD IS A POSSIBILITY IF WINDS BECOME GUSTY OR STRONGER THAN PREDICTED.

While spotting potential should be down, mature red and white pine (C5) and mixed hardwood with conifer(M2) will have the higher probability of ignition of 78% with flame lengths maxing out at around 6ft.

If thunderstorms do develop, watch for strong and erratic winds which can drastically affect fire behavior.

SAFETY:   Partially burned areas of the fire have readily available fuel that will burn hot and fast if something gets started.  Be heads up for the possibility of thunderstorms and resulting wind and lightning.