| INCIDENT RADIO COMMUNICATIONS PLAN | Incident Name/Incident Number WOLF CREEK | Date/Time Prepared 8/7/10 1900 | Operational Period Date/Time 0600 Aug 8, 2010 TO 1800 Aug 8, 2010 |
| --- | --- | --- | --- |
| Ch # | Function | Channel Name/Trunked Radio System Talkgroup | Assignment | RX Freq N or W | RX Tone/NAC | TX Freq N or W | TX Tone/NAC | Mode | Remarks |
| 1 | TACTICAL | USFS TAC 2 | DIVISION A | 168.2000 N | N/A | 168.2000 N | N/A | A |  |
| 2 | TACTICAL | USFS TAC 1 | DIVISION Z | 168.0500 N | N/A | 168.0500 N | N/A | A | ALL CHANNELS ARE |
| 3 |  |  |  |  |  |  |  |  | NARROWBAND |
| 4 | MEDICAL | USFS TAC 4 | SAFETY | 164.1375 N | N/A | 164.1375 N | N/A | A | MEDICAL EMERGENCY ONLY |
| 5 |  |  |  |  |  |  |  |  |  |
| 6 | CMD BACKUP | HTF LEVIATHAN | ALL DIVISIONS | 169.9750 N | N/A | 171.4250 N | 103.5 | A | TONE 8 |
| 7 | CMD REPEAT | NIFC CMD 1 | ALL DIVISIONS | 168.7000 N | N/A | 170.9750 N | 123.0 | A | TONE 2 |
| 8 |  |  |  |  |  |  |  |  |  |
| 9 |  |  |  |  |  |  |  |  | COMMAND MOVED TO |
| 10 | AIR/GND 1 | INCIDENT SPECIFIC | ALL DIVISIONS | 166.9625 N | N/A | 166.9625 N | N/A | A | CMD REPEAT |
| 11 | AIR/GND 2 | INCIDENT SPECIFIC | ALL DIVISIONS | 169.3625 N | N/A | 169.3625 N | N/A | A | NIFC CMD 1 (TONE 2) |
| 12 |  |  |  |  |  |  |  |  | CHANNEL 7 |
| 13 |  |  |  |  |  |  |  |  |  |
| 14 | AIR GUARD |  | ALL DIVISIONS | 168.6250 N | N/A | 168.6250 N | N/A | A |  |
| 15 |  |  |  |  |  |  |  |  |  |
| 16 | AIR GUARD |  | ALL DIVISIONS | 168.6250 N | N/A | 168.6250 N | N/A | A |  |
| 5. Prepared by (Communications Unit) Randy Williams/JAKE CONELY COMLs | Incident Location County State Latitude N Longitude W |

The convention calls for frequency lists to show four digits after the decimal place, followed by either an “N” or a “W”, depending on whether

the frequency is narrow or wide band.   Mode refers to either “A” or “D” indicating analog or digital (Project 25)