## Slide 1: Unit 1 - Readiness

## Slide 2: Unit 1 Objectives
Describe information and material needed for ICS/LE assignment.
Describe the information that is needed from dispatch when assigned to an incident.
Describe the check-in process upon arrival at the incident.
Describe the information gathered from the assigned supervisor at the incident.

## Slide 3: The Helicopter Crewmember
Duties and responsibilities:
Constructs helispots, prepares manifest, load/unload personnel and cargo, etc.
Assist Manager in daily checks, readiness of equipment, and facility/cache maintenance.

## Slide 4: The Helicopter Crewmember
Duties and responsibilities:
3. Proficiency checks and drills.
4. Safety sessions, critiques, passenger safety briefings, safety and welfare aspects of job.

## Slide 5: Aviation Life Support and Survival
Aviation Life Support Equipment (ALSE)
Policy states that, the responsibility of management is to “provide employees with a safe and healthful work environment.”

## Slide 6: Aviation Life Support and Survival
Agency Responsibilities:
Implementing their PPE program.
Evaluating aviation activities.
Provide employees with the appropriate
equipment and training.

## Slide 7: Aviation Life Support and Survival
Why Personal Protective Equipment (PPE)?
The following accident that occurred on August 3, 2000 will help explain the importance of PPE.

## Slide 8: Aviation Life Support and Survival
Why Personal Protective Equipment?
Bell 206L-1 August 3, 2000

## Slide 9: Aviation Life Support and Survival
The passenger sitting in the left front seat was struck in the head twice by the main rotor blades entering the front cabin area.

## Slide 10: Aviation Life Support and Survival
This helmet saved his life!

## Slide 11: Aviation Life Support and Survival
Care and Fitting of your PPE needs prior to operations, LE helicopter crewmember and passengers need to have all appropriate Mission Specific PPE:
Nomex clothing
Leather or Nomex flight gloves
Leather boots (8” tops)
Flight helmet
PPE waiver for Law Enforcement Short Haul (LEASH)

## Slide 12: Aviation Life Support and Survival
Care and Fitting of your PPE
Fire Resistant Clothing:
Clothing must be kept clean
Clothing worn over Nomex should be made of natural fibers e.g., wool, cotton.
Under garments worn under Nomex and next to skin should also be made of natural fibers.

## Slide 13: Aviation Life Support and Survival
Care and Fitting of your PPE
Flight Suit:
Should fit loosely to provide trapped air for insulation.
Sleeves should be long enough to reach the first knuckle of the thumb.
Pant legs should reach the floor while standing.

## Slide 14: Aviation Life Support and Survival
Care and Fitting of your PPE
Gloves:
Should extend above the wrist.
Should fit under a snugly secured flight suit sleeve cuff.
Should fit snugly to provide for dexterity.

## Slide 15: Aviation Life Support and Survival
Care and Fitting of your PPE
Boots:
Made of leather. (No nylon, canvas, etc.)
The flight suit should fit snugly over the tops of the boot around the ankles.

## Slide 16: Aviation Life Support and Survival
Care and Fitting of your PPE
Head, Hearing and Eye Protection:
To comply with national standards flight helmets must consist of a one-piece hard shell, that must cover the top, sides and rear of the head.

## Slide 17: Aviation Life Support and Survival
Care and Fitting of your PPE
Head, Hearing and Eye Protection:
Hearing protection program is required whenever employees are exposed to noise equal to, or exceeding an eight-hour time weighted average of 85 decibels.

## Slide 18: Aviation Life Support and Survival
Care and Fitting of your PPE
Head, Hearing and Eye Protection:
Eye protection is required in work environments where air particle contaminants are present.

## Slide 19: Aviation Life Support and Survival
Care and Fitting of your PPE
The proper fitting of the helmet
will be demonstrated and will include:
Donning and removing (doffing)
Adjusting the nape strap
Fastening and unfastening the chinstrap
Operating the sun visor

## Slide 20: Aviation Life Support and Survival
Care and Fitting of your PPE
Don the helmet as follows:
Grip the retention assembly below the earcups.
Grip and depress the ear pads into the ear cups to allow for more space to roll the helmet onto your head.
Roll the helmet back and down onto the head.

## Slide 21: Aviation Life Support and Survival
Care and Fitting of your PPE
Don the helmet as follows:
4. Check the distance between the eyebrows and the edge of the helmet shell; it should be approximately ¾” for optimum vision.
5. Tighten the rear retention assembly appropriately per manufacture specifications.

## Slide 22: Aviation Life Support and Survival
Care and Fitting of your PPE
Don the helmet as follows:
6. Fasten the chinstrap, insert snap end through the D-ring and snapping the connectors or per manufacture specifications.
Tighten the chinstrap. Once the desired tension is achieved it can be fastened and unfastened via the snap.
Lower and raise the visor to test operation and clearance.

## Slide 23: Aviation Life Support and Survival
Care and Fitting of your PPE
Remove the helmet in reverse steps
of the previous donning the helmet
instructions.

## Slide 24: Aviation Life Support and Survival
Care and Fitting of your PPE
Survival Equipment
The survival equipment each aircraft
carries depends on whether the flight will
be strictly over water, over land or
special use. There are two categories of
survival equipment:
Over Water
Over Land

## Slide 25: Aviation Life Support and Survival
Care and Fitting of your PPE
Survival Equipment
Over Water ALSE consist of:
Type of mission (extended over water or not)
Weather
Water conditions (water temp < 50 degrees F)

## Slide 26: Aviation Life Support and Survival
Care and Fitting of your PPE
Survival Equipment
Personal Flotation Devices (PFD)
An inflatable personal flotation device that meets requirements of 14 CFR 91 or inflatable life preserver required by
14 CFR 135.

## Slide 27: Aviation Life Support and Survival
Care and Fitting of your PPE
Survival Equipment
Personal Flotation Devices (PFD)
PFDs shall be worn by each individual on board the helicopter when conducting operations beyond gliding distance to shore, and during all hovering flights over water sources.
Automatic inflation (water activated) personal flotation devices shall not be allowed.

## Slide 28: Aviation Life Support and Survival
Care and Fitting of your PPE
Survival Equipment
Personal Flotation Devices (PFD)
Inflatable PFDs should not be deployed
until after you have exited the aircraft.
Deploying while inside a submerged or
overturned aircraft may make egress
impossible.

## Slide 29: Aviation Life Support and Survival
Care and Fitting of your PPE
Survival Equipment
Anti-Exposure Garments
All occupants must wear anti-exposure
garments when conducting extended
over-water flights where the water
temperature is less than 50 degrees F.

## Slide 30: Aviation Life Support and Survival
Care and Fitting of your PPE
Survival Equipment - Anti-Exposure Garments
Two Types:
Anti-exposure flight suit, a one-piece insulated coverall that provides some hypothermia protection and buoyancy.
Survival suit, a dry immersion suit made from closed cell material
Caution wearing either suit will hinder egress from
submerged or overturned aircraft.

## Slide 31: Aviation Life Support and Survival
Survival Equipment
Survival Kits
Survival kits are required for all special
use activities and are recommended for
all missions.

## Slide 32: Aviation Life Support and Survival
Knife
Signal Mirror
Signal flares (6)
Matches
Space blanket
Water (1 qt. per person)
Food (2 days per person)
Candles
Water purification tablets
Collapsible water bag
Whistle
Magnesium fire starter
Nylon Rope (50 ft.)

## Slide 33: Aviation Life Support and Survival
Personal Survival Equipment
Although policy does not require that
agency personnel carry personal survival
kits, it is recommended.

## Slide 34: Aviation Life Support and Survival Suggested personal survival kit items:
Waterproof matches
Magnesium fire starter
Space blanket
Large plastic bag
First aid kit
Knife
Hand-held radio
Water purification tablets
Signal mirror
Flashlight
Whistle

## Slide 35: Readiness for Assignment Review LE Operation Plan Suggested items to have:
LESH harness/flight gear
Operation Plan/map
Passenger/Cargo Manifest
Passenger Briefing Card
IRPG
Radio w/flight helmet connector
Cloning cable
Global positioning system (GPS)
Spare batteries
Calculator
Fiber tape
Black electrical tape
Flagging
Knife
Notepads
Blue or black pens
Unit log (ICS-214)

## Slide 36: Assignment Information
ICS Dispatch Ordering Process
When a helicopter is needed, dispatch submits an aircraft resource order.
Local agency’s and cooperators are checked
with first.
If unfilled locally the order goes to a Geographical Area Coordination Center (GACC).

## Slide 37: Assignment Information
ICS Dispatch Ordering Process
If unfilled at a GACC, it goes to the National Interagency Coordination Center (NICC).
NICC in Boise, Idaho has ultimate authority for managing national aircraft resources.
This cycle then returns to the local dispatch.

## Slide 38: Assignment Information
ICS Dispatch Ordering Process
The requesting unit must request a module be assigned to an aircraft when ordering.
When a helicopter is ordered, a manager and module must be ordered at the same time.
If available, these are filled at the regional level first, if unfilled there the order will go to the national level.

## Slide 39: Assignment Information
Acceptance of ICS Assignment
Out of unit assignment information you should
obtain before leaving your home unit.
When you accept an assignment, do not leave
your home unit until you receive a copy of the resource order from dispatch and/or Law Enforcement Supervisor.

## Slide 40: Assignment Information
Acceptance of ICS Assignment
This is usually a “Resource Order” with all the
pertinent information:
Incident Name – Block 2
Incident Order Number – Block 3
Incident Phone Number – Block 8
Request Number – Block 12
Reporting Location and Time – Block 12
Charge code – Finance Codes Box

## Slide 41
Incident Name
Incident Order Number
Request Number
Incident Phone
Report Location
Charge Code

## Slide 42: Mobilization
Be sure to:
Obtain a copy of your resource order and
request number from dispatch and/or LE Supervisor.
Determine mode of travel, comply with weight
limitations.
Commercial airline
GOV
Rental
Charter flight

## Slide 43: Mobilization
Your dispatch/ LE supervisor may be able to provide additional information:
Briefing packets/ Operation Plan
Maps
Situation and Intelligence updates
Additional radio frequencies and contacts
Flight itineraries

## Slide 44: Module Preparation
You may or may not know the other module members or where they are from.
If possible, a brief contact prior to leaving can verify items like LE equipment needs, PPE, radio, and radio equipment compatibility, any details to “marry up.”

## Slide 45: Module Preparation
The marriage of the helicopter and module usually occurs at a pre-designated location away from the incident. This is where the module manager completes the pre-use inspection and documentation.

## Slide 46: Module Preparation
On ICS assignments, the following personnel must be assigned to each aircraft:
Standard Restricted
Category Category
Type 1 Mgr + 4 Mgr Only
Type 2 Mgr + 3 Mgr Only
Type 3 Mgr + 2 Mgr Only
In Alaska, the minimum is a manager for all
categories, although there will often be modules assigned.

## Slide 47: Module Preparation
NICC will not automatically assign a module to helicopter orders; the requesting unit must request a module be assigned when ordering the aircraft.
Occasionally, crewmembers are ordered to support helibase functions.

## Slide 48: Check-In Process
Arrive at the incident and check-in.
Each individual should ensure that all information needed to complete the Check-in List (ICS-211) is provided.
This includes:
  Your resource order and request numbers
  Manifest information
  Home base
  Departure point
  Method of travel
  Other qualifications

## Slide 49: Check-In Process
Check-in Locations
You may check-in at any of the following locations:
Incident Command Post (ICP)
Base or camp
Staging area
Helibase (for direct assignment)

## Slide 50: Initial Briefing
After check-in, locate your incident supervisor (helibase manager or helicopter manager) and obtain your initial briefing.

## Slide 51: Initial Briefing
Your initial briefing should include:
The organization structure
The objectives
Status of the incident/project
Current and predicted weather
Law Enforcement Jurisdiction(s)
Obtain a copy of the Incident Action/ Operation Plan (IAP) or Project Aviation Safety Plan (PASP)

## Slide 52: Initial Briefing
Your initial briefing should include:
Hazard/safety issues
Assigned duties
Radio frequencies
Other resources
Flight hazard map
Maps of the area

## Slide 53: Initial Briefing
Your initial briefing should include:
Meals
Helibase layout
Helispot locations
Deck procedures
Briefing/debriefing times
Crash rescue procedures and plan

## Slide 54: Initial Briefing
Forms in the Incident Action Plan (IAP)
ICS 201 Incident Briefing
ICS 202 Incident Objectives
ICS 203 Organization Assignment List
ICS 204 Assignment List
ICS 205 Incident Radio Communication Plan
ICS 206 Medical Plan
ICS 220 Air Operations Summary

## Slide 55: Unit 1 Objectives
Describe information and material needed for ICS/ LE assignment.
Describe the information that is needed from dispatch when assigned to an incident.
Describe the check-in process upon arrival at the incident.
Describe the information gathered from the assigned supervisor at the incident.