## Slide 1: Unit 4 - Communications

## Slide 2: Unit 4 Objectives
Ensure all communication is performed using clear text.
Describe the process of communication within the chain of command.
Demonstrate proper radio usage.
Describe helicopter marshalling procedures and techniques.

## Slide 3: Communication Protocol
Clear Text
Clear Text is the use of the English language to communicate. All radio transmissions, written messages, and verbal instructions will be in clear text.
No ten codes or agency specific codes are used when using clear text.

## Slide 4: Communication Protocol
Clear Text
Use clear text
Be brief, clear and to the point (short concise communication).
Plan your transmission before you key the radio. “Don’t think out loud on the radio”.

## Slide 5: Communication Protocol
Flight Plans and Flight Following
All aviation missions for USFS and Department of the Interior agencies, regardless of how simple or complex, are required to have an approved flight plan filed.
This is a detailed outline of where, when, and how the mission will be flown.

## Slide 6: Communication Protocol
Either of the following is an acceptable flight plan.
  Federal Aviation Administration (FAA) flight plan
  Agency flight following

## Slide 7: Communication Protocol
Flight Plans and Flight Following
FAA flight plans shall be filed by the pilot prior to take-off whenever possible.

## Slide 8: Communication Protocol
Agency flight following (radio) providing:
  Flight following will be accomplished under
  the agency’s written flight following policy.
  Radio contact will be made at predetermined
  intervals not to exceed one hour. (Most
  agencies use predetermined intervals of less
  than one hour, e.g., 15 to 30 minutes).

## Slide 9: Communication Protocol
Agency flight following (radio) providing:
  Position reports or amendments are
  communicated and recorded.
  Personnel tasked with flight following
  responsibility must monitor the
  communications radio at all times during the
  flight.

## Slide 10: Communication Protocol
Aircraft type and identification
Aircraft color
Pilot name(s)
Fuel on board
Passenger(s) name(s)
Passenger/cargo weight
Nature of mission
Flight routes/point of departure/destination
Estimated duration of mission
Estimated time of departure
Estimated time of arrival
Check-in procedures
    Agency Flight Following Must Minimally Include:

## Slide 11: Communication Protocol
Automated Flight Following (AFF):
AFF is a satellite/web-based system, which allows the dispatcher to monitor aircraft location on a computer screen.
AFF is an approved method of agency flight following. Most agency aircraft have AFF capability.

## Slide 12: Communication Protocol

## Slide 13: Communication Protocol
Flight Planning (emergency response for
overdue/missing aircraft)
Filing a written flight plan and flight following may double your odds of surviving an aircraft mishap.
  The average time for SAR initial notification is about 30 minutes.
  Average time for SAR units to arrive on scene is about 4 hours.

## Slide 14: Communication Protocol
Flight Planning (emergency response for
overdue/missing aircraft)
A written flight plan and flight following dramatically decreases the response time for SAR efforts. It may still require more than five hours for individuals to check and confirm there is a missing aircraft.

## Slide 15: Communication Protocol
Flight Planning (emergency response for
overdue/missing aircraft)
By the time SAR efforts locate the aircraft and arrive on scene, an average time of 38 hours has passed.
What is the potential of surviving a trauma if it takes more than a day to get to you?

## Slide 16: Communication Protocol
Flight Planning (emergency response for
overdue/missing aircraft)
Without a flight plan, in a downed aircraft, with minor injuries, your survival chances are slim. (FAA average 35.5 hours)

## Slide 17: Communication Protocol
Flight Planning (emergency response for
overdue/missing aircraft)
More than three days (FAA average of 82 hours) may pass before someone arrives at the scene of the accident.

## Slide 18: Communication Protocol
Flight Planning (emergency response for
overdue/missing aircraft)
Post-Crash Survival Time–After an accident in a remote area, an injured person may survive for one day. An uninjured person may survive for three days.

## Slide 19
Request for Search & Rescue
SAR Alert
Arrival
Flight Following 0.5 hrs 4.0 hrs
Flight Plan 5.5 hrs 38.0 hrs
No Flight Plan 35.5 hrs 82.0 hrs
Post-Crash Survival Time
Injured – 24 Hours
Uninjured – 72 Hours

## Slide 20: Communication Protocol
Flight Planning (emergency response for
overdue/missing aircraft)
Consider the environment that you will be flying in. Bring clothing and/or supplies commensurate with the conditions in the event you have a mishap.
Know your agencies policy is regarding supplemental survival equipment.

## Slide 21: Communication Protocol
Communication structure for aircraft/Air Ops
organization including
ground resources.

## Slide 22: Communication Protocol
Communication within the Chain of Command
The chain of command refers to the orderly line of authority.
Assignments and request occurs only with the person directly above or below.
Follow the chain of command when contacting another section or function.

## Slide 23: ICS Radio Communications
Ground Communications
Logistics
Line operations
Operations Section Chief
Helibase operations

## Slide 24: ICS Radio Communications
Air to Ground Communications
Air attack
Flight following
Takeoff and landing coordinator

## Slide 25: ICS Radio Communications
Air to Air Communications
Air attack to incident aircraft
Position reporting
Coordination between aircraft

## Slide 26
Radio Communications
Ground Communications
Air to Ground Communications
Air to Air Communications

## Slide 27: Radio Communications
Types of Radios
There are three types of radio communication
VHF-FM use most frequently on incidents.
VHF-AM commonly known as VICTOR radio. It is an AM frequency and can be used to direct aircraft from the ground takeoff and landing coordinator (TOLC) or provide air-to air communications between aircraft. Either of the two, VHF-FM or VHF-AM, can be used for continuous flight following.

## Slide 28: Radio Communications
Types of Radios
There are three types of radio communication
UHF-FM is primarily for logistical helibase and Incident Base Post.
Repeaters are used to link all elements of the operations together.

## Slide 29: Radio Communications
Daily Radio Preparations
Daily routine is to make sure that all assigned
radios are functional:
Checking batteries - replace and change daily (good practice).
Spare batteries with each radio.
Check antenna for damage (replace as needed).

## Slide 30: Radio Communications
Daily Radio Preparations
Daily routine is to make sure that all assigned
radios are functional:
Check key button to make sure it works
Radio check – With personnel or aircraft on deck
Verify frequencies with Incident Action Plan (IAP)

## Slide 31: Radio Communications
Target Description (TD)
TD is a systematic technique for a ground contact to communicate target identification and location by radio, enabling the pilot to locate, identify and take action on the target in the shortest possible time reducing risk for the pilot.

## Slide 32: Radio Communications
Target Description (TD)
The purpose of TD is to have aircraft in the “low and slow” zone the shortest amount of time possible.

## Slide 33: Radio Communications
Target Description (TD)
Ground contact may communicate with:
Air tactical group supervisor (ATGS)
Aerial Supervision Module (ATGS and Lead Plane pilot are in same aircraft)
Fixed wing coordinator
Helicopter coordinator (HLCO)
Helicopter pilot

## Slide 34: Radio Communications
Target Description (TD)
Before talking ground contact needs to know:
Hazards to aircraft
Where you are
Your call sign
Your tactical objective (plan)

## Slide 35: Radio Communications
Target Description (TD)
Before talking ground contact needs to know:
Aircraft call sign
Aircraft frequencies
Primary and secondary targets
Wind speed and direction

## Slide 36: Radio Communications
Target Description (TD)
Where do you get this information?
Helibase
Incident Action/ Operations Plan (IAP)
Division/Group supervisor
Personal observations
Radio traffic
Briefings

## Slide 37: Radio Communications
Target Description (TD)
Operating Procedures - Know the tactical plan.
Reconnaissance
Identify immediate hazards
Buy time
Secure scene

## Slide 38: Radio Communications
Use Target Description (TD)
Parts of the fire
Clock orientation (from the aircraft’s position)
Right, left, nose, tail
High, even, low
Cardinal points (North, South, East, West).

## Slide 39: Clock Orientation Exercise
From the following slides, establish yourself as a reference point using the clock orientation technique and if you are high, even, or low.

## Slide 40
You are here
3 o’clock Low
Describe Your Position (clock orientation)

## Slide 41
Instructor Exercise

## Slide 42: Radio Communications
Target Description (TD)
Operating Procedures – Use identifiable target.
From your position
To topographic or terrain features
To human made features
In reference to suspect Camp or Plot
To cardinal points

## Slide 43: Radio Communications
Target Description (TD)
Operating Procedures – Describe target when pilot is in position to see target.
Be brief, clear and to the point.
Plan your transmission before you key the radio.
Don’t “think out loud” on the radio.

## Slide 44: Stages of Pilot Orientation
Long Distance
Medium Distance
Short Distance

## Slide 45: Long Distance Stage
Geographical and topographical reference points must be large and obvious.
GPS coordinates are useful if air crew has time to enter information.
Relay lat/longs to helibase when ordering aircraft.
Radio contact but no visual contact with aircraft

## Slide 46: Long Distance Stage
Keep positive communication with aircraft until visual contact is established (both ground and pilot)
Radio contact but no visual contact with aircraft

## Slide 47: Medium Distance Stage
Reference points must be obvious
If aircraft is in sight, use the clock orientation technique
Signaling devices are effective (mirrors, strobes, flares)
May or may not have visual contact with aircraft

## Slide 48: Medium Distance Stage
Keep positive radio communication until visual contact is established (both ground and pilot)
Relay aerial hazards to pilot
If appropriate, relay tactical plan to pilot
May or may not have visual contact with aircraft

## Slide 49: Short Distance Stage
Reference point must be unique to your target area
Clock orientation technique is effective
Signaling devices are effective (mirrors, strobes, pannels, flagging)
Have visual contact with aircraft

## Slide 50: Short Distance Stage
Describe target/ tactical plan to pilot
Reemphasize aerial hazards
Have visual contact with aircraft
If the aircraft is getting close and the pilot doesn’t have the target location, communicate any aerial hazards!!!

## Slide 51: Marshalling Helicopters
Safety Precautions to Follow While Marshalling:
Receive a briefing from supervisor
Obtain a radio for communication
Clear the landing area of all obstacles and obstructions before signaling the pilot to take off or land.
Ensure you remain at the front and visual to the pilot at all times.

## Slide 52: Marshalling Helicopters
Safety Precautions to Follow While Marshalling:
Direct pilot the pilot by radio or standard hand signals.
Have an adequate fire extinguisher(s) accessible.
Approved hand signals should be used by all personnel and pilot.
Brace yourself when large helicopters are landing or taking off due to the velocity of the rotor downwash.
Keep landing area free of litter and trash.

## Slide 53: Hand Signals
Use National Standards Use the hand signals in
Basic Aviation Safety, Fireline Handbook or in
the Incident Response Pocket Guide (IRPG).

## Slide 54: Hand Signals
Use National Standards – Standard hand signals should be used.
Include pilot in training so everyone has the same understanding.
Hand signals need to be exaggerated to be effective.
A smooth transition between one signal to the next.
Minimize the time spent holding the helicopter in a hover.

## Slide 55: as a class Practice each HAND signal

## Slide 56: Unit 4 Objectives
Ensure all communication is performed using clear text.
Describe the process of communication within the chain of command.
Demonstrate proper radio usage.
Describe helicopter marshalling procedures and techniques.