## Slide 1: Unit 7 - Operational Safety
Lesson B Briefings and Manifest

## Slide 2: Lesson 7B Objectives
Describe the briefing the Law Enforcement helicopter crewmember should receive from the pilot prior to internal and external cargo operations and passenger transport.
Brief the pilot and passengers of flight plans and potential hazards.
Describe safe helicopter loading and unloading procedures in a wide variety of aviation environments.

## Slide 3: Lesson 7B Objectives
Describe the briefing the Law Enforcement helicopter crewmember would provide to the pilot prior to internal and external cargo operations and passenger transport.
Prepare a passenger/cargo manifest utilizing the helicopter load calculation form.
Describe procedures for in-flight and landing emergencies.
Describe key elements of an After Action Review (AAR).

## Slide 4: Briefings
Pre-flight Briefing
Routine part of every flight.
Pilot and aircraft carded for mission.
Flight plan/following
PPE required for mission

## Slide 5: Briefings
Pre-flight Briefing
Ensure pilot and all involved personnel understand the mission objectives, method and known flight hazards.
  Safety plan and hazard map reviewed
  Review a map of the area where the mission will take place prior to take-off.

## Slide 6: Briefings
Pre-flight Briefing
The map should display:
Intended flight route
Temporary Flight Restrictions
Military Operation Areas
Military Training Routes
Known aerial hazards such as power lines, communication towers.
Failure to attend briefing could lead to assumptions that may compromise safety or completion of mission.

## Slide 7: Briefings
Pilot briefing to passengers
The pilot is required to brief passenger before the flight as a requirement of Federal Aviation Regulation 135.117. The briefing should include:
Smoking restrictions
Use of seatbelts
Emergency exits

## Slide 8: Briefings
Pilot Briefing to Passengers
Operation of doors
Fire extinguisher
Supplemental oxygen, if applicable
Placement of seat backs, if applicable
Location of first aid kit, survival kit and ELT
Shut-off procedures for battery & fuel

## Slide 9: Briefing
LE Crewmember Briefing to Passengers
Many times passengers are thinking more about taking a flight instead of the mission at hand and ensuring their own safety. Providing an effective briefing is the first step towards having a safe flight.

## Slide 10: Briefing
LE Crewmember Briefing to Passengers
It is the responsibility of the person briefing passengers to be familiar with and communicate the specific locations of safety equipment on aircraft to be used.

## Slide 11: Briefing
LE Crewmember Briefing to Passengers
Emergency Locator Transmitter (ELT)
First Aid Kit
Fire Extinguishers
Door Operation
Seatbelt operation
Fuel and Battery Shut-off
Emergency landing positions
Weapon(s) procedures

## Slide 12: Briefing
LE Crewmember Briefing to Officers transporting in custody person
Must notify pilot of suspect transport prior to loading.
Must notify helibase of incoming suspect transport, for additional assistance.
When possible have the pilot shut down the helicopter prior to loading and unloading suspect.

## Slide 13: Briefing
LE Crewmember Briefing to Officers transporting in custody person cont.
Suspect hand-cuffed to the rear.
Suspect not to be seated behind pilot.
Suspect given basic safety briefing to include crash procedures.
Officer will remain in full control of the suspect at all times and is responsible for the safety of the suspect.

## Slide 14: Briefing
LE Crewmember Briefing to Officers transporting in custody person cont.
OPEN DISCUSSION

## Slide 15: Briefing
LE Crewmember Briefing to Passengers
Instructor will demonstrate a passenger briefing.

## Slide 16: Briefing
LE Crewmember Briefing to Passengers
Important Aspects of Passenger Transport
Ensure that all passengers are wearing necessary personal protective equipment for the mission at hand.
Passenger should stay in a safe area until given direction to load.

## Slide 17: Briefing
LE Crewmember Briefing to Passengers
Important Aspects of Passenger Transport (cont’d.)
Ensure that packs are free of items that could come loose in flight.
Ensure weapons and equipment are properly protected and stored.

## Slide 18: Briefing
LE Crewmember Briefing to Passengers
Important Aspects of Loading Passengers and Equipment
Wait for approval from pilot to approach aircraft.
Escort and maintain control of personnel to be transported while approaching aircraft.

## Slide 19: Briefing
LE Crewmember Briefing to Passengers
Important Aspects of Loading Passengers and Equipment (cont’d.)
Make sure passengers are in a crouched position while approaching the aircraft.
Make sure all passengers walk around obstacles, and not over.

## Slide 20: Briefing
LE Crewmember Briefing to Passengers
Important Aspects of Loading Passengers and Equipment (cont’d.)
Have passengers place gear at skid of aircraft, load passengers then cargo.
Assist personnel to assigned seats and help fasten seat belts if needed.

## Slide 21: Briefing
LE Crewmember Briefing to Passengers
Important Aspects of Loading Passengers and Equipment (cont’d.)
Have items removed that could impede egress from the aircraft during an emergency.

## Slide 22: Briefing
LE Crewmember Briefing to Passengers
Important Aspects of Loading Passengers and Equipment (cont’d.)
Have no loose items, including handheld radios.
All other cargo will need to be secured in the cargo compartment, or in cargo baskets.

## Slide 23: Briefing
LE Crewmember Briefing to Passengers
Important Aspects of Loading Passengers and Equipment (cont’d.)
Perform a visual inspection to ensure aircraft and passengers are ready for flight.
Notify pilot that passengers and cargo are ready for flight.

## Slide 24: Briefing
Important Aspects of In-flight Procedures
Keep clear of controls.
Keep control of maps, gear, especially flying with the doors off.
Be aware of emergency exits and crash positions for make and model.
Sit in assigned seating position. No changing seats.

## Slide 25: Briefing
Important Aspects of Unloading
Wait until directed to exit by the pilot or other authorized personnel.
Only authorized personnel should open doors.

## Slide 26: Briefing
Important Aspects of Unloading (cont’d.)
When seat belts are unfastened, check to see they are refastened after passengers have exited.
Make sure that appropriate PPE is in place by all passengers.

## Slide 27: Briefing
Important Aspects of Unloading (cont’d.)
Maintain control of personal gear.
See that passengers exit slowly and in a crouched position.

## Slide 28: Briefing
Important Aspects of Unloading (cont’d.)
Passengers should depart by route specified by authorized personnel to the designated staging area.
See that personnel stay away from the tail and main rotors.
Personnel need to stay out of the departure path when possible.

## Slide 29: Briefings
LE Crewmember to Passenger
Important aspects of in-flight emergencies
Pilot declares an emergency
Notify base of emergency and location
PPE use – Collars up, sleeves down, gloves on, eye protection in use (visor down on flight helmet and/or helmet and chin strap used.

## Slide 30: Briefings
LE Crewmember to Passenger (cont’d.)
Important aspects of in-flight emergencies
All seatbelts snug
Keep hands and feet clear of controls
Secure loose gear
Locate emergency exits
Assume crash position

## Slide 31: Crash Positions
Lap Belt with Shoulder Restraint
When facing forward you should
also tuck your chin to your chest.
Lap Belt Only
Lap belt no longer
utilized by the DOI
and USFS.

## Slide 32: Briefings
LE Crewmember to Passenger (cont’d.)
Important aspects of in-flight emergencies
Wait for all motion to stop before exiting unless, there is a post-crash fire. The safest environment during a crash is in the aircraft.

## Slide 33: Briefings
LE Crewmember to Passenger (cont’d.)
Important aspects of in-flight emergencies
If there is a fire, it is important to get away as soon as practical. Time may be required to help those in need. The fire extinguisher may buy added time to help others.

## Slide 34: Weapon Procedures

## Slide 35: Policy & Regulations
  FAA Advisory Circular 108.2 & 14 CFR 108 -
  Superseded by 49 CFR 1544 – TSA Rules
  49 CFR 1544.201(d) - Prohibitions
  49 CFR 1544.219 - Exemption for LEOs
    Governs carriage and qualifications on commercial flights
    The Office of Law Enforcement/Federal Air Marshal Service maintains training program, FLETC administers training to Federal Officers

## Slide 36: Brief the Pilot on weapon types and safety policy
Long guns - No rounds in chamber, under control of LE
Handguns - may be loaded & shall be holstered
Fully automatic weapons - shall have an empty chamber and the bolt locked in safe position.
All weapons - pointed in a safe direction as determined by the Pilot during the preflight briefing.
Emergency situations – may necessitate carrying weapons with a round chambered. To be determined by LEO, in consultation with pilot.

## Slide 37: Manifest
Manifest requires the following information:
Full name of each person being transported.
Actual weight of each person including personal gear.
Actual weight of any additional equipment.
Destination of personnel
Nature of mission

## Slide 38: Manifest
Manifest will need the following information: (cont’d.)
Ensure total weight on manifest is less than allowable payload for specific aircraft
Submit manifest to helicopter or helibase manager at the end of shift

## Slide 39: Debriefing
Debriefing and After Action Review (AAR)
The debriefing should include:
Post flight evaluation
What was planned?
What actually happened?
Why did it happen?
What can we do next time?

## Slide 40: Briefing
Remember…
The pre-flight briefing sets the stage for a safe mission the debriefing ensures continued success.

## Slide 41: Lesson 7B Objectives
Describe the briefing the Law Enforcement helicopter crewmember should receive from the pilot prior to internal and external cargo operations and passenger transport.
Brief the pilot and passengers of flight plans and potential hazards.
Describe safe helicopter loading and unloading procedures in a wide variety of aviation environments.

## Slide 42: Lesson 7B Objectives
Describe the briefing the Law Enforcement helicopter crewmember would provide to the pilot prior to internal and external cargo operations and passenger transport.
Prepare a passenger/cargo manifest utilizing the helicopter load calculation form.
Describe procedures for in-flight and landing emergencies.
Describe key elements of an After Action Review (AAR).