FIRE BEHAVIOR FORECAST

| INCIDENT: | DRY LAKES COMPLEX & TURNBO | OPERATIONAL PERIOD: | 7/24/03 (day) |
| --- | --- | --- | --- |
| ADMINISTRATIVE UNIT: | GILA NF | FORECAST#: | 36 |
| WEATHER SUMMARY: |
| The Four Corners high will persist through Friday with weak disturbances circulating around the high. These disturbances will kick off isolated to scattered thunderstorms each afternoon and evening. Some storms will be dry. A trough is expected to move through late Saturday, resulting in more storms. A gradual drying trend will begin Monday. Expect high temperatures in the 90s and minimum relative humidities in the mid-teens. Winds will be upslope during the day but variable and gusty near any thunderstorms. Saturday-Monday: Partly cloudy, scattered showers & thunderstorms with relative humidities dropping into the upper teens on Saturday and Sunday, in the 20s on Monday. See attached spot fire weather forecast(s). |
| EXPECTED FIRE ACTIVITY: |
| Short Range: Any precipitation we get along with higher humidities will help slow fire spread; it won’t put it out though. In the absence of rain, fire behavior will pick up when temperatures start to climb & humidities drop. When the relative humidities drop to 15% or lower there is a significant increase in the fire behavior with little wind. Fire spread continues to be from head, backing & flanking fires in pine needles and thicker, more continuous grass and cigarette burning in the larger fuels. Rolling material in conjunction with short uphill runs has also been spreading the fire. Some spotting can occur especially when winds are present. The larger fuels continue to be the carriers of fire where they are more continuous, with flame lengths averaging 4 ft & spread rates <10 chains/hour. Lower flame lengths and higher spread rates will be the norm in fine fuels. Fuels will keep burning out, most notably where heavy fuels are present. Probability of ignition has returned to 90-100% in unshaded fuels and increased 60-70% in shaded fuels. Mid-Range: Fire behavior may begin to increase with predicted relative humidities into the teens and lower. Still no monsoonal moisture in sight for southwestern New Mexico so heavier fuels will continue to burn & smolder. As usual spread rates and flame lengths will depend on specific site conditions. Energy Release Component (ERC) for fuel model G for the Gila Center RAWS is at 88 (as of 7/21/03) starting to drop remember, we still need to drop below 84 to get below the 97th percentile. Record ERC’s continue to be recorded. |
| SPECIFIC FIRE BEHAVIOR: |
| Fire activity was low yesterday over the majority of the Complex Area due to the amount of precipitation that fell and higher humidities the past few days. If any drying & heating occurs the following situations apply. Turnbo has lots of spots smoking up with spread rates less than 1 chains/hour with flame lengths <1 ft. Spread is typically head & backing fire following what dry fuels it can. Some rolling material & short runs up side drainages are still possible. The general spread direction is predominately to the west-northwest with the most activity in White Creek drainage and Shelley Mountain. Moonshine is maintaining it’s spread E/SE to the Middle Fk Gila River & southeast toward Prior Cabin. Most of the rapid spread is in the lighter fuels such as cured grass, needles & leaf litter with the spread slowing when it gets to downed logs & juniper. Granny continues just have low to no activity. The drier conditions, however, may induce more active smoldering and burning. |
| AIR OPERATIONS: |
| Any operations will be affected by thunderstorms and gusty, erratic winds. Visibility should be good but an isolated inversion or two may exist if anything is burning. |
| SAFETY: |
| Continue to watch the weather and how it affects the fuels. What are your fine fuel moistures doing as temperature increases through the day and relative humidity decreases? How is the probability of ignition changing? |

_____________________________________________________	7/23/03	  1730

## Louisa Evers/LTAN							   Date	 	   Time