JUNE 5, 2007

TO ORDER AIRCRAFT CALL

850-523-8600

EXT. 3605 OR 3607

FAX: 850-523-8674

**ALL OTHER CALLS SEE DIRECTORY**

SUNRISE	SUNSET

PENSACOLA	0546	1947	CDT

TALLAHASSEE 	0634	2036	EDT

JACKSONVILLE	0624	2025	EDT

Please ensure distribution to all Fire Pilots/Fire Supervisors

Approved by:	/s/    Bob Butler					AOBD 6/4/07

Approved by:	/s/    Bob Duty					AOBD 6/4/07

Concurrence by:	/s/    John Fort					ASGS 6/4/07

# Quote of the Day

Impossibilities are merely things which 
we have not yet learned.

~ ~

# FLORIDA INTERAGENCY COORDINATION CENTER

### U.S. FOREST SERVICE

### TALLAHASSEE REGIONAL AIRPORT (TLH)

FICC AIR OPERATION PLAN

JUNE 5, 2007

Contents

1.	Aircraft Priorities	  9.	Florida Zone Map

2.	Special Notices	10.	Briefing Checklist

3.	Procedures	11.	Helicopter Daily Use

4.	Airspace Coordination	12.	Helicopter Admin. Costs

5.	Air Tanker Jettison Areas	13.	FICC Air Ops Demob

6.	Dispatch Request	14.	Directory

7.	DOF Communications Plan	15.	Aircraft Assignment

8.	Aviation Communications Plan

1. AIRCRAFT PRIORITIES

### Please notify all appropriate Aircraft Personnel that they must use these priorities:

### 1.	Threat to life imminent

### 2.	Public and Firefighter Safety

### 3.	Occupied structures involved (fire in structure or in neighborhood)

### 4.	Verified evacuated structures involved

### 5.	Wildland initial attack

### 6.	Other extended attack fires

2. SPECIAL NOTICES

### 122.925 is the Primary Air to Air Frequency

### General Messages

It is imperative that all pilots of aircraft who travel on point-to-point missions (point-to-point defined as: Aircraft being assigned to or released by FICC) flight follow with the FAA, complete an Aircraft Flight Request/Schedule Form. The accurately completed form needs to be faxed to FICC Air Operations at 850-523-8674, with a follow up phone call to ensure delivery. This process will assist in maintaining a proper level of safety and documentation for all parties involved. Your assistance in this procedure is appreciated.

Attention All Fire Fighting Aircraft When not utilizing ATC Service, please SQUAWK 1255; if using ATC Service, follow ATC instruction and SQUAWK codes issued by ATC. . . . Thank you.

### Notice to Aviation Personnel

### Ocala National Forest Airspace

The Communications Plan includes a flight following frequency for the Ocala National Forest: 169.175. Aircraft entering Ocala National Forest Air Space contact the Ocala Fire Center on this frequency. Dispatchers contact Ocala Fire Center at 352-759-2081 when dispatching aircraft to or across Ocala National Forest Air Space.

### Okefenokee NWR Airspace

Located North of Osceola N.F. Communications Plan includes the flight following  frequency 123.075 for the Okefenokee NWR. Dispatchers contact Okefenokee Dispatch at 912-496-7366,

ext. 230, when dispatching aircraft across or near Okefenokee NWR Air Space.

Detection flights will be at routine altitudes and under normal operational procedures outside of TFR’s

Generally Dispatchers, ASGS, ATGS, HEB, ATBM, HEMG and HECM will report to Tallahassee for briefing and then travel to their final assignment location. Other overhead will report directly to assignment for briefing there.

The Ops Plan now has a briefing checklist attached, to be used by base managers, ASGS or other appropriate unit leaders. Please review the checklist and order materials needed to distribute to incoming personnel (item#5 on checklist).

FICC AVIATION CONFERENCE CALL

The FICC aviation call will be held daily at 0930 hrs on the SACC conference call number until further notice. Please be prepared to discuss:

SACC weather and intel updates	Aircraft and overhead needs/concerns

Tanker base and helibase issues	Team AOBD aviation updates

Aviation safety issues 	Other issues and concerns

SAFECOMS

Please fax SAFECOM to FICC Air Ops 850-523-8674. We will then fax to SACC and attach to the daily Aviation Action Plan.

### Air Ops Overhead Ordering/Demobing

### Aircraft Release and Demob

FICC Air Support will notify bases and aircraft personnel of planned release via phone conversation.

FICC will notify SACC, who will notify NIFC of planned release and will respond with any reassignment.

FICC will notify base and aircraft personnel of release or reassignment. Aircraft managers will complete contract formalities.

All demobed aircraft will complete a formal written flight plan to be filed with FICC, with continuing notification to SACC.

ALL Air Ops overhead orders should be sent to FICC Air Support. You can either Fax a resource order or general message as long as all the information (ie: Incident/Project Number, P-Code, reporting destination, date needed, etc.) is included.

If you have personnel to demob, please fax the demob form to FICC Air Support (especially your fax number) at least two (2) days prior to the travel day. Again, please insure all information is included. FAX 850-523-8674, ATTN: ASGS)

Finally, we’d appreciate your requests to be as legible as possible so the fax will be clear and cut down on follow-up phone calls.

Any questions, give FICC Air Support a call at 850-523-8600, ext 3601.

3. PROCEDURES

**The FICC Air Support briefing will be held each day at 0800. An internal debriefing will be held each day at 1930.

### Introduction

The Florida Fire Situation is complex involving essentially the entire state and South Georgia, multiple incidents and numerous aircraft. The following procedures are established to provide additional safety margins flight following, operations and tactical missions.

1.	All tactical aircraft assigned to the National Forests of Florida will be dispatched by the respective Forests.

2.	If Incident teams that have aircraft resources of their own, and need aircraft from outside their areas of operations, requests will be made through FICC Air Ops.

3.	High level flight following (for example, air tankers and ATGS enroute to an incident) will be with FAA. All aircraft entering incident airspace will flight follow with that incident

4.	Point-to-point aircraft arriving at their destination should contact their dispatch origin via landline and notify them of arrival. For aircraft arriving for tactical missions, the receiving unit should report arrival of the aircraft to the sending unit.

4. AIRSPACE COORDINATION

A. DOD Airspace Coordination Procedures

Heads Up!

DOD Aviation Activity – this means that the restricted areas, MOAs, etc., could be hot.

To gain clearance in Military designated Airspace over the Ocala National Forest:

Fire suppression activities within the restricted area R-2910 in Ocala National Forest, refer to Guidelines for Fire Suppression on the Pinecastle Bombing Range. Contact Ocala Dispatch or FICC Air Ops to receive the information.

Restricted Areas:	2906, 2907 A and B, 2910

All aircraft will contact JAX Sea Lord on frequency 134.65 for clearance.

Clearance is mission-specific.

Comm. Phone is 904-542-2250 for assistance.

Source Agreement is the Letter of Agreement between the Ocala, USFS, Florida Game and Freshwater Fish Commission, and the Fleet Area Control and Surveillance Facility Jacksonville also known as “Sea Lord”.

Other DOD Airspace not involved in above agreement – follow FAA procedures for entry:

Tyndall C, D, E, F, G	Tyndall RAPCON (Tyndall Approach)	850-283-4900

Palatka 1, 2	ZJX TRACON	904-741-0767

Moody 1, 2, North, South	ZJX Cntr	904-549-1542

Mayport Low	Jacksonville TRACON	904-741-0766

R-2904A, 2903 A, C, D	JAX TRACON	904-741-0767

Camp Blanding	Range Control	904-533-2268

Eglin Scheduling – Eglin MOA’s		850-882-5800

Eglin Mission Control R-2914A, R-2915A, R-2917	850-882-9153

Call FICC – AIR SPACE COORDINATOR, at 850-523-8600 Ext 3615 for further information

e-mail - airspacecoordination@hotmail.com

B. Federal Aviation Regulations (FAR) for Temporary Flight Restrictions (TFR’s)
Here is the FAR you are operating under

TFR’s under FAR 91.137 (a) 2 are designed to provide a safe environment for the operation of disaster relief aircraft. (c) When a NOTAM has been issued under paragraph (a) (2) of this section, no person may operate an aircraft within the designated area unless at least one of the following conditions is met:

1.	The aircraft is participating in hazard relief activities and is being operated under the direction of the official in charge of on scene emergency response activities.

2.	The aircraft is carrying law enforcement officials.

3.	The aircraft is operating under the ATC approved IFR flight plan.

4.	The operation is conducted directly to or from an airport within the area, or is necessitated by the impracticability of VFR flight above or around the area due to weather, or terrain; notification is given to the Flight Service Station (FSS) or ATC facility specified in the NOTAM to receive advisories concerning disaster relief aircraft operations; and the operation does not hamper or endanger relief activities and is not conducted for the purpose of observing the disaster.

5.	The aircraft is carrying properly accredited news representatives, and prior to entering the area, a flight plan is filed with the appropriate FAA or ATC facility specified in the Notice to Airmen and the operation is conducted above the altitude used by the disaster relief aircraft, unless otherwise authorized by the official in charge of on scene emergency response activities.

C.  Temporary Flight Restriction (TFR)

### Procedure for Wildfires

- Determine the need for a TFR. Be prepared with the following:

VOR/DME or LAT/LONG of Center Point

Size request (IE: 5NM Radius or LAT/LONG coordinates for corners of polygon to determine dimension.)

Altitude in MSL for ceiling of Restrictions

- Call request for TFR to FICC Air Operations at 850-523-8600, Ext. 3615 or FAX request using the TFR request form on page 7.

- Points to consider: Airport and towers, impacts on local operators, banner towing, flight schools, flying clubs, sky diving schools, traffic patterns approach and departure, size and shape of TFR.

- NON-circular TFRs are allowed with a LAT/LONG description. All descriptions will use degrees, minutes, seconds format.

- Immediate notification of intrusions is to be placed with FICC Air Space Coordinator:

File a SAFECOM through appropriate channels.

- TFR’s are posted on the DOF Web Site, and you may also view them at https://www.notams.jcs.mil  or https://www.notams.faa.gov .

The TFR is a tool to provide what you need for safety. Be sure to ask for the airspace you need. This resource needs to be managed and released when not necessary. For further information, please call FICC Air Operations at 850-523-8600, Ext. 3615.

### Current TFRS

NOTAM #	FIRE NAME	ALT	RADIUS	LAT/LONG	FREQUENCY

7/1820	The Big Turn	3000 MSL	310900N/0823850W	310900N/0820227W	122.575

Around Complex		303100N/0820227W	304000N/0823850W

NOTE:  Per agreement with FAA, approach traffic to Jacksonville International & Cecil Field

crossing the SE portion of TFR (7/1779) will be at 3000 MSL.

TFR Cancelled 6/3 1830		261540N/0812500W	254930N/0811000W

7/2182	BICY Complex	3000 MSL	261540N/0805230W	260100N/0811600W	123.4

255330N/0805230W	260100N/0812500W

7/1779	Florida Bugaboo	3000 MSL	304000N/0823850W	303100N/0820227W	123.4

301500N/0820227W	301500N/0824500W

304000N/0824500W

Call FICC Air Operations at 850-523-8600, Ext. 3615 for modifications or cancellations.

e-mail -   airspacecoordination@hotmail.com

INTERAGENCY REQUEST FOR TEMPORARY FLIGHT RESTRICTION

(TFR  request  must be phoned in as per FAA.  This form may also be FAXed to provide  documentation.)

| RESOURCE ORDER NUMBER: Request #: A - | DATE: TIME: |
| --- | --- |
| TO: FAA ARTCC ________________________________ FAA PERSON CONTACTED: _____________________________ FAA PHONE:____________________ FAX:_________________ | FROM: DISPATCH OFFICE ________________ PERSON REQUESTING TFR: __________________ 24 HR. PHONE (No Toll Free #s) ___________________ |

(Check if this TFR is a replacement.  If so, NOTAM # of TFR being replaced. _________________________

(Existing TFRs can not be changed, only cancelled and replaced.)

Geographic Location of Incident (nearest town, state) ______________________________________________

| Location (Circular TFR) List nearest NAVAID (distance should be less than 50 NM) - do not use NDB or T-VOR. |
| --- |
| VOR ID | RADIAL (Degrees) | DISTANCE (NM) | LAT/LONG of Center Point (use US NOTAM OFFICE FORMAT ddmmssN/dddmmssW) | RADIUS (NM) (5 NM is standard) |
|  |  |  | N/ W |  |

OR (Polygon TFRs should be rare and only used if circular shape is not adequate.)

| Location (Polygon TFR) (List perimeter points in clockwise order) List nearest NAVAID (distance < 50 NM) - do not use NDB or T-VOR. |
| --- |
| Point # | VOR ID (XXX) | Radial (Degrees) | Distance (NM) | Lat/Long ddmmssN/dddmmssW | Point # | VOR ID (XXX) | Radial (Degrees) | Distance (NM) | Lat/Long ddmmssN/dddmmssW |
| 1 |  |  |  | N/ W | 5 |  |  |  | N/ W |
| 2 |  |  |  | N/ W | 6 |  |  |  | N/ W |
| 3 |  |  |  | N/ W | 7 |  |  |  | N/ W |
| 4 |  |  |  | N/ W | 8 |  |  |  | N/ W |

Altitude restrictions:   ____________  FEET MSL (do not use AGL – Standard is 2000’ above highest terrain point)

The _______________________/___________________ at _____________________ , ___________________

Agency Name                                 Incident Name                           24 Hr. Phone # (No Toll Free #s)               VHF-AM Air/Air Frequency

is in charge of on scene emergency response activities.  TFR to provide a safe environment for fire fighting aircraft operations; effective immediately, until further notice, 24 hrs/day.

| The requested TFR affects the following Special-Use Airspace: |
| --- |
| The requested TFR affects the Military Training Routes listed below: |
| Route | SCHEDULING ACTIVITY | SEGMENT(S) | Route | SCHEDULING ACTIVITY | SEGMENT(S) |

IMPORTANT NOTE TO FAA:  If the TFR affects SUA and/or MTR(s), we request NOTAM distribution to all military bases involved, to the Coordinating Flight Service Station, and, for MTRs, to the Flight Service Station and Air Route Traffic Control Center with responsibility for the airspace at the route entry point(s).

NOTAM # ________________________ ISSUED AT ____________ (Time) On _______/_______ (Date)

Date/Time TFR Cancelled: 				   By:

Rev.09-07-02

5. AIR TANKER JETTISON AREAS

### Osceola National Forest

Range Strip/Pipe Line		Lat.		N 30o 16, 0

Long.		W82o 28.29

### Ocala National Forest

Bombing Range			Lat.		N29o 06.53

Long.		W 81o 42.57

This area is an active bombing range and should not be considered during an emergency due to short time available to obtain necessary clearances. This area could be used for proficiency drops if the Ocala Airport is unavailable.

This Section Intentionally Left Blank

6. DISPATCH REQUESTS

***DO NOT ABBREVIATE ON THIS FORM***

AIRCRAFT DISPATCH REQUEST

*items must be completed for initial dispatch  ** PLEASE REVIEW COMMUNICATION PLANS **

DATE 					TIME

INCIDENT/PROJECT ORDER # 					  P CODE:

CALL BACK# 							  FAX #

FIELD UNIT 	(DO NOT ABBREVIATE)	REQUESTED BY

FIRE NAME

*LOCATION (NEAREST TOWN, DISTANCE AND DIRECTION)

*LAT/LONG: NORTH  					*WEST

*AIR CONTACT  					*AIR TO AIR FREQ.

FIXED WING	 HELICOPTER	  AIR TACTICAL 	 DETECTION

*OTHER AIRCRAFT IN AREA

*GROUND CONTACT

*AIR TO GROUND FREQ. (NOT CHANNEL) 					WIDEBAND	NARROWBAND

FLIGHT FOLLOWING UNIT/FREQUENCY					WIDEBAND	NARROWBAND

FIRE SIZE 				  NUMBER OF SETS OR FIRES

*KNOWN HAZARDS

AIRCRAFT REQUESTED

OTHER INFORMATION

LIFE OR STRUCTURES IMMINENTLY THREATENED?

EVACUATIONS?

FAX TO:  850-523-8674

“CALL TO CONFIRM FICC HAS RECEIVED DOCUMENT”

AT 850-523-8600 Ext. 3605 or 3607

7. DOF COMMUNICATION PLAN

Florida Division of Forestry

Radio Frequency Plan

| Channel | RX | TX | N / W Band | Field Unit Number | Dispatch Center or Function |
| --- | --- | --- | --- | --- | --- |
| 1 | 159.315 | 159.315 | W |  | Mobile to Mobile |
| 2 | 159.225 | 159.225 | W | 4, 11 | Tallahassee and Withlacoochee |
| 3 | 159.240 | 159.240 | W | 15, 7 | Jacksonville, Myakka River and Forestry Youth Academy |
| 4 | 159.270 | 159.270 | W | 1, 5, 12 | Perry, Orlando and Blackwater |
| 5 | 159.330 | 159.330 | W | 6, 14 | Suwannee and Lakeland |
| 6 | 159.390 | 159.390 | W | 8, 18 | Gainesville (South), Usher and Everglades |
| 7 | 159.405 | 159.405 | W | 8, 2, 16 | Chipola River, Gainesville (North), and Okeechobee |
| 8 | 159.450 | 159.450 | W | 10, 17 | Bunnell and Caloosahatchee |
| 9 | 151.235 | 151.235 | W |  | Tactical |
| 10 | 151.295 | 151.295 | W |  | Tactical |
| 11 | 159.285 | 159.285 | W |  | Southeastern Compact |
| 12 | 151.235 | 159.285 | W |  | Alpha Repeater |
| 13 | 151.295 | 159.300 | W |  | Bravo Repeater |
| 14 | 169.175 | 169.175 | W |  | USFS Dispatch * |
| 15 | 169.900 | 169.900 | W |  | USFS Fire |
| 16 | 154.265 | 154.265 | W |  | Fire Mutual Aid (Red Channel) |
| 17 | 154.280 | 154.280 | W |  | Fire Mutual Aid (White Channel) |
| 18 | 154.295 | 154.295 | W |  | Fire Mutual Aid (Blue Channel) |
| 19 | 159.300 | 159.300 | W |  | Base to Base, Aircraft |
| 20 | 168.675 | 168.675 | W |  | Air Ops, Statewide ** |
| 21 | 170.475 | 170.475 | W |  | Air Ops, Statewide ** |
| 22 | 171.425 | 171.425 | W |  | Air Ops, Statewide – less North Florida ** |
| 23 | 171.575 | 171.575 | W |  | Air Ops, Statewide ** |
| 24 | 172.275 | 172.275 | W |  | Air Ops, Statewide – less North Florida ** |

* Guard Tone Frequencies: (Transmit Only)

Apalachicola National Forest			136.5HZ

Ocala National Forest			123.0Hz

Osceola National Forest

Olustee Tower (South)			167.9Hz

Eddy Tower (North)			146.2Hz

**For Use Only As Directed in the Florida Interagency Aviation Communications Plan.

8. INITIAL ATTACK AVIATION COMMUNICATIONS PLAN

| RX | TX | Tone | N/W Band | FUNCTION | ASSIGNMENT | REMARKS |
| --- | --- | --- | --- | --- | --- | --- |
| 122.925 |  |  |  | AIR to AIR (Primary) | STATEWIDE - Florida |  |
| 122.425 |  |  |  | AIR to AIR (Sec) | STATEWIDE - Florida |  |
| 122.225 |  |  |  | AIR to AIR (Third) | STATEWIDE - Florida | Temporary Assignment |
| 123.075 |  |  |  | Air to Air/Flight Following | SE Georgia | Okefenokee NWR |
| 159.390 |  |  | W | Air to Ground | Georgia statewide | Okefenokee NWR |
| 122.850 |  |  |  | Backup IA A/A | Ocala NF Only | Exclusive Use Only |
| 118.775 |  |  |  | Primary Air to Air | Within 50 nautical mi. of Ft. Myers | See Map |
| 135.800 |  |  |  | Primary Air to Air | Within 70 nautical miles Florida City | See Map |
| 123.975 | DO | NOT | USE | Tanker Base Contact | All Tanker Bases Conflict w/Sandford Airport (SFB) | 40 Nautical Miles Radial, All Tanker Bases |
| 123.025 |  |  |  |  | Media Ships |  |
| 134.650 |  |  |  | SEALORD Contact | MOA’s 2906, 2907 A& B, 2910 (Ocala National Forest) | Contact Central Dispatch For Instructions |
| 126.150 |  |  |  | Avon Park Range Control | Avon Park MOA’s R-2901 A-I |  |
| 159.300 |  |  | W | Flight Following | STATEWIDE FIRES |  |
| 168.650 |  |  | N | National Flight Following (Backup) | National Forests in Florida | National Flight Following is monitored by National Forest Offices only |
| 168.625 |  | 110.9 | N | Air Guard | Safety/Redirect |  |
| 169.175 |  | 131.8 | N | Contact Frequency IA Air to Air IA Air to Ground | Central Dispatch (Ocala NF) | Check in with Central Dispatch when within Ocala NF airspace |
| 168.675 |  |  | See Remarks | Tactical Air to Ground | Zones 1 and 2 | See Map State – Wide; Fed – Narrow |
| 171.575 |  |  | See Remarks | Tactical Air to Ground | Zone 3 | See Map State – Wide; Fed – Narrow |
| 171.425 |  |  | See Remarks | Tactical Air to Ground | Zone 4 | See Map State – Wide; Fed – Narrow |
| 172.275 |  |  | See Remarks | Tactical Air to Ground | Zone 5 | See Map State – Wide; Fed – Narrow |
| 170.475 |  |  | See Remarks | Tactical Air to Ground | Zone 6 | See Map State – Wide; Fed – Narrow |
| 170.500 | 164.125 | 167.9 | N | Forest Repeater | Tallahassee Dispatch | Apalachicola NF |
| 164.825 | 164.125 | 123.0 | N | Forest Repeater | Central Dispatch | Ocala NF |
| 171.550 | 171.550 |  | N | Forest Net | Osceola Dispatch | Osceola NF |
| 171.550 | 172.375 | 146.2 | N | Forest Repeater | Osceola Dispatch | Osceola NF (North End) |
| 171.550 | 171.550 |  | N | Forest Net | Osceola Dispatch | Osceola NF |
| 171.550 | 172.375 | 167.9 | N | Forest Repeater | Osceola Dispatch | Osceola NF (South End) |
| 168.200 |  |  | N | Direct | Florida Panther NWR | Lat. 26( 10’ 05” Long. 81( 21’ 01” |
| 164.625 | 163.150 | TX/RX 118.8 | N | Florida Panther NWR | Florida Panther NWR | Lat. 26( 10’ 05” Long. 81( 21’ 01” |

Assigned Air Frequencies

The Latitude and Longitude information listed is only a general reference for fire location, it is not

intended for navigational use.

GACC	SACC

Incident	BICY [All BICY Aviation frequencies will be cancelled 6/4/07 1800]

Use	Frequency	Remarks	Latitude / Longitude

A/A	123.4000	A-13	26 12 17N, 80 59 59W

A/G	167.9500	A-12	26 12 17N, 80 59 59W

A/G	169.2000	A-17	26 12 17N, 80 59 59W

A/G	171.1375	A-15	26 12 17N, 80 59 59W

Incident	Big Turnaround

Use	Frequency	Remarks	Latitude / Longitude

A/A	122.5750	A-3 TFR	31 04 44N, 82 18 41W

A/A	123.1250	A-109	31 04 44N, 82 18 41W

A/G	167.9500	A-4	31 04 44N, 82 18 41W

A/G	170.0000	A-96	31 04 44N, 82 18 41W

Incident	Florida Bugaboo

Use	Frequency	Remarks	Latitude / Longitude

A/A	123.4000	A-4 TFR	30 32 40N, 82 20 32W

A/A	136.2500	A-29	30 32 40N, 82 20 32W

A/G	166.6750	A-12	30 32 40N, 82 20 32W

Incident	Lake City Tanker Base

Use	Frequency	Remarks	Latitude / Longitude

A/A	123.9750	Ramp	30 10 02N, 82 34 01W

Incident	Ocala Tanker Base

Use	Frequency	Remarks	Latitude / Longitude

A/A	125.6500	FAA Temp Tower Freq	29 10 36N, 82 13 45W

A/A	125.0250	FAA Temp Tower-Grd Control	29 10 36N, 82 13 45W

A/A	136.0000	Ramp	29 10 36N, 82 13 45W

Incident	Punta Gorda Tanker Base

Use	Frequency	Remarks	Latitude / Longitude

A/A	136.0000	Ramp	26 55 06N, 81 59 24W

Incident	Sweat Farm

Use	Frequency	Remarks	Latitude / Longitude

A/A	122.5750	A-3	31 09 05N, 82 26 19W

A/A	167.9500	A-4	31 09 05N, 82 26 19W

A/A	125.2250	A-96	31 09 05N, 82 26 19W

9. FLORIDA DOF DISPATCH ZONE MAP

10. BRIEFING CHECKLIST

# Aviation Personnel Briefing Checklist

- Where to report/To whom

- Copy of Daily OPS Plan (most briefing information is in Daily OPS Plan-REVIEW-  	THOROUGHLY).

2a.	Flight Following Procedures

2b.	Dispatch Procedures

2c.	Air Space Coordination Procedures (special air space restrictions)

2d.	Organization Chart

2e.	SAFECOM Procedures

2f.	Reporting of Out-of-Service Aircraft

2g.	Aircraft Priorities

2h.	Current Intel Update

2i.	Radio Frequency Banding

3.	Safety

3a.	General Safety Issues

3b.	Florida Weather, Fuels, & Fire Behavior

3c.	Review local crash rescue plan; overdue aircraft procedures

4.	Administrative Procedures

4a.	Personnel Logistics (food, housing, transportation)

4b.	Extension 14 to 21 Day Letter and Process

4c.	Demob Forms

4d.	Conference Call Schedule

4e.	Daily Reporting Requirements (Nightly-Gallons, Daily-Costs)

4f.	Human Resource Considerations

5.	Materials to Distribute to Incoming Personnel

5a.	Communications Plan

5b.	Sectional of assigned area

5c.	WAC Chart

5d.	2007 Airport Directory

5e.	Florida State Aeronautical Chart

5f.	Florida Road Map

5g.	DOF District Map

5h.	Current Air Operations Plan

6.	Other Local Issues/Logistics/Information

11. HELICOPTER DAILY USE

# Helicopter Daily Use and Cost Summary

(Submit to Helibase Manager At End Of Each Day’s Operations)

Helibase:  						Date:  				Helicopter N #:

Make/Model:  					Manager’s Name:

Type:  	     1  	    2  	      3  	        CWN  	     CONTRACT          OTHER (SPECIFY)

FLIGHT INVOICE REFERENCE NUMBER (S):

| FLIGHT TIME (HRS) X HOURLY RATE | TOTAL FT COST = $ |
| --- | --- |
| DAILY AVAILABILITY X DAILY RATE | TOTAL AV COST = $ |
| EXTENDED PILOT STANDBY X HOURLY RATE | TOTAL EP COST = $ |
| EXT. DRIVER STANDBY X HOURLY RATE | TOTAL ED COST = $ |
| EXT. MECHANIC STANDBY X HOURLY RATE | TOTAL EM COST = $ |
| # OF CREW MEMBERS X RON (FS) RATE/DAY | TOTAL FS COST = $ |
| SERVICE TRUCK MILES X RATE/MILE | TOTAL SM COST = $ |
| GALLONS FOAM X COST GALLON CONCENTRATE USED | TOTAL FOAM COST = $ |
| GALLONS RETARDANT X COST GALLON | TOTAL RETARDANT COST = $ |
| SPECIAL EQUIPMENT (Radio, FLIR, Longline/Remote Hook, Agency Supplied Fuel, Etc.) | TOTAL MISCELLANEOUS = $ |
|  | TODAY’S TOTAL COST = $ |

P_Fire 	 Other Costs 	 Flight Time 	P-Code Cost Total

P_Fire 	 Other Costs 	 Flight Time 	P-Code Cost Total

P_Fire 	 Other Costs 	 Flight Time 	P-Code Cost Total

P_Fire 	 Other Costs 	 Flight Time 	P-Code Cost Total

P_Fire 	 Other Costs 	 Flight Time 	P-Code Cost Total

Miscellaneous Costs Examples:  Personnel, Per Diem, Rental Vehicles, Base Transportation, Office Trailer, Crew Trailer, Telephone Lines, Cell phones,  Water Connection, Electrical Service, Airport User Fees, Office Supplies, Radio Kit Shipping etc.

USE:

| TOTAL PASSENGERS TRANSPORTED | TOTAL LBS. CARGO DELIVERED | TOTAL GALLONS WATER | TOTAL GALLONS RETARDANT | TOTAL GALLONS FOAM |
| --- | --- | --- | --- | --- |

COMMENTS:

* Do not calculate for exclusive use contracts where availability is paid from presuppression funds.

HCM-17

12. HELICOPTER ADMINISTRATIVE COSTS

# Helicopter Administrative Costs

HELICOPTERS/TAIL #		DATE

HELIBASE	   ACCOUNTING CODE:

(NOT ASSIGNED TO HELIBASE)	PREPARED BY:

ITEM	NUMBER	COST/UNIT/DAY	DAILY TOTAL

| 1. Personnel |  | $ 300/Day |  |
| --- | --- | --- | --- |
| 2. Per Diem (Meals & Lodging) |  | $ 126/Day |  |
| 3. Rental Vehicles |  | $ 35/Day |  |
| 4. Rental Space |  | $ /Day |  |
| 5. Rental Equipment |  | $ /Day |  |
| 6. Telephones, Fax Computer Lines |  | $ 17/Day |  |
| 7. Cell Phones |  | $ 10/Day |  |
| 8. Electrical Service |  | $ 7/Day |  |
| 9. Supplies |  | $ /Day |  |
| 10. Other |  | $ /Day |  |
| 11. One Time Cost |  | $ /Day |  |
| 12. Transportation Cost |  | $ 750/Day |  |
|  |  | Cumulative Cost |  |

1.	Determine number of agency/casual personnel assigned and multiply by average unit cost show

2. 	Multiply number of agency personnel by avg. cost shown

3.  	Determine number of rental cars and multiply by cost shown

4.  	Determine actual monthly cost of rental space, office trailers, crew trailers, etc.; divide by 30 and enter daily cost

5.  	Determine actual monthly cost of rental equipment (pumps, etc.); divide by 30 and enter daily cost

6.  	Use daily cost shown on form unless actual daily cost is available

7.  	Use actual cost of daily supplies

8.  	Other daily costs

9.  	Other Time Costs- enter items not paid on a periodic basis, e.g. radio shipping costs

10.	Transportation Costs are added upon the arrival of new personnel who are not on an aircraft order

* Use separate form if more than one accounting code is involved

13. FICC AIR OPS DEMOB

# INCIDENT DEMOB REQUEST

MUST BE COMPLETED IN FULL!

Florida Interagency Coordination Center

3250 Capital Circle SW

Tallahassee, FL 32310

| INCIDENT NAME: |  |
| --- | --- |
| INCIDENT NUMBER: |  |
| TRAVELER’S NAME: |  |
|  | (Name on Driver License) |
| REQUEST NUMBER: |  |
| DATE/TIME OF RELEASE: |  |
| TRAVEL DATE/TIME: |  |
|  | (Day that Travel will Begin) |
| DEPARTURE AIRPORT: |  | / |  |
|  | (Jetport ID) |  | (City/State) |
| RETURN AIRPORT: |  | / |  |
|  | (Jetport ID) |  | (City/State) |
| GROUND TRAVEL INFO: |  |
|  | (Type of Vehicle/ETA Home) |
| PAYMENT CODE: |  |
|  | (P or F Code) |
| FAX NUMBER: |  |
|  | (To Send Completed Itinerary) |
| SPECIAL INSTRUCTIONS: |  |
| Available for Reassignment? | Yes | No |
| SIGNATURE OF DEMOB UNIT LEADER: |  |

### CALL FICC FOR ADDITIONAL INFO (850) 523-8600 EXT. 0

(FICC FAX – 850-523-8674)

(850-523-8600 EXT 3601 or 3607 to verify receipt)

FICC Air Operations

Extension Request

| FILE CODE: | 5100 |  |  |
| --- | --- | --- | --- |
| DATE: |  |  |  |
| TO: |  | Location: |  |
| FROM: |  | Location: |  |
| SUBJECT: | Tour of Duty Extension |
| Please check the appropriate item: I wish to extend my tour to 21 days . I wish to take two days off and return to duty for 14 additional days . |
| Individual Name: |  | Agency ID: |  |
|  |  |  | (i.e. VA-VAS) |
| Incident Position Assignment / Location: |  |
| Current Resource Order: |  | Request No.: |  |
| 14th Day on Assignment (date): |  |  |
| Reasons for Extension: |
| 1) | It is currently very difficult to fill orders for all aviation positions. |
| 2) | Aviation resources are a key element in Florida wildfire suppression operations. |
| 3) | The number of aviation resources now in Florida is much greater than normal. |
| 4) | There is a no short-term outlook for any improvement in wildfire potential. |
| 5) | Most new wildfire starts in the state have the potential to quickly become an immediate threat to homes and other property. |
| Note: | Wildfire suppression personnel here are housed in motels and either eat in restaurants or are provided regular meals. |
| Home Unit Approval: |
| Home Unit Administrator |  |  |
| USFS – Florida Approval: |
| James Hart |  |  |
| Fire Staff Officer |  |  |

14. FICC AIR OPERATIONS DIRECTORY

Florida Interagency Coordination Center, Air Ops

AOBD, Office Number	850-523-8600 Ext. 3617

Bob Butler, AOBD	Cell 850-524-9963

AOBD, Office Number	850-523-8600 Ext. 3609

Robert Duty, AOBD, DOF	Cell 850-228-7765

Office Number	850-523-8600 Ext. 3611

Forrest Sumner, Dist Ranger	229-726-0285

ASGS, Office Number	850-523-8600 Ext. 3601

John Fort, ASGS	Cell 850-524-9964

Office Number	850-523-8600 Ext. 3601

Dick Dudley, ASGS	Cell 850-524-9958

Janet Muncy, RESL	850-523-8600 Ext. 3601

Cell 434-996-2077

Scott Plue, ASGS	Cell 850-570-5484

COMC, Office Number	850-523-8600 Ext. 3613

Mike Tuominen, COMC	Cell 208-863-4141

Don Schnee, COMC(T)	Cell 208-866-2874

Airspace Coord, Jim Unrue	Cell 850-570-5497

Office	850-523-8600 Ext. 3615

Rawles Williams, EDSP (Aircraft)	850-523-8600 Ext. 8609

Cell 850-570-5498

Shauna McIntosh-Harris, EDSP(T)	850-523-8600 Ext. 8609

Kathy Krusow, IADP (Aircraft)	850-523-8600 Ext. 3607

Carol Robinson, EDSD (Aircraft)	850-523-8600 Ext. 3605

Robin Brooks, IADP (Aircraft)	850-523-8600 Ext. 3603

Kim Brookshire, ACDP (Aircraft)	850-523-8600 Ext. 3603

Ann Etheridge, COST	850-576-8148

Aircraft Costs/Time (federal)	Cell 850-524-9967

Shannon Williams, Costs (state)	850-523-8600 Ext. 3611

FAX, Aircraft Dispatch (incoming only)	850-523-8674

Florida Interagency Coordination Center.	850-523-8600

Center Coordinator, Eva Moore	850-523-8602

Administration, Thelma Jackson	850-523-8604

Forest Dispatcher, Pam Brown	850-523-8605

FAX	850-523-8621

Punta Gorda Tanker Base	941-575-0907

(second line)	941-575-0434

FAX	941-575-0974

Bob Shoemaker, ATBM	Cell 208-358-5519

John Beck, ASM	940-389-0421

Region 8 Aviation

FAX, Aviation	770-458-6308

Eddy Holt, Air Tankers, Retardant	423-476-9761

FAX	423-476-9792

Dave Broadnax, RAO	Cell 404-909-1739

Jack Finley, IHOS	404-909-0248

770-330-6075

Rick Gicla, ASM Pilot	770-335-9595

Carol Brown, Retardant Orders	Cell 601-591-5076

After Hours	601-942-9932

Welch Fair, Retardant Orders	404-347-1761

Donna Shope, Maint.Inspection	404-386-4849

Larry Roberts, Heli. Pilot Inspector	404-909-0245

Aviation Management Directorate	770-458-7474

Director, Stew Walker	Cell 770-298-6217

Meg Gallagher, Training & Airspace	770-458-7474

Cell 770-598-2359

Shari Phillips, Aviation Resources	770-598-3021

FAX	770-458-6677

Southern Area Coordination Center…….	 678-320-3000

Aircraft – FAX	678-320-3036

Aircraft Coordinator, Darrell Barlow	678-320-3005

Aircraft Dispatcher, Marlin Whetten	678-320-3012

Aircraft Dispatcher, John Caldwell	678-320-3029

Coordinator, Kelly Jerzykowski	678-320-3001

Meteorologist, Kevin Sczany	678-320-3008

SACC Conference Call	1-877-710-5722

Password	476230#

Lake City Tanker Base	386-758-9078

Robbie Staten, ATBM	386-961-8941

Cell 850-524-9968

Base – FAX	386-752-8901

FIRE ONLY, Lake City	386-758-9078

Lake City FBO FAX (Bailey Aviation)	386-752-5584

Ocala Tanker Base	352-291-1035

(second line)	352-291-1071

FAX	352-291-1149

Bob Pell	Cell 509-630-1166

Wayne Burns, ATBM	Cell 386-623-5265

Melbourne Airport (MLB)

Chris Worrell, ATGS	Cell 863-661-1827

Helibase/Helicopter Managers

Richard Coleman (129NH) OFC	Cell 540-460-3854

Dan Krapf, HELM (58126) OFC	Cell 440-476-0405

Mike Carr, HELM (HT-701) MAI	Cell 520-850-3860

Ken Burland, HELM.(HT-762) FMY U/A	Cell 406-465-1855

Steve Christiansen, HELM (827MW) BKV	Cell 208-610-2199

Philip Reid, HELM (HT-761) GNV	Cell 503-830-1291

FAX	352-338-0593

Angie Sites, HELM (57Z) TLH	Cell 573-201-5271

Doug Colaprete, HELM (57Z) TLH	Cell 573-201-8327

Bryan Larson, HELM (212AH) ISM	Cell 850-570-5504

Chris Gauthier, HELM (206MP)	Cell 386-344-1189

Mark Akeson, HELM (HT-744) PGD	Cell 218-340-6877

Ray Shows, HELM (6979R) MLB	Cell 601-325-3223

R.C. Martin, HELM (HT-769) TLH	Cell 740-739-0914

Judy Evans, HELM (97HJ) TLH	Cell 601-507-2618

Jack Benzilio, HEB1 TLH	Cell 970-799-1232

Danny Wyatt, HEB1 LCQ	Cell 386-466-8331

Jim Wallace, HEBM OFC	352-759-2081

Terry Grogran, HELM	Cell 509-304-8422

Dan Cottrell, HELM	Cell 847-217-6692

Okefenokee NWR	912-496-7366

Dispatch	Ext. 230

Expanded Dispatch – Aircraft	912-496-4698

POGO Helibase (T-3) 0BJ	912-496-4415

FAX	912-496-3332

Panther NWR

Josh O’Conner, RX	 239-657-5812

FAX	 239-657-5943

Big Cypress National Preserve…………….239-695-2000

John Nobles, FMO	239-695-1145

Cell 239-777-9656

Mike O’Leary	Cell 239-450-2481

Program Assistant	239-695-1146

FAX	239-695-2756

Everglades National Park	305-242-7740

Communications Center………………………305-242-7740

Dispatch Center…………………………………305-242-7850

FAX	305-242-7855

Bob Panko, FMO……………………………….305-242-7852

Merritt Island……………………………………321-861-0846

National Forests in Florida

Supervisor’s Office	850-523-8500

Marsha Kearney, Forest Supervisor	850-523-8549

John Ramey, Advisor	Cell 828-551-5012

James Hart, FMSO 	Cell 850-570-9090

Office	850-523-8562

Lewis Kearney, FMSO Asst.	Cell 850-570-5478

Debbie Casto, FMO	Cell 850-524-9966

Office	850-523-8606

Harold Shenk	Cell 850-524-2578

Glen Fortenberry	Cell 501-622-7762

Interagency Fire Center	850-523-8600

Osceola N.F. Dispatch	386-752-2577 Ext. 4536

FAX	386-754-8479

Ocala N.F. Dispatch	352-759-2081

FAX	352-759-3929

Apalachicola R.D	850-643-2282

Wakulla R.D	850-926-3561

Phil Niswander	850-524-2547

Dick Stiliha, ATGS (901Q)	530-604-2861

Lester Tisino, ATGS (T) (901Q)	318-542-6499

Florida Division of Forestry

Forest Protection	850-488-6111

Brian McKee, Aviation Manager	850-488-1728

Cell 850-228-7764

Robert Duty, Air Tactical Coord.	Cell 850-228-7765

Greg Loper, SEAT Mgr	Cell 850-570-5492

Virginia Ely, SEAT Mgr (T)	Cell 928-202-1060

Jeff Johnson,Military Helicopter Mgr	Cell 850-570-5488

FAX	352-797-5808

Keith Fender, Pilot (122FC)	Cell 850-228-6007

Jeff Lodge, Pilot	Cell 850-228-7769

Larry Davis, Pilot (120FC)	Cell 850-228-7773

John Rourke, Pilot (128FC)	Cell 850-228-7770

Georgia Interagency Coordination Center	770-297-3036

FAX	770-297-3034

Renee Bishop, EDSP	770-297-3027

Kay Akins, EDSD	770-297-3039

Tom Anderson, FMO	770-297-3039

Terry Stolz, Fire Staff Officer	770-297-3090

Georgia Forestry Commission

Alan Dozier, Forestry Protection	478-751-3490

Mike Leverette, State Air Ops Supervisor	478-751-6176

Jerome Harvey, Telecom. Manager	478-751-3494

Macon Dispatch	478-751-3487

FAX	478-751-3506

Macon Expanded Dispatch	478-751-3533

Gainesville District Office	770-531-6043

FAX	770-531-4080

Forrest Sumner, Dist. Ranger	229-726-0285

FOR DISTRICT MANAGERS – SEE DIVISION OF FORESTRY DIRECTORY

Unified Command	850-410-1330

FAX	850-410-1849

Big Turnaround Incident

Doug Grimmett,AOBD	Cell 870-818-1484

John Vinson, ASGS	Cell 352-636-4927

Sweat Farm Rd. Fire

AOBD, Bob Seigler	828-231-4560

FAX	912-285-6014

Operations	912-285-6039

Helibase, Waycross	912-218-8937

James (Zoni) Anzalone, HEB1	505-228-8942

Helibase, POGO	912-496-4415

COST		912-496-7536

Florida Bugaboo

AOBD Dennis Delack	Cell 208-827-1562

FAX		386-719-2734

ATGS Bill Palmer	Cell 252-229-0421

Lake City Helibase	386-754-1017

Second Line	386-755-7271

FAX		386-754-1016

Suwannee Complex

IC Glenn Davis	386-365-4443

FAX		352-473-2736

BICY Complex

ICP		239-695-4198

AOBD		239-695-1152

Don Clark, ASGS	Cell 928-245-2539

Doug Houston, ATGS	406-370-9141

Frank Hayes, ATGS	928-380-5369

Helibase	239-695-0278

15. FICC AIRCRAFT ASSIGNMENT

## Aircraft List – Florida National Forest, Florida Division of Forestry and Georgia Fires 	June 5, 2007

| Number | Type | Pilot | Tail # | Location | Assignment | Status | Day off/Tour | Comments |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Air Attack |
| Baron |  | C. Worrell, ATGS | N841L | MLB | IA | AV |  | Unified |
| ASM/Lead Planes |
| B-2 | ASM | Naveaux/Pryce | 30W | OCF | IA | UA | 5/29-6/4 | Day Off |
| L-4-9 | LP ASM | G. McDonald | 22N | LCQ | IA | AV |  |  |
| L-1-9 | LP |  | 92M | LCQ | IA | UA |  | Unstaffed |
| L-2-1 | LP ASM | Landon/Beck | 76DC | LCQ | IA | AV |  |  |
| Air Tankers |
| T-20 | P3 | Reifenberg | N920AU | OCF | IA | AV | Sunday |  |
| T-21 | P3 | Darnell | N921AU | OCF | IA | AV | Tuesday |  |
| T-22 | P3 | Leslie | N922AU | OCF | IA | AV | Thursday |  |
| T-43 | P2V | Hunt | N443NA | LCQ | IA | AV | Monday |  |
| Seats |
| T-484 | AT802 | Loper, SEMG/Ely, SEMG-T | 166LA | 09FA | IA | AV |  |  |
| T-485 | AT802 | Loper, SEMG/Ely, SEMG-T | 802LA | 09FA | IA | AV |  |  |
| Type/Name | Type | Tail # | HEMG | Location | Assignment | Status | Day Off | Comments |
| S-61 | HT-701 | 1 | 611CK | M. Carr | MAI | IA | AV |  | (DOF) S.Walton |
| S-61 | HT-762 | 1 | 612RM | K. Burland | LAL | IA | AV |  | (DOF) Lee-Collier |
| S-61 | HT-761 | 1 | 81661 | P. Reid | GNV | IA | AV |  | Unified (FS/DOF) |
| S-64 | HT-744 | 1 | 179AC | M. Akeson | PGD | IA | AV |  | (DOF) |
| S-64 | HT-707 | 1 | 6979R | R. Shows | MLB | IA | AV |  | (DOF) Lee-Collier |
| UH-60 | Blackhawk | 1 | 26975 | J. Johnson | BKV | IA | AV |  | (FL National Guard) |
| UH-60 | Blackhawk | 1 | 26608 | “ | BKV | IA | AV |  | (FL National Guard) |
| UH-1H | Super Huey | 2 | 120FC | L. Davis | OBE | IA | AV |  | (DOF) |
| UH-1H | Super Huey | 2 | 122FC | K. Fender | OCF | IA | AV |  | (DOF) |
| UH-1H | Super Huey | 2 | 128FC | J. Rourke | TLH | IA | AV |  | (DOF) |
| UH-1H | Super Huey | 2 | 124FC |  | TLH | IA | UA |  | (DOF) |
| S-58T |  | 2 | 827MW | S. Christianson | BKV | IA | AV |  | (DOF) |
| B-212 |  | 2 | 212AH | B. Larson | ISM | IA | AV |  | (DOF) Lee-Collier |
| 205A++ |  | 2 | 58126 | D. Krapf | 42J | IA | AV |  | Unified |
| 205A1 |  | 2 | 97HJ | J. Evans | TLH | IA | AV |  | Unified |

# Text boxes

(May, 1994)

MODIFIED 4/14/01

NOTE:  ZONE DIVIDERS

Between 1 & 2 – APALACHICOLA RIVER

Between 2 & 3 – SUWANNEE RIVER

Between 3 & 4 – STATE RT. 44 (APPROXIMATE)

Between 4 & 5 – STATE RT. 60 (APPROXIMATE)

Between 5 & 6 – STATE RT. 80 (APPROXIMATE)

Primary	    Primary

Zone	Location	Flt. Following	Air to Ground      Air to Air

1 & 2	Tallahassee	159.300	168.675	122.925

3	Suwannee	159.300	171.575	122.925

4	Withlacoochee	159.300	171.425	122.925

Orlando

5	Okeechobee	159.300	172.275	122.925

Ft. Meyers (50 Mi. radius only)		118.775

6	Caloosahatchee	159.300	170.475	122.925

*Florida City (Within 70 Mile Radius ONLY)                *135.800

* Note: 118.775 (Ft. Myers) becomes primary ONLY within the 50 Mile Radius. 135.800 (Florida City) becomes primary ONLY within the 70 Mile Radius.