Geographic Information System

Standard Operating Procedures on Incidents Project

GIS Standard Operating Procedures

February 2006—Draft 3

Contents

Page

Executive Summary

Introduction

Acronyms

Chapter 1.  GIS Minimum Expectations

Chapter 2.  File Naming and Directory Structure

(Appendix 3.)  Sample Directory Structure

(Appendix 4.)  Sample File Names

Chapter 3.  Documentation and Metadata

Chapter 4.  GIS Minimum Essential Datasets

MEDs for Map Products (spreadsheet)

Essential and Optional Datasets Specifications (spreadsheet)

Chapter 5.  Map Symbology

Map Symbology Samples

Chapter 6.  Map Products

Map Product Definitions

(Appendix 5.) Map Product Samples (posted on http://gis.nwcg.gov/gstop)

[NOTE TO GRAPHICS: place Definitions and Samples on facing pages]

Chapter 7.  Data Archiving and Sharing

Chapter 8.  Team Transition

Appendix 1. ICS Form 213- General Message Form (posted at : http://www.nwcg.gov/pms/forms/icsforms.htm)

Appendix 2.  ICS Form 214- Unit Log (posted at : http://www.nwcg.gov/pms/forms/icsforms.htm)

Glossary

References

Executive Summary

Standard operating procedures (SOP’s) are necessary to clarify the GIS business needs and functional standards for GIS in support of wildland fire incidents, including wildland fire use.  These SOP’s were developed in order to provide consistency in information delivery of GIS products and services.  These SOP’s focus on the GIS work performed by GIS Specialists to fulfill the GIS needs of the Plans Section of the Incident Management Teams. The SOPs may be useful for other types of events, such as all-risk incidents.

These SOP’s were produced by the NWCG Geographic Information System Standard Operating Procedures on Incidents Project (GSTOP) work team under the guidance of the Information Resources Management Working Team (IRMWT) and the Geospatial Task Group (GTG). The SOP’s that are covered in this document pertain to map product development, incident GIS documentation and archiving, and guidance for the GIS Specialist, or those that are performing the mapping function at the incident.

This document contains SOPs which will be met by all NWCG participating agencies. However, it is acknowledged that under some extenuating circumstances it may not be possible to comply with these standards.  Guidelines are also specified throughout the SOPs and are strongly encouraged.

Introduction

The Geographic Information System Standard Operating Procedures on Incidents Project (GSTOP) was chartered by the National Wildfire Coordinating Group (NWCG) fall 2004.  The primary objective of GSTOP was to create SOPs for the use of GIS on wildland fire incidents.  Before this project, there were no GIS SOPs for wildland fire incidents.  The absence of SOPs has created consistency in service issues i.e. data management problems for incident management teams - especially during team transition periods.

The primary audience for this document is the GIS Specialist, other members of the Planning Section, and other personnel reliant on the Planning Section; specifically for use by the people who are actually doing the GIS work on a wildland fire incident.

This SOP addresses a national interagency GIS information management issue. This SOP is intended to provide a technology-independent standard. While over time changes in technology will lead to different actual structures, the design parameters that represent business needs should remain constant.

GIS SOPs are needed on incidents for the following reasons:

- to provide people with all the safety, health, environmental, and operational information necessary to perform a job properly;

- to ensure that production operations are performed consistently;

- to maintain quality control of processes and products;

- to ensure that processes continue uninterrupted and are completed on a prescribed schedule;

- to serve as a training document for teaching users about the process for which the SOP was written;

- to serve as a historical record of the “how, why, and when” steps in an existing process so there is a factual basis for modifying or updating those steps; and

- to ensure the future utility of data generated on wildland fire incidents.

In this document you will find SOPs that have been developed for the following application areas:

- GIS Minimum Expectations – describes the requirements for the fulfillment of the GIS function

- File Naming and Directory Structure – provide an organized file naming and directory structure for the geospatial data

- Documentation and Metadata – provide procedures for the daily documentation of incident GIS data

- Minimum Essential Datasets – describes the minimum base datasets needed for incident mapping (not incident data)

- Map Symbology – provides standard map symbology for incident mapping

- Map Products- provides guidelines for the creation of GIS map products

- Data Archiving and Sharing – provides procedures for the sharing and archiving of GIS data developed on an incident

- Team Transition – provides a method of transitioning from one operational GIS group to another.

This document is aimed at the GIS function on type 1 or type 2 wildland fire incidents.  As the size or complexity of a wildland fire incident increases the mapping demands often expand to adequately portray information relevant to the protection of life, property, and resources.  Local resources (from home unit or a nearby unit) generally handle the GIS needs for type 3 wildland fire incidents; knowledge and use of these SOP’s may be appropriate.

For Wildfire Use Fires, the specifications for hardware, software, and skill set for GIS expertise may be slightly different from those needed for other incidents and may require a higher skill level for environmental modeling and image processing.  SOP’s for modeling and remote sensing are not addressed. Nor do they directly address GIS needs on all risk incidents or for Burned Area Emergency Response (BAER).

Change management procedures for these SOP’s will be administrated by the NWCG

IRWMT Geospatial Task Group. See the GTG website http://gis.nwcg.gov.

Acronyms

APR—(file format) ArcView Project

BAER—Burned Area Emergency Response

BIA—Bureau of Indian Affairs

BLM—Bureau of Land Management

CD—Compact Disk

COTS—Commercial off-the-shelf software

CTSP—Computer Technical Specialist

DHCP—Dynamic Host Configuration Protocol

DHS—Department of Homeland Security

DOC – (file format) Microsoft Word Document

DOCL—Documentation Unit Leader

DOQ—Digital orthophoto quadrangle

DOQQ—Digital orthophoto quarter-quadrangle

DP—Drop Point

DPRO—Display Processor

DRG—Digital Raster Graphics

DVD—Digital videodisc

DVOF—Digital Vertical Obstruction File

ECC – Emergency Coordination Center

ESRI—Environmental Systems Research Institute

FBAN—Fire Behavior Specialist

FEMA—Federal Emergency Management Agency

FGDC—Federal Geographic Data Committee

FIRESCOPE—Firefighting Resources of California Organized for Potential Emergencies

FOBS—Field Observer

FTP—File Transfer Protocol

GACC —Geographic Area Coordination Center

GAO—Government Accountability Office

GEOMAC—Geospatial Multi-Agency Coordination

GNIS—Geographic Name Information System

GPS—Global Positioning System

- GSTOP—Geographic Information System Standard Operating Procedures on Incidents Project

- GTAG—Geospatial Training Advisory Group

GTG—Geospatial Task Group

HTML—Hypertext Markup Language

IAP—Incident Action Plan

IMT—Incident Management Team

IR— Infra-Red

IRIN—Infrared Interpreter

JPG – (file format) Joint Photographic Group

LCES—Lookouts, communications, escape routes, safety zones

LTAN—Long Term Fire Analyst

MED—Minimum Essential Dataset

MMA—Maximum Manageable Area

MOA—Memorandum of Agreement

MTR—Military Training Route

MXD—(file format) Multiple XML Documents (file)

NFES—National Fire Equipment Systems

NTM— National Technical Means

NWCG—National Wildfire Coordinating Group

OGC—Open GIS Consortium

OMB—Office of Management and Budget

PDF—(file format) Portable Document Format

PTB—Position Task Book

PMS—Publication Management System

PNWCG—Pacific North West Coordinating Group

RAM—Random Access Memory

ROSS—Resource Ordering and Statusing System

SITL—Situation Unit Leader

SOP—Standard Operating Procedure

STANDD—Scale bar, Title, Author, North Arrow, Date of Data, Datum

T&E—Threatened and Endangered

TFR—Temporary Flight Restriction

TXT—(file format) Text only

UPS—Uninterruptible Power Supply

UNC—Universal Naming Convention

USB—Universal Serial Bus

UTM—Universal Transverse Mercator

VFR—Visual Flight Rules

WFIP—Wildland Fire Implementation Plan

WFSA—Wildland Fire Situation Analysis

WUI—Wildland Urban Interface

# GIS Minimum Expectations

Purpose:  To describe the requirements for the fulfillment of the minimum GIS function on an incident, including:

- Knowledge and abilities required of the individual GIS Specialist,

- Procedures the GIS Specialist can be expected to follow

- Environmental considerations affecting the worksite of the GIS Specialist

- Equipment needed for a GIS Specialist to function at a basic level—this may vary as the size and type of incident changes

# Critical Items for GIS Operations:

As per national standards, every piece of equipment taken to an incident must be on a Resource Order.

Hardware:

- PC or laptop with CD writer, USB ports and sufficient RAM to run GIS software

- Appropriate output device (e.g., large-format (minimum 36″ wide) plotter with sufficient paper and inks, 11″ × 17″ printer with paper and inks, projector)

- Appropriate connection cables, hubs, power supplies

- External portable hard drive (suggested)

Software:

- Standard current versions of commercial off-the-shelf (COTS) GIS software installed on the computer and operational

- Any required dongles (also known as sentinel or hardware keys) for appropriate licensing

- Appropriate software extensions and tools.

## Specific software tools can be found at http://gis.nwcg.gov.

Infrastructure:

- Internet connection and service

- Power to the work site

- Uninterruptible Power Supply (UPS) with battery backup/surge protection (recommended)

Media:

- USB jump drives/memory sticks

- Blank CD/DVDs

Data:

Refer to Chapter 4, Minimum Essential Datasets

GIS Specialist Knowledge, Skills, and Abilities:

Specific tasks are outlined in the GIS Specialist Position Task Book. Recommended training is outlined in the Qualifications Guidelines (PMS 310-1).

GIS Specialist must be able to:

- Effectively use the standard commercial off the shelf GIS software

- Work with a variety of spatial data types (raster and vector) including knowledge of various data types such as: coverages, geodatabases, and shapefiles

- Understand Global Positioning System (GPS) data collection methods and be able to download, process, and incorporate the data

- Understand the use of a variety of projections and datums including geographic coordinates (latitude/longitude) and be able to reproject data in multiple formats

- Answer questions such as number of acres burned, acres by ownership or other questions requiring basic GIS analysis and geoprocessing functions.

- Troubleshoot hardware and software problems sufficient to keep the GIS function operational.  This may include basic software installs, ensuring the license managers are functioning, installing print drivers, or connecting a plotter to a computer.

- Communicate effectively with people both external to and within the Situation Unit (e.g., GIS Specialists, Situation Unit Leader (SITL), Infrared Interpreters (IRIN), Field Observers (FOBS), Display Processors (DPRO), local hosting agency personnel or cooperating agency personnel)

  - to explain technical issues/concerns

  - to train others in basic map reading

  - to exchange technical information

- Perform the role of GIS Specialist in “incident conditions,” which may include:

  - long hours (12–16-hour shifts, day and night)

  - close quarters shared with other personnel

  - working in stressful conditions

  - traveling (away from home base) for 14 days or longer

  - fire camp conditions (sleeping on the ground, lots of dust and smoke, showers may not be available, and food may be arranged by the incident command staff).

  - working around fire camp personnel, which may include agency, contract, military, or prison crews

GIS Specialist must have knowledge of:

- Basic Incident Command System (ICS) structure and procedures, as outlined in the self-study course (ICS Orientation, Module 1, I-100), sufficient to operate within the chain of command on a wildland fire incident. For example:

  - Know the organizational structure, and whom to go to for issues or support

  - Be familiar with the fire camp operations

  - Understand the general expectations of their supervisor, the SITL.

- Work/Rest standards and other pertinent standards as outlined in the Interagency Standards for Fire and Fire Aviation Operations manual

- GIS Specialists must understand that: firefighter and public safety is the first priority of the fire management organizations.  “The commitment to and accountability for safety is a joint responsibility of all firefighters, managers, and administrators.  Individuals must be responsible for their own performance and accountability.  Safety comes first on every fire, every time.”For the GIS Specialist this means that each individual must demonstrate the maturity and judgment to:

  - Recognize when there might be too much work. The individual must be able to communicate to the SITL the need to prioritize, to adjust workloads or to bring in additional staffing

  - Monitor one’s own physical, emotional and mental limits

  - Follow safe work practices and procedures, as well as identify and report unsafe working conditions using the appropriate chain of command.

- Complexity of the GIS function is independent of the complexity of the fire. It is possible to have a very complex GIS function on a fire of lower complexity.

Incident Procedures:

At the time of dispatch, before arriving at an incident:

Follow the mobilization tasks in the GIS Specialist PTB

- If possible, contact the Situation Unit Leader and/or any GIS Specialist currently assigned to the incident to inquire about the current situation. Inquire about hardware and software currently being used, any special needs or conditions, location of incident, what data is already available, and any transition needs (media, timing, etc.)

- Recognize what resources are lacking (e.g. is there a plotter available?) and handle the need. This could include such things as obtaining permission and logistics for using the hardware/software network of a local unit. It may be necessary to rent a plotter or other necessary equipment.  This must always be done through proper chain of command and proper ordering processes.

Setting up the GIS function and running through the first operational period:

- Check in—follow incident check-in procedures

- Conduct a briefing with SITL to establish ground rules and expectations, as well as the planning timeline for map product production

- Work with SITL to establish an appropriate physical work space

- Do an analysis of data, hardware, personnel, and supplies available and order what you need.  Orders are submitted through your supervisor (SITL) using an ICS Form 213 General Message Form (Appendix 1).  The request is then delivered to the Ordering Manager which allows the incident to rent plotters or other equipment as needed for effective GIS productivity.

- Set up network and shared drives and electronic workspace(s) coordinating with the Computer Technical Specialist (CTSP)

- Set up the file directory structure in accordance with Chapter 2, File Naming and Directory Structure

- Initiate ICS Form 214 Unit Log (Appendix 2) in accordance with Chapter 3, Documentation and Metadata

- Insert base data into directory structure

- Establish what coordinate system and units will be standard for the incident data

- Establish outer boundary of the incident’s area of interest

- Gather what incident data you can; collect hard-copy maps already in use

- Generate map products according to the SOP for Standard Map Products and the SITL timelines and priorities

When serving on an incident, the GIS Specialist is responsible for the following:

- Maintain the standardized filing structures according to Chapter 2, File Naming and Directory Structure

- Collect and maintain the Minimum Essential Datasets in accordance with Chapter 4, Minimum Essential Datasets

- Create new data as needed for incident operations:

  - Incorporate data from (GPS) units and other sources.

  - Digitize fire perimeter and other incident data

- Create necessary products as identified in Chapter 6, Map Products using the Map Symbology defined in Chapter 5 meeting agreed upon timeframes

- Properly document data and archive work according to Chapter 3, Documentation and Metadata and according to Chapter 7, Data Archiving and Sharing.

- Comply with security data management agreement as outlined in Chapter 3 Documentation and Metadata, Chapter 7 Data Archiving and Sharing, and Chapter 8 Team Transition

- Transfer GIS data to and from various locations, which may include FTP sites or websites as requested by the SITL while adhering to Chapter 7, Data Archiving and Sharing

- Effectively transfer the products, projects, and data created in GIS to other personnel on the incident or to the hosting agency according to Chapter 8, Team Transitions

- Comply with demobilizations procedures as required by the incident.

Responsibilities:

GIS Specialist is responsible for the following:

- Keep informed of any known hardware, software, or data difficulties and concerns

- Provide maps as requested by the SITL, focusing on the basic maps

- Collect, process, and disseminate incident related spatial data.

With regard to the GIS function, the Situation Unit Leader is responsible for the following:

- Direct and prioritize all tasks of the GIS Specialists, allowing for individual strengths

- Coordinate and prioritize incoming requests especially those requested by others (e.g., public information officers, cooperators, and others)

- Request map products

- Monitor the workload

- Authorize uploading perimeter data

- Order necessary equipment or people to accomplish the GIS work most effectively (computer support, power, equipment)

Others are responsible for the following:

- People collecting data with GPS units are responsible for knowing how to use their GPS units and to have GPS download cables with them for downloading the data.

Communications:

The GIS Specialist needs to maintain timely and effective exchange of information among the Situation Unit and all affected agencies and organizations.  When communicating with other technical staff from outside the incident, it is imperative that the GIS Specialist maintain a professional demeanor when performing duties.  When communicating within the incident it is essential that the GIS Specialist follow the Incident Command System chain of command at all times.  Most incident communications such as requests for materials, maps, or information will be tracked by using the ICS-213 General Message form.

Whenever there is more than one GIS Specialist on an incident, one of them is usually designated a “lead” to function as a coordinator and deal with the SITL directly on behalf of the GIS group. Some Incident Management Teams carry a GIS Specialist who will usually be designated by the SITL as the “GIS Lead”.

# Appendixes:

# 1—ICS Form 213, General Message Form

# 2—ICS Form 214, Unit Log

# File Naming and Directory Structure

Purpose:  This chapter gives GIS Specialists an efficient, consistent file naming and directory structure that is repeatable, clear, and enables consistent archiving of incident geospatial data. The intention is to allow some extensibility while still meeting the business needs of the GIS function (people, hardware, software, data, and physical location) and those with whom it cooperates.

The incident directory structure provides a framework for storing and using GIS data and documents, efficiently and in an organized way.  The directory structure is designed to facilitate the job of the personnel on an incident.  Ensuring that all incident GIS files are stored within a standardized directory structure is important because it promotes an efficient workflow and data archival process.

This chapter is intended to provide standardized file naming and directory filing structure guidelines for GIS data and related documents created and used on incidents managed under the Incident Command System (ICS).  Typically, this structure would be established and used by incident GIS Specialists, but could also be used by GIS professionals at the home unit of the incident or other organizations after incident operations are over and the GIS data have been archived.

Specifications:

The File Naming and Directory SOP and the Metadata SOP are designed so that the file and folder names include basic incident-specific identification information.

# File names cannot be longer than 255 characters.

# File and folder names must not contain spaces or periods, aside from file extension delimiters.

# File names for specific layers include descriptive data about the incident.

# File names must be complete and stand on their own outside of the file structure.

# The following are required name elements for various file types and listed in sequence they should be shown in the file name separated with underscore:

# The general format is: {date} {incident information} {other information}

# Master map documents (could be an MXD or APR file)

# This file is stored directly under the Projects folder.Year (yyyy) (year the incident started)

# Incident name (the name of the incident)

# Type of map (the standard map product description abbreviation)

# Page size (in inches or ANSI size – A-E)

# Orientation of page (landscape or portrait)

# Map documents backup files (could be an MXD or APR file)

# Date including year (yyyymmdd) (the date the file was saved)

# Time the file was saved (hhmm 24-hour clock)

# Incident name

# Type of map

# Page size

# Orientation of page

# Master Incident geospatial data file (the primary geospatial database used on the incident, could be a personal geodatabase)

# This file is stored directly under the Incident Data folder.

# Year (yyyy) of the incident

# Incident name

# Incident number

# Tool and version used to produce data (optional)

# Incident geospatial data backup file (could be a personal geodatabase)

# Date including year (yyyymmdd) (when the file was backed up)

# Time the file was saved (hhmm 24-hour clock)

# Incident name

# Incident number

# Tool and version used to produce data (optional)

# Incident geospatial theme data files (could be shapefile or coverage or any other data type)

# Incident perimeter export file (exchange format, may be compressed file)

# Date including year (yyyymmdd) (when the data was collected)

# Time of data collection (hhmm using 24-hour clock)

# Incident name

# Incident number including 5-character Unit ID

# Incident data type (the type of data portrayed by the data layer)

# Feature type (point, line, polygon)

# Coordinate system

# Datum

# GPS data files (could be shapefile or coverage or any other data type)

# Date including year (yyyymmdd) (when the data was collected)

# Time of data collection (hhmm using 24-hour clock)

# Incident name

# Incident data type

# Source of data (the ICS position or name of person who collected the data)

# Feature type (point, line, polygon)

# Coordinate system

# Datum

# Map product files (any map produced could be PDF, JPG or EPS)

# Date including year (yyyymmdd) (when the map was produced)

# Time the map was produced (hhmm use 24-hour clock)

# Incident name

# Incident number (the official alpha-numeric incident designation)

# Type of map

# Shift the map will be produced for

# Page size

# Orientation of page

# Other Supporting Documents, Spreadsheets, and other nongeospatial files (could be XLS, DOC, JPG, TIFF, etc.)

# Date including year (yyyymmdd)

# Incident name

# Document contents

# Incident Directory Structure:

# This structure can be stored in any location, however the following describes the core directories to be present for every incident and does not preclude other folders being added.

# Due to agency needs, files for multiple incidents may be stored under a root folder named:{yyyy}_incidents {at the root level, where yyyy = the current calendar year}

- {yyyy_incident_name} {i.e., 2005_dog, where yyyy = the year the incident started}

  - base_data {base data not created on the incident}

    - dem {digital elevation model data and derived products}

    - logos {agency logos, typically in nongeospatial raster format}

    - raster {other raster data such as orthoimagery or scanned quads}

    - vector {vector data file types}

  - documents {spreadsheets, text documents, unit log, digital photos used on maps, etc.}

  - incident_data {data created on the incident stored by date}

    - incident spatial data file {the master incident spatial data file}

    - { yyyymmdd } {contains date/time stamped incident spatial data files backed up from incident spatial data file}

      - gps {optional, contains GIS data from field GPS downloads}

      - other optional folders such as IR, FARSITE, …

    - modified_base_data {base data edited for the incident, i.e. roads, ownership & structures}

    - progression {workspace to create progression data}

  - products {contains GIS product files produced on the incident}

    - { yyyymmdd } all products for an intended date of use (versus the date created)

    - final contains copies of all final products for the incident

  - projects {GIS product tasks, daily map document files}

    - master map document files {the master map document files, one for each map product}

    - { yyyymmdd } {contains backup  map document files copied from master map document files}

  - tools {extensions, tools or other software tools and used on the incident}

Common Abbreviations:

This is a list of standard abbreviations for file naming. For other features, select an unambiguous term.

Incident Data Types

per = Raw Perimeter

dzr = Dozer line

prog = Progression Perimeter

origin = Point of origin

uncfire = Uncontrolled Fire Edge

ctlfire = Controlled Fireline

contin = Contingency line

burn = Burned area, area affected in a given time period

wfsa_alt_a = Wildland Fire Situation Analysis (alternatives a,b,c, etc.)

Damage = Damage caused by incident or suppression efforts

icp = Incident Command Post

ics_fln = ICS fireline symbolized with ICS symbology

ics_pt = ICS points symbolized with ICS symbology

ics_div = ICS division breaks symbolized with ICS symbology mma = Maximum Manageable Area map = Management Action Points hand = handline

Source Codes

gps_name = Global Positioning System (add collectors name) i.e., gps_jones

ir = Infrared

fobs = Field Observer

sitl = Situation Unit Leader

Features (for shapefiles, not needed with Personal GeoDatabases)

pt = point

ln = line

pl = polygon

gr = grid

Coordinate System Codes (for shapefiles, not needed with Personal GeoDatabases)

(coordinate system, datum) u10n27 = Universal Transverse Mercator (UTM) Zone 10, NAD 27

u13n83 = UTM Zone 13, NAD 83

lln83 = Latitude/Longitude; i.e., geographic NAD 83

{st}sp5n27 = {state abbreviation} State Plane Zone 5, NAD 27

Product Type

airops = Aerial Operations map

brief = Briefing map dam = Damage Assessment Map

facil = Facilities map

fuels = Fuels map

iap = Incident Action Plan map

owner = Ownership map

plans = Situation/Plans map

prog = Progression map

rehab = Rehabilitation

struct = Structural protection map

trans = Transportation map

veg = Vegetation map

wfsa = Wildfire Situation Analysis map wfip = Wildland Fire Implementation Plan

Page Orientation

land = Landscape

port = Portrait

Date Format

yyyy = Year in which incident began, e.g., 2005

yyyymmdd = year, month, day, e.g., 20051207

hhmm = Hour and minutes, 24-hour clock, e.g., 0945

Responsibilities and Communications: It is the responsibility of GIS Specialist to communicate the file naming and directory structure used on an incident to other GIS Specialists, hosting unit GIS staff and regional GIS staff.

The Situation Unit is responsible for ensuring only that GIS file naming and directory structure standards are in place for the incident. This chapter specifies a national interagency standard, which should not be overridden at the incident level.

# Appendixes:

# 3—Sample Directory Structure

# 4—Sample File Names

Appendix 3.  Sample Directory Structure

FOR PUBLICATIONS - DO NOT HAVE THIS WRAP

Appendix 4.  Sample File Names

Example from Cottonwood Incident:

Master map document:

2005_cottonwood_iap_11x17_land.mxd

Map document backup file:

20050516_2120_cottonwood_iap_11x17_land.mxd

Master incident geospatial data file:

2005_cottonwood_AR-CRR-1016_fimt91.mdb

Incident geospatial data backup file:

20050516_2230_cottonwood_AR-CRR-1016_fimt91.mdb

Incident perimeter export file:

20050516_2230_cottonwood_ AR-CRR-1016_per_u15n83.zip

Incident geospatial theme data file:

20050516_2230_cottonwood_ AR-CRR-1016_per_fobs_ln_u15n83.shp

Map product file:

20050516_2120_ cottonwood_ AR-CRR-1016_20050517Day_iap_11x17_land.pdf

Non spatial Document:

20050516_1923_cottonwood_ownership.xls

# Documentation and Metadata

Purpose:  The purpose of this SOP is to provide procedures for the daily documentation of incident GIS data and to provide information (metadata) about the data that have been created.  This chapter provides procedures for further documentation to aid the local unit in creation of Federal Geographic Data Committee (FGDC) compliant metadata.

It is recognized that time and resources on an incident do not allow the collection of full FGDC metadata.  To provide for quick and efficient metadata collection, the file name is used to capture the most basic and important metadata components.  Additional metadata about the data can be stored as attributes or as an HTML file.

This chapter does not address how the metadata will be stored; for example, as attributes or in a text file. For incident metadata standards, refer to the Geospatial Task Group (Web site: http://gis.nwcg.gov/)

Specifications:

The following items are in Chapter 2, GIS File Naming and Directory Structure

# Date including year (yyyymmdd)

# Time of data collection (hhmm, using 24-hour clock)

# Type of feature portrayed by the data (see Appendix: list of abbreviations for SOP for File and Folder Structure)

# Source of data (the ICS position or name of person who collected the data)

# Feature type (point, line, polygon)

# Coordinate system

# Datum

# Incident name

# The Daily Fire Perimeter data standard proposed by the GTG is in review by the DAWG. See (website) for current status on this. These are minimum national data standards and local requirements may be added.

Procedures:  Documentation is kept on a Unit Log (ICS 214) by units operating in an incident situation to track significant events that occur throughout the operational day. The log may be hardcopy or digital files with attachments.

Keep a log of events such as the arrival of the IR perimeter, transition of personnel, or archiving of data.  Include one of each type of map produced per shift.  This provides a record of significant changes to the incident data and the products produced.

If base data are used or edited they become Modified Base Data; then the GIS function needs to fulfill the metadata/documentation requirements for that data.

Responsibilities:

The SITL (Situation Unit Leader) is responsible for ensuring that the GIS group is functioning and properly supported and that it fulfills its obligations to the Plans Section. SITL authorizes what documentation the GIS group will provide.

GIS group is responsible for providing agreed-upon documentation to the Documentation Unit Leader (DOCL) and managing agencies as directed by SITL.

DOCL (Documentation Unit Leader) is a customer of the GIS group and is responsible for communicating needs to the SITL.

# Definitions:

# (Reference Glossary)

# Metadata: Information about data, such as content, source, vintage, accuracy, condition, projection, responsible party, contact phone number, method of collection, and other characteristics or descriptions.

Documentation: Methods of tracking information about geospatial data using methods that are less than FGDC compliant.  These may include “ReadMe” files (in TXT or HTML format) or attribution of datasets describing the projection, methods of collection, contact information, and other information.

# Minimum Essential Datasets

Purpose:  This chapter describes the minimum base datasets (other than incident data) that are needed to meet the business needs to make GIS maps or perform analyses on wildland fire incidents. Also, this chapter addresses where to obtain data and how to evaluate whether the data are suitable for use.

# Procedures:

Datasets are used to develop 1) Standard Map Products or 2) other products and deliverables, which include optional maps, Wildland Fire Situation Analysis (WFSA)/Wildland Fire Implementation Plan (WFIP) preparation, and providing data for analysis.

This chapter distinguishes three classes of datasets:

- Those which provide “required elements” for the Standard Map Products

- In addition to those in A, those which provide “required elements” for optional map products and other deliverables

- In addition to those in B, those which provide “optional elements” data to any of the defined map products or other deliverables.

(Reference Chapter 6 Map Products.)

The GIS Specialist is responsible for gathering and evaluating all datasets to be used on an incident.  Class A datasets should be gathered before arrival on an incident, and as many of the Class B datasets as possible.

Specific information regarding preordering will be provided on the GTG Web site at http://gis.nwcg.gov/.  See Essential Optional Datasets Specification for recommendations for obtaining base data, including possible data sources and required fields.  Some datasets may be obtained from the local unit.

Upon receiving orders for GIS Specialist assignment, the GIS Specialist will contact the GIS staff at the local unit where the incident is located and request data to be sent to the Situation Unit.

In all cases, these datasets must be evaluated to determine if they are adequate for use on the incident. The evaluation of the datasets should include a review of the following elements:

- Coordinate system and datum information.  This can be in the form of a file containing coordinate system information for vector data and a world file for images, or documentation associated with the dataset.

- Scale.  Datasets designed for use at one scale may not be suitable for use at other scale (i.e., roads digitized off small scale State transportation maps may not be usable at 1:24000 scale IAP maps).

- Currency.  Determine that the dataset is the most current dataset available.  For example, aviation sectionals are updated at least annually and old versions should not be used.

- Attributes.  Datasets should contain meaningful attributes as per Map Product and Deliverables Matrix.  Use caution with datasets with incomplete attribution.

- Coded Attributes.  Lookup/translation table for codes should be available.

- Security of Data.  Some datasets may contain sensitive or proprietary information and should not be distributed.  Other datasets may have been procured under the premise that they will be used only on the incident and should not be copied or distributed.

- Spatial Accuracy.  The dataset must meet locally acceptable accuracy requirements in order to be fit for a particular use. Marginal datasets may be used if a disclaimer is placed on the output product.

Each dataset that is obtained from a federal source should contain metadata per Executive Order 12906 (http://www.fgdc.gov/metadata/contstan.html )

>>insert spreadsheet

Minimum Essential Datasets for Map Products

Essential and Optional Dataset Specifications

| DATASET | Data Content and Specifications | Suggested Acquisition |
| --- | --- | --- |
| Roads | Road Names, Road Class, Road Surface, Lookup tables with descriptions of coding. Accurate for use at 1:24000 scale. | Prearrival |
| Topographic Base (usually DRG) - optional | Source Date, USGS Standard Color scheme--13 or 256 colors, Revision Date, Collar removed, scan resolution 200-1000 DPI (USGS standard) | Prearrival |
| Water (rivers/lakes) | Name (Optional) | Prearrival |
| GNIS Geographic Names Information System | Name, Type | Prearrival |
| Administrative Boundaries/Ownership/Land Status | Agency/Owner Name, contact info | Prearrival |
| DEMs (Elevation, Slope, Aspect) | Resolution | Prearrival |
| Public Land Survey | Township, Range, Section | Prearrival |
| Structures | Address, Risk Assignment (Optional) | Prearrival |
| Subdivisions | Name | Prearrival |
| Canopy Cover |  | Local Unit |
| Fire Occurrence Polygons | Fire Name, Year | Local Unit |
| Fuels | Fuel Model | Local Unit |
| Land Parcels | Parcel ID, Contact info (Optional) | Local Unit |
| Vegetation | Forest Type, Age, Basal Area, Height | Local Unit |
| Communities (GNIS Populated Places) | Name | Prearrival |
| Airports/Helibases | Name, Type, Lat, Long | Local Unit |
| Aviation Hazards (including DAFIF and DVOF) | Hazard Type, Elevation, Lat, Long | Local Unit |
| Ortho Imagery (usually DOQ) | Source Date, Resolution | Prearrival |
| Political Boundaries (County/State) | Name | Prearrival |
| Shaded Relief | N/A | Prearrival |
| Archaeological Sites | Contact info | Local Unit |
| Cultural Resources | Contact info | Local Unit |
| Infrastructure | Name, Type | Local Unit |
| Other Scanned maps | Source, Source Date | Local Unit |
| Response Areas (Direct Protection Areas) | Name | Local Unit |
| Schools | Name | Local Unit |
| Threatened and Endangered Species (T&E) | Type | Local Unit |
| Wilderness | Name | Local Unit |
| Wildland Urban Interface (WUI) | Type | Local Unit |
| Aviation Sectional | Source Date | Prearrival |

# Responsibilities:

There may be shared responsibilities with other positions (IRIN, FBAN, BAER, or Area Command) or individuals. Identify those individuals, agencies, or groups emphasizing the responsibilities of GIS Specialist.

Communications:

Important contacts:

- SITL regarding available map layers, needed map layers, potential sources, etc.

- Computer Technical Specialist (CTSP) to obtain internet access (if available) for downloading datasets.

- Local unit GIS staff for obtaining best available versions of local datasets relevant to the incident.

# Map Symbology

Purpose:  The use of standard symbols in mapping wildfires facilitates quick and consistent interpretation of mapping products.  Standard map symbols are required to avoid ambiguous map interpretation, which can become a safety issue in the field.

Symbols that are used by anyone who may hand draw maps on an incident are addressed in this SOP to encourage safety, consistency, and readability.

Procedures:

The NWCG Fireline Handbook (410-1) map symbols are the primary Standards.  This document presents additional standard map symbols.

Accompanying text must be given for Drop Point (“DP”) and Helispot (“H”).  These map symbols look identical displayed as black/white.  The text is used not only as a designator of the symbol type, but also as an identifier of a particular feature (e.g., DP-1, DP-2, H-5, etc.).  Hotspot symbols also look like Drop Points and Helispots when displayed in black and white.  However, these features do not include accompanying text.  Care should be taken to place the identifying text close enough to the map symbol to avoid confusion with nearby symbol features.

Caution is also advised in the use of a white halo border for symbols.  A thin, white border around map symbols may facilitate visibility of the symbol.  However, the halo may obscure relevant data underneath.

Although the symbols are evaluated individually and thus technically stand on their own as standards, it is best to assemble the standard symbology as a set of symbols for distribution.

This SOP is intended to be technology independent.  Standard symbols sets for presently accepted GIS software packages (i.e. ArcGIS style set), along with instructions for loading the symbology, can be found on the GTG Web site (http://gis.nwcg.gov).  The symbols will also be available individually as graphics files to be incorporated into any GIS software that allows custom symbols.

Choice of symbol size is left to the discretion of the GIS Specialist and SITL.

General symbology such as hydrography and roads are not included as standards for mapping wildland fire.  However, it is highly recommended that national symbology standards be used where appropriate (e.g. BLM Ownership).

Specifications:

The following acceptance criteria are used for symbol selection:

- GIS symbols must represent features that are incident-based only.

- Standard GIS symbols must relate to the standard map products under the SOP for Standard Map Products.

- Symbols must be easily and quickly identifiable when displayed in color and black and white.

- Symbols must be clearly distinguishable between other ICS symbols when displayed in both color and black and white.

- Symbols must be designed to allow field personnel to easily hand draw the symbols on hard-copy map.

- Symbols in the Fireline Handbook (410-1) shall be included and are not subject to modification with the exception of symbol size and optional halo.

Note: The symbols for Fire Origin, Mobile Weather Unit, and Fire Spread Prediction (from the Fireline Handbook) do not satisfy the GIS SOP Symbology acceptance criteria defined for digital symbols. But while these symbols cannot be modified, you can adjust the symbol size and/or use halo borders.

Map Symbols (standard GIS ICS symbology)

Special Consideration: Safety Symbols

When there is an occasion to map important safety features, the use of these standard map symbols is recommended.

A word of caution: Field conditions can change, making locations outdated and dangerously misleading. These symbols should only be displayed on maps at the direction of the SITL.

Safety Zone (point)-

Several variations of Safety Zone symbols have been created and used on incidents.  A standard Safety Zone symbol will facilitate safety through universal symbol recognition. The triangle shape is unique in ICS symbology.  This makes the Safety Zone symbol easy to identify and distinguish between other ICS symbols.

Lookout – (point)

These features represent the locations of Lookouts posted to facilitate safety of operations.  It is not intended to locate lookout towers or other fixed locations.  Examples of use of this map symbol are in rare situations where a Lookout position is determined in advance for planning purposes, or for showing where Lookouts were posted after the fact.

Escape Route – (line)

Escape Route map symbols represent corridors of passage to safety zones.  These features would most likely be determined in the field.  However, in some instances, escape routes could be identified in advance and mapped accordingly.

Proposed Point (marker) symbols not in the Fireline Handbook (410-1):

- Aerial Hazard

- Aerial Ignition

- Drop Point

- Lookout

- Maximum Manageable Area (MMA) Segment Breaks

- MediVac sites

- Safety Zone

Proposed Line symbols not in the Fireline Handbook (410-1):

## Active Burnout

## Aerial Hazard

## Air Tanker Foam

## Air Tanker Retardant

## Completed Burnout

## Escape Routes

## Explosive Line

## Heat Line

## Helitanker Foam

## Helitanker Water

## Management Action Points (MAP)

## Maximum Manageable Areas (MMA)

## Plow Line

## Proposed Burnout

## Temporary Flight Restriction (TFR)

Proposed Fill (polygon) symbology not in the Fireline Handbook (410-1):

- Intense Heat areas (is this in or out)

- Delegation of Authority

- Temporary Flight Restriction (TFR)

Responsibilities:

The Situation Unit Leader (SITL) is responsible for ensuring that standard map symbology is used for mapping wildland fire incidents.

The GIS Specialist, in turn, is responsible for using the standard GIS map symbology.  However, the GIS Specialist has the cartographic license to adapt (e.g., enlarge, use halo) the symbology for map readability while maintaining the essential design of the standard symbols.  Map symbol colors, if applicable, will be maintained.

Communications:

The GIS Specialist should communicate with the SITL regarding the use of standard mapping symbology on an incident.  This is especially important when the GIS Specialist uses cartographic license to enhance map symbols.

# Definitions:

# Lookouts—Person(s) assigned to vantage points that allow observation of operations and surrounding conditions for safety reasons.

# Plowline—Fireline created by using a tractor plow.

# Fire Location (for Fire Location symbol)—Fire location to be used on large, small-scale maps such as vicinity maps

# Map Symbology Samples

# Map Products

Purpose:  This chapter describes the production of the Standard Map Products that have been defined as used often during ICS Incidents. The intention here is to provide guidelines for the creation of GIS map products during an incident. Optional map definitions have also been developed for other GIS maps that may be created during an incident.

The objective is not to create an impossible standard, nor a standard for every possible product.  These “standards” are intended to be used as guidelines.  Flexibility will need to be applied to these standards as Situation Unit leaders and other end-users may have specific needs or preferences.

Map examples are available on the GTG website (http://gis.nwcg.gov).

General Procedures:

Maps produced on an incident should communicate the intended message clearly.  All map products produced should follow these standards where applicable.  Although some maps may be by special request and there will be no standard to follow, always include the following elements:

- Incident Name and Number

- Legend

- STANDD:

- Scale. The scale is usually drawn at bottom of map. If map is “not to scale” then write that on the map. Map scale may change with copying process.

- Title. Map title should be placed at top of map. Incident name and number should also be included (includes state, unit identifier, and number. For example: ID-BOF-0095).

- Author. The person who created the map should write their name or initials in the lower right corner.

- North Arrow. North arrow should always be on the map.

- Date. The date and time information gathered should be written somewhere on the map.

- Datum. The datum of the coordinates on the map should be written somewhere if coordinates are shown. This is important information for those who use Global Positioning Systems.

Also map products should adhere to:

- ICS Symbology standards (refer to Fireline Handbook)

- Use of standardized colors for maps printed in color (ref. USGS standards), blue for water, green for vegetation, etc.

Accuracy and Completeness:

- Data should be current

- Features are in correct location

- Map scale is accurate

- Map should be complete, readable, and meet the deadlines

Other Procedural Considerations:

- Situation Unit Leader approves all maps and is considered the primary customer

- Use of logos shall be directed by the Situation Unit Leader

- Placement of fire acreage on maps is also at the discretion of the SITL

- Consider page size and whether color is needed; many maps are reproduced on black-and-white copy machines and may need specific formatting

- North arrow may need to be rotated to correctly indicate true north

- include “DRAFT” on maps that are “for review only”

- Sensitive Information—maps may need labels defining the sensitivity of the data (e.g., “For Official Use Only,” “Not for Public Distribution or Use”)

- Any other disclaimers if requested

- Proprietary Information—cite source

- Planning Cycle Timeline—schedule map production to meet specific deadlines (ref. Fire Line Handbook)

# The Standard Maps

# The minimum maps as defined by the GIS Specialist position task book are the:

# Incident Action Plan

# Incident Briefing map

# Situation Map

# Transportation Map

# Progression Map

Responsibilities:  Timelines for map production need to be established with the Situation Unit Leader (SITL). It is the responsibility of the GIS Specialist to produce all products in time for scheduled briefings and other meetings. Map definitions should be used as general guidelines, and Situation Unit Leaders have the authority to direct variations of the standards.

Communications:  All map requests go through the SITL.  This keeps the SITL informed of the GIS function workload and helps prioritize needs.  The SITL may instruct the GIS Specialist to work with the end-user of the map to clarify map product requirements. Final map products are approved by the SITL before release, unless otherwise arranged.

Product Name Incident Action Plan (IAP) Map STANDARD

Product Description The IAP Map is the primary map used by operations personnel in completion of their mission and is a supplement to the Incident Action Plan. Primary Customer Situation Unit Leader Target Audience Incident operations personnel Objective The objective of the IAP Map is to effectively communicate geographic feature relations and incident management objectives on an incident. The IAP map is a tool used by operations staff to show field assignments, crew instructions, and division concerns at the shift briefings and breakout meetings. The IAP Map is a tool for firefighter safety.

Guidelines Standard ICS symbology Black and white to enable clear duplication Letter (8½″ × 11″) or tabloid (11″ × 17″) size Generally 1:24,000 scale Prepared for shift briefings

Required Elements Cartographic STANDD (Scale, Title, Author, North Arrow, Date of Data, Datum) Date and time produced (small font for reference) Incident name and number Symbol legend Shift (day–night) Data* Incident Perimeter and Fireline Division/Branch breaks and labels Topography (usually DRGs with green turned off, use best topo line quality) ICS points (Drop points, aviation features, camps, ICP, spot fires, Safety Zones, and others) Geographic reference (usually Latitude/Longitude)

Optional Elements Index map (when multiple sheets are required) Roads Water (rivers and lakes) Wilderness Boundaries Data source citation (if special data or requested) Disclaimer language (when incident information is estimated or changing quickly, or upon request Magnetic declination and date

*If the incident is a Wildland Fire Use incident, include MMAs, MAPs and MMA segments when applicable.

Product Name Transportation Map STANDARD

Product Description A small planimetric map showing the access routes to the incident. Primary Customer Situation Unit Leader Target Audience Operations, logistics, crews, runners Objective The objective of the Transportation Map to provide an overview of the transportation network in the incident vicinity to support safe transportation. This map is used to facilitate land-based delivery of equipment, supplies, and personnel to and from the incident location.

Guidelines Standard ICS symbology Black and white to enable photocopying and faxing Prepared for shift briefings—insert into IAP

Required Elements Cartographic STANDD (Scale, Title, Author, North Arrow, Date of Data, Datum) Incident name and number Date and time produced Symbol legend Data Incident Perimeter Division/Branch breaks and labels Major roads and names, type of route (dirt, 4wd only, one-way, etc.) Route restrictions (e.g. bridge weight limits) ICS features (e.g. Drop Points, Camps, ICP)

Optional Elements Incident Fireline Geographic reference (Latitude/Longitude, Public Land Survey) Landmarks Vicinity map(s) Label distances along travel routes Mile markers Disclaimer language Administrative boundaries Hydrographic features, such as rivers and lakes County boundaries Communities (GNIS Populated Places) Airports/Helibases Other Scanned Maps

Product Name Incident Briefing Map STANDARD

Product Description The Incident Briefing Map is a large-format map of the incident area, which is used during briefings to discuss work assignments and other details for the upcoming shift. Primary Customer Situation Unit Leader Target Audience Plans Section Chief, Incident Commander, Operations Section Chief, Safety Officer, Fire Behavior Analysts. Objective The Incident Briefing Map objective is to communicate sufficient incident detail to enable operations staff to brief personnel assigned to the upcoming shift.

Guidelines Standard ICS symbology Simple fonts and symbols, large enough to be read from the back of the briefing area Reduced clutter to enable clear communication “E” size (34″ × 44″) or larger

Required Elements Cartographic STANDD (Scale, Title, Author, North Arrow, Date of Data, Datum) Incident name and number Date and time produced Symbol legend Data* Incident Perimeter and Fireline Division/Branch breaks and labels Major transportation routes to incident ICS features (Drop Points, Camps, ICP, Aviation features)

Optional Elements Safety Hazards Escape Routes Topography Geographic reference (Latitude/Longitude, Public Land Survey) Administrative boundaries (e.g., Land Status, Administrative, Ownership, Jurisdiction, Containment WFSA area) *If the incident is a Wildland Fire Use incident, include MAPs and MMA segments when applicable.

Product Name Progression Map STANDARD

Product Description The Progression Map shows the areas impacted by the incident over time. Primary Customer Situation Unit Leader Target Audience Fire Public Information Officer, Fire Behavior Analysts Objective The purpose of the Progression Map is to graphically show the progression of the incident over the landscape.

Guidelines Can be scalable from letter size to “E” size If more than five time periods are shown, shade color ramps are effective to show trends rather than discrete values. Distribution through the web should be considered.

Required Elements Cartographic STANDD (Scale, Title, Author, North Arrow, Date of Data, Datum) Incident name and number Date and time produced Symbol legend Data Point of Fire Origin Origin date and time Shaded relief base/topography base Key geographic features, such as mountains, valleys, peaks, major roads Differing colors for each perimeter time period Acreage affected for each time period

Optional Elements Administrative Boundaries Vicinity map(s) Water (rivers and lakes) Wilderness Boundaries

Product Name Situation/Plans Map STANDARD

Product Description The Situation/Plans Map is a large-format master map with an accurate, current, and detailed record of the incident information. Primary Customer Situation Unit Leader Target Audience Planning Section, Incident Command General Staff Objective The objective of the Situation/Plans Map is to provide a geographic tool for the Plans Meeting to develop incident strategies and alternatives. This is also the map used as the master map for tracking incident intelligence.

Guidelines Standard ICS symbology Feature symbology discernable from the back of the meeting area Usually “D” size (22″ × 34″) or larger Usually 1:24,000 scale

Required Elements Cartographic STANDD (Scale, Title, Author, North Arrow, Date of Data, Datum) Incident name and number Symbol legend Date and time produced Geographic reference (coordinate grid, lat/longs) Data* Incident Perimeter and Fireline ICS points Division/Branch breaks and labels Transportation routes Safety hazards, if available Some kind of base background, vis: Orthoimagery base Shaded relief base Topographic base (usually Digital Raster Graphics)

Optional Elements Safety zones Escape routes Vicinity map(s) Water (rivers and lakes) Wilderness Boundaries Structures Subdivisions Public Land Survey System Political Boundaries (County/State) Response Areas (Direct Protection Areas) *If the incident is a Wildland Fire Use incident, include MMAs, MAPs and MMA segments when applicable.

Product Name Ownership/Land Status Map

Product Description The Ownership/Land Status Map shows the ownership or land status for the areas impacted by the incident. It graphically shows such things as the land ownership or fire protection responsibility in the area of the incident. Target Audience Plans Section, Fire Information Officer, Finance Section, Local Unit or Managing Agency Managers Objective The Ownership/Land Status Map is used in operational planning, public meetings, and for cost apportionment purposes.

Guidelines Can be scalable from letter size to “E” size If the ownership is public it is best to use a standardized color palette to avoid confusion.

Required Elements Cartographic STANDD (Scale, Title, Author, North Arrow, Date of Data, Datum) Incident name and number Date and time produced Symbol legend Data* Incident Perimeter and Fireline Ownership or Land Status Key geographic features Data source citation Incident origin (may be sensitive information so may not be shown on draft maps until authorized)

Optional Elements Total acres or percentage of area affected by owner Shaded relief base Vicinity map(s) Topographic base (usually DRG) Ortho imagery base Administrative boundaries, if different from ownership Political boundaries (County/State) Water (rivers and Lakes) Disclaimer (if requested, or accuracy issues with data sources)

*If the incident is a Wildland Fire Use incident, include MMAs, MAPs and MMA segments when applicable.

Product Name Aerial Operations Map

Product Description The Aerial Operations Map is a map of an incident that emphasizes features important for air operations. Primary Customer Situation Unit Leader Target Audience Pilots, air operations staff Objective The purpose of the Aerial Operations Map is to provide air operations with enough detail to aid in locating key features on an incident.

Guidelines Standard ICS symbology Minimal clutter on map Small size for lap reading in aircraft

Required Elements Cartographic STANDD (Scale, Title, Author, North Arrow, Date of Data, Datum) Incident name and number Date and time produced Symbol legend Latitude/Longitude reference Data* Incident Perimeter and Fireline Division/Branch breaks and labels Airports/Helibases Aviation hazards ICS Points Key landmarks Water (rivers and lakes) Temporary Flight Restrictions (TFR) , if available

Optional Elements Table showing latitude and longitude of key locations Elevation shaded relief Topographic Data (FAA Sectionals or DRGs) Military Training Routes (MTR) and Military Operation Areas (MOA) Wilderness Boundaries

*If the incident is a Wildland Fire Use incident, include MAPs when applicable.

Product Name Damage Assessment Map

Product Description The Damage Assessment Map shows the buildings damaged by the incident. Primary Customer Situation Unit Leader Target Audience Structural Liaison, Information Officer, Public Objective The purpose of the Damage Assessment Map is to be a tool to track buildings and resources damaged in the incident. This product will be used in operational planning and public meetings.

Guidelines Should be done at a scale to distinguish individual structures. May be made early in an incident to serve as a triage tool.

Required Elements Cartographic STANDD (Scale, Title, Author, North Arrow, Date of Data, Datum) Date and time produced (small font for reference) Incident name and number Symbol legend Data Incident Perimeter Structures symbolized based on type or extent of damage Roads—including names and addresses

Optional Elements

Latitude/Longitude indicator Tax lot base Administrative Boundaries Political Boundaries (county/state) Public Land Survey System Topographic base Vicinity map(s) Ortho imagery base Shaded relief Key geographic features

Product Name Structural Protection Map

Product Description The Structural Protection Map shows the buildings potentially threatened by the incident. Primary Customer Situation Unit Leader Target Audience Structural Liaison, Information Officer, Public Objective The purpose of the Structural Protection Map is to be a tool to track buildings and resources that could be impacted by the incident. This product will be used in operational planning and public meetings.

Guidelines Should be done at a scale to distinguish individual structures. May be made early in an incident to serve as a triage tool.

Required Elements Cartographic STANDD (Scale, Title, Author, North Arrow, Date of Data, Datum) Date and time produced (small font for reference) Incident name and number Symbol legend Data* Incident Perimeter Structures symbolized based on type or triage Structure addresses or ID numbers Trigger points and evacuation routes Roads—including names and addresses

Optional Elements Latitude/Longitude indicator Tax lot base Topographic base Vicinity map(s) Ortho imagery base Key geographic features Political Boundaries (county/state) Road blocks

*If the incident is a Wildland Fire Use incident, include MMAs, MAPs and MMA segments when applicable.

Product Name Public Information Map

Product Description The Public Information Map shows the area affected by the incident. Target Audience Information Officer, Public Objective The purpose of the Public Information Map is to keep the public informed of the location of the incident. This product will be used in public meetings and for bulletin boards and displays. Many different types of public information maps may be requested to fit specific needs of the public for information.

Guidelines Should be made at a scale large enough for public meetings. Also may need smaller copies for handouts at meetings.

Required Elements Cartographic STANDD (Scale, Title, Author, North Arrow, Date of Data, Datum) Date and time produced (small font for reference) Incident name and number Symbol legend Data Incident Perimeter (Fireline may be optional) ICP location Major towns and road names Roads and Road Names Communities (GNIS Populated Places)

Optional Elements Structures if available Location of campgrounds or lodges Evacuation areas if established Roadblocks if established Public meeting places Information Board locations Latitude/Longitude indicator Water (rivers and streams) Administrative Boundaries Political Boundaries (county/state) Public Land Survey System Schools Topographic base Vicinity map(s) Ortho imagery base Shaded relief Key geographic features

Product Name Rehabilitation Map

Product Description The Rehabilitation Map shows the rehabilitation requirements, and progress of rehabilitation efforts for the areas impacted by the incident. Primary Customer Situation Unit Leader Target Audience Burned Area Emergency Rehabilitation (BAER) Team, Information Officer, Public Objective The purpose of the Rehabilitation Map is to be a tool to assist in the rehabilitation efforts in the area of the incident. This product will be used in operational planning and public meetings.

Guidelines Should be made as a tool to be used long after the Incident Management Team (IMT) has left.

Required Elements Cartographic STANDD (Scale, Title, Author, North Arrow, Date of Data, Datum) Date and time produced (small font for reference) Incident name and number Symbol legend Data Incident Perimeter and Fireline Treatments—uniquely symbolized

Optional Elements Acreage affected for each treatment Shaded relief base Topographic base Ortho imagery base Latitude/Longitude indicator Vicinity map(s) Key geographic features Political Boundaries (county/state) Water (rivers and lakes)

Product Name Facilities Map

Product Description The Facilities Map shows the layout of the Incident Command Post (ICP) and the associated units. Primary Customer Situation Unit Leader Target Audience Command and general staff, Facilities, law enforcement, visitors to camp Objective The purpose of the Facilities Map is to assist individuals in locating various resources and support functions in and around the ICP.

Guidelines Standard ICS symbology May be schematic

Required Elements Cartographic STANDD (Scale, Title, Author, North Arrow, Date of Data, Datum) Date and time produced (small font for reference) Incident name and number Symbol legend Data Locations of facilities

Optional Elements Vicinity map(s) Political Boundaries (county/state)

Product Name Infrared Information Map

Product Description The Infrared Information Map is a large format topographic map showing the interpretation of remotely sensed infrared imagery of the entire incident. Primary Customer Situation Unit Leader Target Audience Situation Unit, Planning Section, Incident Command General Staff Objective The objective of the Infrared Information Map is to provide a geographic tool for the Situation Unit to determine the incident perimeter, and key areas of operational focus.

Guidelines Standard ICS symbology May be produced by the Infrared Interpreter (IRIN) Usually 1:24,000 scale

Required Elements Cartographic STANDD (Scale, Title w/IR, Author, North Arrow, Date of Data, Datum) Date and time produced (small font for reference) Incident name and number Symbol legend Data Heat perimeter, isolated heat points, heat areas by intensity (these may not all be available) Incident Perimeter, Fireline, and points Usually on topographic base

Optional Elements Geographic reference (Latitude/Longitude, Public Land Survey) Shaded relief Vicinity map(s) DOQQ base Political Boundaries (county/state)

Product Name Fire Perimeter History Map

Product Description The Fire Perimeter History Map shows the polygons of previous fires in the area of the present incident. Primary Customer Situation Unit Leader Target Audience Operations, FBAN, LTAN Objective The purpose of the Fire Perimeter History Map is to be used in operational planning to determine where fires have burned in the past and where the present active fire may or may not go as judged from previous history.

Guidelines Standard ICS symbology

Required Elements Cartographic STANDD (Scale, Title, Author, North Arrow, Date of Data, Datum) Date and time produced (small font for reference) Incident name and number Symbol legend Data Fire history perimeters—perhaps colored by decade with year labels Present fire perimeter and fire line Usually on topographic base

Optional Elements Shaded relief DOQQ Roads Administrative Boundaries

Product Name Vegetation Map

Product Description The Vegetation Map shows the vegetation in the area of the present incident. Primary Customer Situation Unit Leader Target Audience Operations, FBAN, LTAN Objective The purpose of the Vegetation Map is to show the vegetation in the area of the present fire perimeter. It may be used by fire behavior analysts to help predict fire behavior and to develop suppression strategies. It may also be used to develop rehabilitation strategies.

Guidelines Standard ICS symbology Color vegetation types (suggest grasses = yellow, brush = orange, oak woodlands = blue-green or light green, conifers = green, alpine species = purple, barren = gray, water = blue)

Required Elements Cartographic Elements STANDD (Scale, Title, Author, North Arrow, Date of Data, Datum) Date and time produced (small font for reference) Incident name and number Symbol legend Data Elements Vegetation Usually on topographic base Present fire perimeter and fire line

Optional Elements Shaded relief

Product Name Fuels Map

Product Description The Fuels Map shows the surface fuels in the area of the present incident. Primary Customer Situation Unit Leader Target Audience Operations, FBAN, LTAN Objective The purpose of the Fuels Map is to show the fuels in the area of the present fire perimeter. It may be used by fire behavior analysts to help predict fire behavior, to develop suppression strategies. It may also be used to develop rehabilitation strategies.

Guidelines Standard ICS symbology Color fuel types

Required Elements Cartographic STANDD (Scale, Title, Author, North Arrow, Date of Data, Datum) Date and time produced (small font for reference) Incident name and number Symbol legend Data Fuels Present fire perimeter and fire line Usually on topographic base

Optional Elements Shaded relief

Product Name Areas of Special Concern Map

Product Description The Areas of Special Concern Map shows sensitive cultural or environmental areas in the vicinity of the present incident. Primary Customer Situation Unit Leader Target Audience Operations, Resource Advisor, Archaeologist Objective The purpose of the Areas of Special Concern Map is for operational planning to identify sensitive areas such as Endangered Species habitats or locations, Cultural Resources, and other areas at risk.

Guidelines Standard ICS symbology Coordinate symbology for areas of concern with local resource advisor Not for public distribution

Required Elements Cartographic STANDD (Scale, Title, Author, North Arrow, Date of Data, Datum) Date and time produced (small font for reference) Incident name and number Symbol legend Data* Cultural or environmental areas of concern Present fire perimeter and fire line Incident points Usually on topographic base

Optional Elements Shaded relief DOQQ Structures Administrative Boundaries Political Boundaries (county/state) Communites (GNIS Populated Places) Fire history perimeters—perhaps colored by decade with year labels Vegetation Archaeological Sites** Cultural Resources** Schools Threatened and Endangered Species (T&E) Wildland Urban Interface (WUI)

*If the incident is a Wildland Fire Use incident, include MMAs, MAPs and MMA segments when applicable.

**These datasets may be used for land manager planning, but may not be displayed on the final map as the sites are sensitive and not for public display

Product Name Wildfire Situation Analysis (WFSA)/Contingency Map

Product Description The WFSA/Contingency Map shows the area in which to plan the attack. Primary Customer Situation Unit Leader Target Audience Land Managers, Incident Management Team/Planning Unit Objective The purpose of the WFSA/Contingency Map is for operational planning to identify contingency lines and areas at risk.

Guidelines Standard ICS symbology

Required Elements Cartographic Elements STANDD (Scale, Title, Author, North Arrow, Date of Data, Datum) Date and time produced (small font for reference) Incident Name & Number Symbol legend Data Elements Contingency lines WFSA Alternative lines/boundaries Current fire perimeter and fire line Incident points Usually on topographic base Values at Risk (e.g. forage areas, forest plantations, cultural resources**, archaeological sites**, recreational resources, structures, safety concerns, etc.) Administrative boundaries Communities (GNIS Populated Places)

Optional Elements Shaded relief Wilderness Roads Water (rivers and lakes) Land Parcels Political Boundaries (county/state)

** These datasets may be used for land manager planning, but may not be displayed on the final map as the sites are sensitive and not for public display

Product Name Wildland Fire Implementation Plan (WFIP) Map

Product Description The WFIP map shows the area in which the fire can be managed. Primary Customer Situation Unit Leader Target Audience Land Managers, Incident Management Team/Planning Unit, Fire Use Manager Objective The purpose of the WFIP Map is for operational planning to identify the maximum area in which the fire can be managed.

Guidelines Standard ICS symbology

Required Elements Cartographic Elements STANDD (Scale, Title, Author, North Arrow, Date of Data, Datum) Date and time produced (small font for reference) Incident Name & Number Symbol legend Data Elements Maximum Manageable Area (MMA) Maximum Manageable Area Segments Management Action Points if required Current fire perimeter Incident points Values at Risk (e.g. forage areas, forest plantations, cultural resources**, archaeological sites**, recreational resources, structures, safety concerns, threatened and endangered species, etc.) Administrative boundaries Usually on topographic base

Optional Elements Shaded relief Wilderness Vegetation Risk Assessment Trajectories – RERAP/Farsite/Behave outputs

** These datasets may be used for land manager planning, but may not be displayed on the final map as the sites are sensitive and not for public display

# Data Archiving and Sharing

Purpose:  The purpose of this document is to provide procedures for the sharing and archiving of GIS data developed on an incident. Data sharing guidelines minimize the workload on the GIS Specialist by having data made available in a central location, known by all interested parties. Handling of sensitive data is subject to restrictions.

The purpose of archiving data is to capture incident data in a digital format.  In addition, data archiving allows the GIS function to recover a recent status of the incident in case of computer failure or data corruption.

Specifications:

All vector incident data shall be exported to shapefiles before archiving. This allows for compatibility of data among software versions and vendors.

# The primary datasets that need to be shared on a daily basis are the fire perimeter and fireline datasets.  This data shall be posted on a designated ftp or website such as GEOMAC and ftp.nifc.gov.

Incident data and Incident base data layers that have been edited for the incident must be archived.

Procedures:

Data Sharing: At the end of each operational period in which the Fireline and Fire Perimeter data are updated, upload these files to ftp.nifc.gov. Follow FTP directions provided on the GTG website (http://gis.nwcg.gov ) . This allows the data to be accessed by local agencies and other interested parties.  File names must adhere to Chapter 2, File Naming and Directory Structure. Reference GTG website (http://gis.nwcg.gov ) for list of the current upload sites and acceptable file formats (may need to export to shapefiles before sharing the data).

The posting of map products on a standard ftp site is done as a courtesy to other users and done whenever possible.

Data Archiving: GIS data are in a digital format that requires constant maintenance.  Part of this maintenance is the backing up and archiving of data.  For the purpose of the SOP, “archiving” will be used for the process of copying data from an operational format to another for safety purposes and record keeping.  Refer to the Definition, below, for complete information.

Guidelines:

(reference Chapter 2  for File Naming and Directory Structure)

- At the end of each operational period, “incident_data,” and “products” and “projects” directories shall be archived to a different location than the operational computers.

- For incident data, export to shapefiles before any archive task; also archive the geodatabase

- Only dynamic datasets need to be archived.  All base data should also be stored on media separate from operational systems.

- Data should be archived in formats that allow for quick recovery.

- Make an entry in the GIS function Log for each archive.

- Hourly or simple backups can occur for datasets as they change.

- Consider providing a copy of the GIS incident data archive to CTSP or DOCL Unit leader for safekeeping.

Responsibilities:

The GIS function is responsible for checking with GIS representatives of local agencies regarding preferred data format, ensuring proper transition and ease of use of data.

Communications:

As a courtesy, GIS staff may communicate with interested parties as to the location where the data and current map products have been posted.

# Definitions:

# Backup—Backup is intended to provide a mechanism for securing your current, active files; that is, files and data that are resident on your local disk and by implication actively in use.  It enables you to recover your disk to its most recent state in the event that it is lost (for example, hardware failure); it also enables you to recover a file or files that have been lost (for example, accidentally deleted).

# Archive—Archive is the long-term storage of data that are considered to be of value to the Incident.  It is held, independent of the file's continued existence on your local disk. Archived files may be removed from the local disk on your computer if required (for example, for space reasons).

Base Data - Existing data that is used to provide the base features for mapping (e.g. Roads, Land Ownership, DRGs, etc).  This data is not edited during the Incident.

Modified Base Data –  Base Data which has been edited in support of the Incident, but is not ICS data.

Incident Data - Data that is created or edited in support of the Incident.

The main features of archive policy are:

- The archived copy may be kept indefinitely or for a defined period of time; the archive retention period is usually set at 3 or 5 years in the first instance and can be renewable.

- Multiple versions of the same file may be archived; this is not recommended unless the contents of files are different and required.

- Archived data should also include the datasets in their original format.

Data sharing is the process of distributing data to other interested parties/agencies during the course of an incident. At the end of the incident, data is transitioned (see chapter 8 Team Transition)

# Team Transition

Purpose:  This chapter provides the GIS function an effective and consistent method of transitioning from one operational GIS group to another.  The objective of this chapter is to provide the methods of work and direction to ensure that all data and products, plus other related information, are transferred successfully.

Specifications:

Transition of the GIS function refers to any hardware purchased by the incident GIS plus all relevant GIS data and media.  It is important that all data are transferred and remain in their current directory structure per Chapter 2, GIS File Naming and Directory Structure.

Procedures:

Transition is marked by a time of chaos and relief.  It is always important for the GIS function to remain focused and follow procedures when operating during this time period.

The first procedure that must be addressed is transferring data from one storage device to another. The most critical element is to preserve the directory structure, drive letter mapping, or to follow Universal Naming Conventions (UNC) from one GIS group to the next.

GIS groups use a variety of media when operating on an Incident.  These storage devices range from basic shared drives on computers utilizing workgroups; shared portable hard drives; and advanced computer networks utilizing switches, hubs, DHCP, and Snap Servers.  Several methods can be used (Peer to Peer, DVD, extendable hard drives).

General Guidelines:

- Before saving all final products, turn off all software extensions so that the final GIS documents can be opened with the basic installation of the relevant GIS Commercial Off-the-Shelf Software (COTS).

- Before data transfer begins, archive all Incident data to permanent media. (ref. Chapter 7  Data Archiving and Sharing).

- Document any unique characteristics of the data, along with the software (including version) and any tools being used.

- Check for any sensitive information and what guidelines need to be satisfied for it to be transitioned to the next team. (This could include the need to reformat contractors’ hard drives or any other media that will be leaving the incident.)

Documentation useful at transition includes:

- An image, hardcopy, and a list of each map type that has been produced on the incident, as an example of products produced.

- A short narrative describing the status of equipment, workload, work schedule, and other activities.

- A list of resources being used for mapping and data collection. (IR, Contract, NTM, Helicopter, FOBS)

- If one or more GIS Specialists remains on the Incident, he or she should work with the SITL to describe the skill sets of the individual GIS Specialists to better utilize them with the incoming team and advise of their schedule and availability.

- If the SITL authorizes use of nonstandard symbols on an incident, the GIS Specialist should include necessary documentation in the transition package to incoming Incident Management Teams (IMTs) or GIS Specialists.

- The outgoing GIS Specialist will include this map symbology information with incoming GIS Specialists or the SITL during transition briefings.  This is to facilitate consistency in the use of map symbols throughout the life of an incident.

To ensure transition is complete, use the following checklist:

- Are there enough GIS Specialists and is workload appropriate?

- Are the incoming GIS Specialists able to reproduce products by the existing unit?

- Are the needs of the local unit and other entities being met?

- Is the local unit able to work with the new GIS group to continue to access the GIS data? (e.g., sharing of perimeter data)

Responsibilities:

It is the responsibility of the outgoing GIS Specialist to:

- Ensure that the incoming GIS group has a clean, usable, and documented copy of the Incident Data.

- Satisfy requirements for the handling of sensitive data.

It is the responsibility of the outgoing GIS Specialist and SITL to:

- Ensure that the GIS staffing and equipment requirements are planned for and will be met during the transition

It is the responsibility of the Incoming GIS group to:

- Test and verify that all data have been transferred successfully and are fully usable (access, read, and edit) from the target storage device to which the data were moved.

Communications:

If any Sections and Units on the Incident want maps, requests should be made to the SITL directly.

The Computer Specialists (CTSPs) of the outgoing and incoming teams should be made aware of the status of the GIS group, including its network, hardware, and software usage.

Appendix 1 Incident Command System (ICS) Form 213, General Message Form

Appendix 2 Incident Command System (ICS) Form 214, Unit Log

Glossary

Attribute—information about a geographic feature, generally stored in a table and linked to the feature by a unique identifier (6)

Backup—a copy of one or more files made for safekeeping in case the originals are lost or damaged (8)

Coordinates—the x- and y-values that define a location in a planar or three-dimensional coordinate system (21)

Coordinate System—a reference system consisting of a set of points, lines, and surfaces, and a set of rules, used to define the positions of points in space in either two or three dimensions (21)

Datum—in the most general sense, any set of numeric or geometric constant from which other quantities, such as coordinate systems, can be defined (25)

Differential Correction—a technique for increasing the accuracy of GPS measurements by comparing the readings of two receivers—one roving, the other fixed at a known location (27)

Digitize—to convert the shapes of geographic features from media such as paper maps or raster imagery into vector x, y coordinates (28)

Declination [magnetic]—the horizontal angle between geographic north and magnetic north from the point of observation (25)

Dongle [sentinel key]—the sentinel key is a parallel or USB port hardware dongle that provides a unique number used in the generation of your licenses. The sentinel key will return its number only when the sentinel key and the sentinel key driver are communicating properly

Documentation—tracking information about geospatial data using methods that are less than FGDC compliant.  These may include “ReadMe” files (in TXT or HTML format) or attribution of datasets describing the projection, methods of collection, contact information, and other information

Feature—(1) an object in a landscape or on a map; (2) a shape in a spatial data layer, such as a point, line, or polygon, that represents a geographic object (37)

Infrared Imagery—an image created by a device that detects infrared radiation and converts it into an electrical signal that is recorded on film or magnetic tape (52)

USB External Storage Drive—an external disk drive that is connected to a computer through a USB connection

Latitude—the angular distance along a meridian north or south of the equator, usually measured in degrees.  Lines of latitude are also called parallels (59)

Longitude—the angular distance, expressed in degrees, minutes, and seconds, of a point of the earth’s surface east or west of a prime meridian (usually the Greenwich meridian).  All lines of longitude are great circles that intersect the equator and pass through the North and South Poles (62)

Map Scale—the ratio or relation between distance or area on a map and the corresponding distance or area on the ground (89)

# Metadata—information about data, such as content, source, vintage, accuracy, condition, projection, responsible party, contact phone number, method of collection, and other characteristics or descriptions.

Orthoimagery—a digital perspective aerial photograph from which distortions owing to camera tilt and ground relief have been removed.  An orthophotograph has the same scale throughout and can be used as a map. (73)

Projection [map]—a mathematical model that transforms the locations of features on the earth’s curved surface to locations on a two-dimensional surface.  It can be visualized as a transparent globe with a light bulb at its center casting lines of latitude and longitude onto a sheet of paper.  Generally, the paper is either flat and placed tangent to the globe (a planar or azimuthal projection), or formed into a cone or cylinder and placed over the globe (cylindrical and conical projections).  Every map projection distorts distance, are, shape, direction, or some combination thereof. (63)

Planimetric [map] —a map that gives only the x, y locations of features and represents only horizontal distances correctly (77)

Remote Sensing—collecting and interpreting information about the environment and the surface of the earth from a distance, primarily by sensing radiation that is naturally emitted or reflected by the earth’s surface or from the atmosphere, or by sensing signals transmitted from a satellite and reflected back to it.  Examples of remote sensing methods include aerial photography, radar, and satellite imaging. (85)

Shaded Relief Image—a raster image that shows light and shadow on terrain from a given angle of the sun (91)

Shapefile—a vector file format for storing the location, shape, and attributes of geographic features. It is stored in a set of related files and contains one feature class. (91)

Server—a computer and storage device dedicated to storing files. Many users on a network can store files on a particular server.

Topography—the shape or configuration of the land, represented on a map by contour lines, hypsometric tints, and relief shading (100)

( Check the NWCG Glossary; add those into the GIS SOP Glossary. Create definitions for those symbols which do not have definitions.

Note:  Numbers after entries refer to pages in Dictionary of GIS Terminology, The ESRI Press, Redlands, California, 2001, edited by Heather Kennedy.

References

ESRI.  Dictionary of GIS Terminology.  The ESRI Press, Redlands, California.  2001.

Federal Emergency Management Agency, United States Fire Administration.   	Developing Effective Standard Operating Procedures for Fire and EMS 	Departments.  1999.

Federal Geographic Data Committee.  Content Standard for Digital Geospatial 	Metadata.  FGDC-STD-001-1998.  l998.

Government Accountability Office.  Geospatial Information: Holds Promise for 	Wildland Fire Management, but Challenges Remain.  GAO-03-1047. 2003.  	Washington, D.C.

Government Accountability Office.  Geospatial Information—Better Coordination 	and Oversight Could Help Reduce Duplicative Investments.  2004.

NIFC.  Interagency Standards for Fire and Fire Aviation Operations.  (NFES 2724).  	2004.

NIFC Multi-Agency Coordinating Group.  National Interagency Mobilization Guide.  	2003.  Boise, Idaho, National Interagency Fire Center.

NWCG Geospatial Task Group.  Draft Geographic Information Systems Technician 	Taskbook.  2005.

NWCG Incident Operations Standards Working Team.  Fireline Handbook NWCG 	Handbook 3.  PMS 410-1 (NFES 0065).  1998.  Boise, Idaho, National 	Interagency Fire Center.

NWCG Incident Operations Standards Working Team.  Wildland Fire Qualification 	Guide.  PMS 310-1 (NFES 1414).  2000.  Boise, Idaho, National Interagency 	Fire Center.

NWCG Training Working Team—Leadership Committee.  Developing Standard 	Operating Procedures in Wildland Fire Management.  2003.

NWCG/Information Resources Management Working Team—Geospatial Task Group. 	Draft Daily Fire Perimeter Standard.  2004.  (http://gis.nwcg.gov)

NWCG/Information Resources Management Working Team—Geospatial Task Group. 	Draft Fire History Standard.  2004.  (http://gis.nwcg.gov)

Pacific Meridian Resources. Study of Potential Benefits of Geographic Information 	System for Large Fire Incident Management.  1999.  Salt Lake City, Utah.

Subject Matter Experts.  Document Unit Leader Job Aide.  J-342.

U.S. Department of Agriculture and the U.S. Department of Interior Wildland Fire Use Implementation Procedures Reference Guide 2005

# Footnotes

Interagency Standards for Fire and Fire Aviation Operations, January 2005, NFES 2724, Chapter 6 Safety

Interagency Standards for Fire and Fire Aviation Operations, January 2005, NFES 2724, Page 06-1