Fire Perimeter Data Transfer Standards

# Layer:  Daily Fire Perimeter

The daily fire perimeter layer naming convention contains the following:

fire_name_date_time   Example: moose_0705_1700

## Layer Name:  fire_name_date_time

| Layer Description: | Daily fire perimeter data represent the location and includes information associated for the respective fire. . Associated National Application: GACC, FIO, FirePak Fire perimeter polygons represent the daily mapped wildfire perimeter. The data are maintained by the Incident Management Team assigned to the fire. Final products are maintained at the Forest / District level to track the area affected by fire. |
| --- | --- |
| References: | GEOMAC Fire Perimeter Data Elements Paper Information concerning FirePak can be found at the following link. www.fs.fed.us/fire/gis |
| Spatial Data Source: | Best available source with a target scale of 1:24,000 for Continental U.S., Puerto Rico, and Hawaii and 1:63,360 for Alaska. |
| Horizontal Accuracy: | Targeted to National Map Accuracy Standards (NMAS). |
| Projection: | Unit appropriate. Include projection information. |
| Datum: | Unit appropriate. Include projection information. |
| Units of Measure: | Unit appropriate. Include appropriate units for projection selected. |
| Feature Type: | polygon |
| File Type: | ArcView shapefile. |

DBF Attribute Tables

#### fire_name_date_time.dbf

| COLUMN | ITEM NAME | WIDTH | OUTPUT | TYPE | N.DEC | ALTERNATE NAME | INDEXED? |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | SHAPE |  |  |  |  |  |  |
| 2 | ID |  |  |  |  |  |  |
| 3 | AREA |  |  |  |  |  |  |
| 4 | PERIMETER |  |  |  |  |  |  |
| 5 | ACRES |  |  |  |  |  |  |
| 6 | UNITID |  |  |  |  |  |  |
| 7 | FIRENAME |  |  |  |  |  |  |
| 8 | FIRENUM (Fire Number) |  |  |  |  |  |  |
| 9 | DATE |  |  |  |  |  |  |
| 10 | TIME |  |  |  |  |  |  |
| 11 | METHOD |  |  |  |  |  |  |
| 12 | SOURCE |  |  |  |  |  |  |
| 13 | TRAVEL (Travel Method) |  |  |  |  |  |  |
| 14 | DIFFERNTL (Differential Correction) |  |  |  |  |  |  |
| 15 | MAPSCALE |  |  |  |  |  |  |
| 16 | CONTACT |  |  |  |  |  |  |
| 17 | PHONE |  |  |  |  |  |  |
| 18 | EMAIL |  |  |  |  |  |  |
| 19 | PROJECTION |  |  |  |  |  |  |
| 20 | UNITS |  |  |  |  |  |  |
| 21 | DATUM |  |  |  |  |  |  |
| 22 | COMMENTS |  |  |  |  |  |  |
| 23 | PERIM_MILES |  |  |  |  |  |  |

| Domain for DBF files: Daily Fire Perimeter Transfer Standards |
| --- |
| ITEM NAME: Description |
| Valid Values | Value Description |
| ACRES: Determined during use of FirePak or normal GIS calculations |
| Example: 684 | Description: Daily acreage as reported in the Incident Command System Status Report 209 |
| CONTACT: Contact person for information concerning the fire perimeter |
| Example: Smokey T. Bear | Description: First and last name. Middle initial optional |
| COMMENTS: Fire related comments |
| Example: Fire perimeter from GPS and field information | Description: Comments related to fire perimeter generation |
| DATE: Collection Date for the fire perimeter |
| Example: 20020705 | Description: (YYYYMMDD) Perimeter collected July 5, 2002 |
| DATUM: Datum that fire perimeter is in |
| WGS84 | World Geodetic System 1984 |
| NAD27 | North American Datum 1927 |
| NAD83 | North American Datum 1983 |
| Other | Specify Datum used |
| DIFFERENTIAL CORRECTION: Specify Differential Correction process used |
| No Correction |  |
| Real-time WAS |  |
| Real-time CORS |  |
| Post-processing |  |
| Other |  |
| EMAIL: email address for individual identified as contact |
| Example: sbear@fs.fed.us |  |
| FIRE NAME: Assigned incident name |
| Example: Kokopelli | Name may be textual or numeric |
| FIRE NUMBER: Assigned Incident order number |
| Example: MT-LNF-016 | Description: Not “P” or “G” number |

| Domain for DBF tables: Daily Fire Perimeter Transfer Standards cont. |
| --- |
| MAP SCALE: If fire perimeter was digitized identify the native map scale resolution |
| 24,000 | Description: representative map scale fraction at which the |
| 63,360 | Fire perimeter was digitized. Values Shown are selection |
| 100,000 | Options in FirePak. |
| 250,000 |  |
| Other | Specify scale at which digitized |
| COLLECTION METHOD: Collection method used to generate fire perimeter |
| GPS | Description: Global Positioning System |
| Digitized | Description: |
| PERIMETER_MILES: Daily perimeter expressed in miles. Calculated by FirePak. View distance units must be set to miles. |
| Example: 5 | Description: Daily fire perimeter in miles as reported in the Incident Command System Status Report 209 |
| PHONE: Phone number where contact person can be reached. |
| Example: 928.216.3456 | Description: Incident location, include area code and extensions |
| PROJECTION: Identify Projection used |
| Geographic | Description: |
| UTM Zone 12 | Description: Zone Specific |
| Alaska Albers | Description: |
| Other | Identify appropriate projection |
| SOURCE: Identify the type Global Positioning Unit or digitizing method used to create the fire perimeter |
| Garmin III Plus | Description: Options shown are selection options in FirePak |
| Garmin V |  |
| Garmin eTrex |  |
| PLGR GPS |  |
| Trimble GeoExplorer II/III |  |
| Trimble Pathfinder Pocket |  |
| Trimble ProXR |  |
| Aerial Hand Drawn |  |
| IR Interpretation |  |
| IKONOS |  |
| LandSat |  |
| LandSat Delta NBR |  |
| Other |  |
| Domain for DBF tables: Daily Fire Perimeter Transfer Standards cont. |
| TIME: Collection Time in 24 hour military |
| Example: 1700 | Description: Military (HHMM). Time daily fire perimeter represents. |
| TRAVEL: Travel method used during Global Positioning System collection |
| Helicopter |  |
| Fixed Wing |  |
| ATV | Description: All Terrain Vehicle, e.g., four-wheeler |
| Foot |  |
| Other |  |
| UNIT ID: Unique unit ID covered by where the incident occurs |
| Example: 110301 | Description: Concatenation of region, unit, subunit. Agency: 2 characters: 11 (Forest Service) Unit: 2 characters: 03 (Forest Service Region) Subunit: 2 characters: 01 (Forest number) All parts of this code are right justified and zero filled. |
| UNITS: Appropriate units associated with projection and datum used for the fire perimeter |
| Decimal Degrees |  |
| meters |  |
| feet |  |
| other |  |

#### Relational Database Views

NONE