Potential Smoke Impacts Daily Report

| Daily PC HYSPLIT Forecasted Smoke Dispersion and Air Quality Index Forecast for May 11, 2011 (HYSPLIT Meteorological File: May 10, 2011 UTC18) |  |
| --- | --- |
|  | Daily AQI |
| The PC HYSPLIT results above allow you to compare to a benchmark that reflects the 24-hour PM2.5 standard (35 ug/m3). The Orange polygon represents those areas where the 24 hour average concentration higher (including a background concentration of 10 ug/m3) is greater than the benchmark on May 11. This area (within 45 miles of the burn unit) is where unhealthy levels of fine particulates could occur and the value exceeds the daily PM2.5 National Ambient Air Quality Standard (NAAQS). Folkston, Kings Island, and Hilliard, GA may experience fine particulate matter concentrations near the or above the NAAQS. State air regulatory agencies provide forecasts using the Air Quality Index (AQI) that correspond to different pollution concentrations and related health warnings. The round dots on the above map (excluding city centers) are color coded according to the AQI. Code yellow (moderate air quality) is predicted for the monitoring sites shown on the map. The results above are best viewed in Google Earth. The filename is: HoneyPrairie_May11_Daily_HYSPLITconc_0510_evening.kmz |

| Hourly PC HYSPLIT Forecasted Smoke Dispersion for May 11, 2011 (HYSPLIT Meteorological File: May 10, 2011 UTC18) |  |
| --- | --- |
|  | Hourly AQI |
| Short-term (1-hour or less) concentrations of Unhealthy, Very Unhealthy or Hazardous fine particulate matter concentrations are predicted for tomorrow. Numerous communities that are east of the burn unit and between Brunswick, GA and the Georgia/Florida state line are predicted to have the air quality significantly degraded from smoke attributed to the wildfire. Heavy smoke concentrations should be anticipated along highways and Interstate 95. The high concentrations of fine particles combined with the predicted high relative humidity may result in smoke/fog formation in some location. If super-fog forms then there will be an increase likelihood of vehicle accidents because visibility quickly degraded for the motorists. The results above are best viewed in Google Earth. The filename is: HoneyPrairie_May11_Hourly_HYSPLITconc_0510_evening.kmz |

| Fire Spread and Emissions Profile Predicted for May 11, 2011 |
| --- |
| Rate of Spread | PM2.5 Hourly Emissions |
| The gray polygon shown above is the approximate total area burned by 1000 hour on May 10. This analysis assumed the rate of active fire spread will continue to blacken approximately 550 acres per hour and this is based upon the average rate of spread between May 7 – 10. The estimated total blackened area by May 10 at 1000 hours was 72,792 acres. | The average consumption was estimated to be 13 tons per acre, and this includes 3.6 tons per acre of duff consumption. Smoldering (drifted PM2.5) emissions are predicted to occur throughout the nighttime. Atmospheric stability is predicted to be moderately unstable until about 1800 then atmospheric conditions will become less favorable for smoke dispersal. |

| Hourly PC HYSPLIT Forecasted Smoke Dispersion for May 12, 2011 (HYSPLIT Meteorological File: May 10, 2011 UTC18) |  |
| --- | --- |
|  | Hourly AQI |
| The hourly modeling predictions above are for May 12, 2011 between midnight at 2:00 PM. The meteorological model has predicted a wind shift from the southeast beginning at midnight. Heavy smoke concentrations should be anticipated along highways in the early morning hours and throughout the day. The results above are best viewed in Google Earth. The filename is: HoneyPrairie_May11_Hourly_HYSPLITconc_0510_evening.kmz |