OPERATION SAFETY ACTION PLAN

2012 MAFFS TRAINING - May 06 2012 -- May 10, 2012

Donaldson Airport, Greenville South Carolina

PURPOSE – The purpose of this Plan is to provide for individual and public safety by identifying, monitoring and managing all safety hazards for the duration of the operation.

POLICY – It is the policy of the MLO and Mission Commander that safety of personnel is of primary importance and concern throughout all aspects of the operation. Once identified, safety hazards or concerns shall be appropriately mitigated or addressed.

ROLES & RESPONSIBILITIES :

MLO – Establish safety policy.

Safety Officers – Implement safety policy.

Operations personnel – Assure that safety considerations are included in all tactical and strategic decisions.

Supervisors – Communicate safety information to all assigned personnel and closely monitor their activities to assure compliance.

All Personnel – Responsible for performing in a safe manner at all times.

ELEMENTS – Safety Officers will develop a system sufficient to address safety issues associated with MAFFS operations. MAFFS operations involve many hazardous conditions to which personnel must be aware of and sensitive to in order to avoid personal injury and / or property damage. Hazards include but are not limited to: operation of vehicles, aircraft, forklifts, and other miscellaneous machinery; wet, slippery surfaces; obstructions to both walkways and vehicle routes; congestion due to limited operating space; suspended or blowing dust, retardant (not used in training operation) and debris; and especially high noise levels.

Daily safety briefings will be the primary means of communicating safety concerns and issues to personnel. It is imperative that supervisors communicate information to all personnel assigned to them, to assure that the information reaches all levels.

Daily safety briefings are required for ANYONE in the ramp and pit area within the security gates.

Safety Officers will monitor conditions on the ramp, pits, parking areas (aircraft & vehicles), facilities, and adjacent areas to the operation. Important or useful information and mitigation measures will be communicated to affected personnel.

MITIGATION OF CONCERNS OR HAZARDS:

COMMUNICATION –   The most effective mitigation measure to correct any safety hazard is communication. This includes all forms of communication including verbal, visual, or written. Any safety hazard regardless of who identifies the hazard is to be communicated to the MLO, Operations, Assistant MLO, or Safety Officer so measures can be taken to mitigate the hazard.

HAZARDOUS MATERIALS - In compliance with the “Hazard Communications” standard required by the Occupational Safety and Health Administration (OSHA) the following guidelines will be followed during any MAFFS operation. The following will be provided by United States Forest Service, Military, and Contractors:

Hazardous Chemicals will be identified and labeled.

Material Safety Data Sheet (MSDS) for each identified hazardous material will be available for employee review.

Any hazard information will be communicated to all personnel and visitors through labels, signs, MSDS’s, and briefings.

MEDICAL PLAN – All medical emergencies will be handled by Donaldson Center Airport Fire & Rescue. They can be contacted by dialing 911, and 864-277-1117 or 864 277-1429.  Donaldson Fire & Rescue will arrange for any transportation needs to medical facilities. MAFFS Operations Bldg# 1312 is designated for reporting of emergencies purposes.

SAFE MAFFS OPERATING PROCEDURE

- Aircraft

  - Never walk beneath, between, or in close proximity to aircraft propellers (turning or stopped).

  - Do not approach aircraft until the engines have been shutdown and aircraft is chocked.

  - Avoid the area to the rear of the aircraft while engines are running. Some Hazards include:

    - Propeller blast, dust, debris, fumes

    - Fumes from unspent fuel after shutdown can ignite.

  - Forest service& military crew/maintenance personnel will perform aircraft operational functions.

  - Always follow the instructions of the air crew while in or around aircraft.

  - Aircraft takeoff intervals and pit sequence will be directed by assigned forest service personnel with visibility of ramp/pit area. Agency will request deviations through the Mission Commander or MLO.

  - Only essential personnel to the mission will be allowed aboard the aircraft.

  - Air Force refueling procedures will be complied with.

  - Air Force flight crews shall wear protective clothing during all MAFFS missions.

  - NO HOT RELOADING OF ANY AIRCRAFT.

(11) Only essential civilian vehicles will be authorized in the ramp area. Vehicles must obtain and display a ramp pass, which will be issued by the forest service security personnel prior to entering ramp area. All vehicles will be approved through Mission Commander & MLO.

(12) All press/news and other visitors will be escorted by authorized MAFFS personnel and obtain a visitors pass while on the ramp.

- Compressors

  - Only qualified personnel will operate compressors.

  - Avoid walking/standing near compressors and high pressure hoses while in operation. Pressure is released from the air line by a pressure relief valve mounted on the compressor. Noise, air release, hot surfaces and moving parts hazards exist.

  - Loaders and compressor operators will prearrange hand signals before commencing loading operations.

Note: Compressors produce up to 3,500 psi of pressure.

- Safety Equipment:

  - Ear protection is required in the ramp/pit area.

  - Safety glasses or eye protection is required in the ramp/pit area.

  - Personnel involved in ramp/pit operations will wear shoes with non-skid soles, and shirt at all times (gloves recommended).

  - Fire extinguishers will be immediately accessible to the air compressor units.

  - Loading and maintenance personnel will use reflective vest or reflective strips on clothing if working after dark.

- Vehicles & Traffic:

  - MLO will designate type of vehicle authorized in each operation. Vehicles in the ramp/pit area must be kept to the minimum necessary for the operation.

  - No vehicles other than refueling, security, MAFFS maintenance, and fire rescue will approach aircraft nearer than 50 feet.

  - Crossing ramps/planks for vehicle traffic will be placed at hose crossing points.

  - Golf cart type vehicles are highly recommended for there low profile, low impact nature.

  - No vehicles will cross pressurized hoses.

  - Hose couplings, valves, ect. Will be marked with pylons to avoid damage from vehicles, equipment, ect. Pylons and other loose objects will be weighted to avoid prop blast.

- Visitors

  - Visitors to the ramp/pit area must be authorized by the MLO, Tanker Base Manager, or Mission Commander. It is required that the visitors receive a full safety briefing and are escorted by agency or military personnel.

  - Visitors will be provided appropriate safety equipment, including ear protection.

  - Members of the press will be escorted by the assigned Incident Information Officer or other appropriate personnel assigned by the MLO.

  - Visitors should remain clear of parking ramps, aircraft, pits, compressors, and retardant operation.

- Smoking Areas

  - Smoking is permitted in designated break area.

- Other

  - Any spills will be mitigated immediately.

  - Fire lanes will remain clear for fire/rescue vehicles.

  - Liquid oxygen will only be handled by qualified personnel.

- Hazard Analysis

The following matrix generally defines working areas for personnel and hazards existing in those areas. Personnel should review applicable sections of the analysis to become familiar with hazards and attempt to avoid areas they are not assigned to reduce congestion.

|  | Military Crews & Maintenance Personnel | Loaders | Tanker Base Managers | Mix Masters & Contractors | MAFFS Mechanic | Wash Down Crew | Ramp MGR | *Hazards |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Aircraft Parking Ramp | X | X | X | X | X | X | X | All |
| Loading Pits |  | X | X | X | X | X | X | 1,2,3,5,6,7, 8,9 |
| Aircraft | X | X | X | X | X | X | X | All |
| Compressor & Hose |  | X | X |  | X |  |  | 1,3,4,5, 6,7,8,9 |
| Retardant Plant |  |  | X | X |  |  |  | 1,4,5, 6,7,9 |

HAZARDS LISTING:

1. Noise					6. Slippery Surfaces

2. Operating Aircraft Hazards		7. Suspended Dust, Debris or Retardant

3. High Pressure Hoses			8. Fire

4. Moving Parts				9. Moving Vehicles

5. Walkway Obstructions

LIGHTING PLAN

Determination of lightning activity:

•	The FAA Tower at Donaldson Air Center receives airfield weather and lightning information from the National Weather Service at Greer, South Carolina.

•	The following sequence describes the notification for lightning activity within 5 nautical miles of the airfield: FAA Tower personnel will notify Donaldson Air Center Fire Department Dispatch.

The Fire Department Dispatch will contact MAFFS Ops

The Fire Department Dispatch will contact Lockheed to open their gates in the fence separating Lockheed and the MAFFS operations ramp. MAFFS Ops will notify Ground Safety Managers, the "Sugar Shack", and Bldg # 1312 and relay the weather alert via radio. The "Sugar Shack" will relay the weather alert via agency ramp radio frequency and safety officers will contact the flightline area personnel.

•	Three blasts of an air horn will serve as notification to take cover.

•	Personnel will move into designated building # 1312 MAFFS “Sugar Shack” primary and the Donaldson Fire Department overflow of personnel. MLO Operations, “Sugar Shack” will serve as primary shelter during lightning or wind events.

•	When threat of lightning has passed, personnel will be allowed to return to the outside environment.

•	Verbal permission from appropriate authority {Safety MLO Officer ,Line Chief, etc.) or one long blast from an air horn may serve as notification of release from restrictions.

Flightline Active:

•	Aircraft engine noise can obscure conventional methods of notification for personnel to take cover. An agency representative {NCANG Safety Officer, MAFFS MLO Base Manager, etc.) and or a military representative {Safety Officer, line Chief, etc.) should walk the operations area and notify personnel. Face to face notification will be expedited to reduce exposure.

•	Personnel will move into designated buildings. MLO Operations “Sugar Shack” Bldg#1312, will serve as primary shelter during lightning or wind events. Overflow personnel will go to the Donaldson Fire Department at the entrance gate.

•	If aircraft enter the ramp area, military and agency personnel will remain under cover. MAFFS Operations will have radio contact with C-130 pilots to communicate detection of lightning. Military pilots may exercise the choice to park at their discretion and shut-down aircraft engines. Once lightning danger has passed these aircraft can be towed into appropriate pit or parking areas.

•	When threat of lightning has passed, personnel will be allowed to return to the outside environment.

•	Verbal permission from appropriate authority (Safety Officer, line Chief, etc.), or one long blast from an air horn may serve as notification of release from restrictions.

LIGHTING PLAN

Security personnel at entrance gates:

• 		It is strongly advised that vehicle be made available to security personnel and staged in close proximity to a guarded entry gate. Upon notification, security personnel will take cover from lightning inside the vehicle.

•		If a vehicle is not available to shelter security personnel, gates will be secured and personnel will move into a designated building. Donaldson Air Center Fire Department's substation adjacent to the FAA Tower will serve as lightning and wind shelter for security personnel and overflow of flightline MAFFS personnel.

EMERGENCY PROCEDURES

Aircraft Crash Rescue Response (continued)

Dependent on declared emergency the Fire Department Crash Rescue unit can elect to stop the aircraft on any airfield surface. Aircraft attached to MAFFS training may be diverted to another area.

In the event of an emergency requiring Crash Rescue Fire Department response, the aircraft and     ramp are the jurisdiction of the Fire Department and their Incident Commander. Until the response has been cleared by the Fire Department, Agency and military personnel will not enter the aircraft ramp or. Approach the aircraft.

Fire Hydrant Precedence

Fire hydrants adjacent to the aircraft ramp will supply water to MAFFS operations. These hydrants are primary water supplies for Fire Department emergency operations. Fire Department use of these hydrants will take precedence over MAFFS operations.

(

| MEDICAL PLAN | Incident Name MAFFS Training Greenville, SC | Date Prepared 6 MAY 2012 | Time Prepared 10:00 AM | Operational Period |
| --- | --- | --- | --- | --- |
| 5. Incident Medical Aid Station |
| Medical Aid Stations | Location | Paramedics Yes No |
| Donaldson Center Airport | Fire Service Area, | X |  |
|  | Donaldson Center Airport |  |  |
|  | Greenville, SC |  |  |
| EMERGENCY'S ONLY | Ph. No. 864-277-1117 |  |  |
| Business Office | (864) 277-1429 |  |  |
| 6. Transportation |
| A. Ambulance Services |
| Name | Address | Phone | Paramedics Yes No |
| Emergency Medical Service | Greenville County | 864-277-1117 | X |  |
| Gantt District Fire Dept. | 1331 White Horse RD | 864-277-0429 | X |  |
| South Greenville Fire District | 8305 Augusta RD Pelz | 864-243-5650 | X |  |
| B. Incident Ambulances |
| Name | Location | Paramedics Yes No |
| EMS UNIT @ DONALDSON | Donaldson Center Airport | X |  |
| CENTER FIRE SERVICE |  |  |  |
| 7. Hospitals |
| Name | Address | Travel Time Air Ground | Phone | Helipad Yes No | Burn Center Yes No |
| Greenville Memorial | 701 Grove Road, Greenville, SC | 4 | 10 | 864-455-7000 | X |  |  | X |
| TRAUMA CENTER |  |  |  |  |  |  |  |  |
| St. Francis Hosp. | 1 St. Francis Drive | 5 | 15 | 864-255-1000 | X |  |  | X |
| Augusra Burn Center | Augusta, GA | 30 | 150 | 706-651-3232 | X |  | X |  |
| 8. Medical Emergency Procedures |
| Any emergency’s are to be routed through Donaldson Airport Fire Department @ (864) 277-1117. They are the first responders and will dispatch closest Emergency Services (EMS) as necessary. |
| Prepared by: 145th AW – Safety Manager – SMSGT J. ALLEN “SGT MAC” MCGAHA – CELL# 980-721-0142 REVIEWED BY: US FORREST SERVICE MLO OFFICER AND SAFETY OFFICER |