Project Date:  4.7.2003

PCF GIS Department

Passage: Jocassee Gorges

Section: tablerock to Beasley gap

Coverages/Shapefiles:  jocasee1_utm,  jocassee1_sp

Staff:	Tom Savage

Comments:

I have attached two shapefiles depicting the trail passage from Table Rock to Beasley Gap (US HWY 178).  The data was collected using Trimbles ProXL Unit, and post processed using the Greenville Base Station.

The original data was projected in Stateplane Coordinate System and reprojected to UTM, using ArcInfo and NADCON projection algorithm.

State Plane Parameters used:   Stateplane, fipszone 3900, datum NAD83, units feet

UTM Parameters: UTM, zone 17, datum nad83, units meters.

## Conclusion