PART F - INDIVIDUAL TREATMENT SPECIFICATION

| TREATMENT/ACTIVITY NAME | #3 Upsize culverts | PART E Abbreviated Name | Upsize culverts |
| --- | --- | --- | --- |
| NFPORS TREATMENT CATEGORY* | Emergency Stabilization | FISCAL YEAR(S) (list each year): | 2007, 2008 |
| NFPORS TREATMENT TYPE * | Emergency Stabilization Plan Preparation | WUI? Y / N | N |
| IMPACTED COMMUNITIES AT RISK | None | IMPACTED T&E SPECIES | None |
| FSM 2520 REFERENCE | 2523.2 (3b) Structures | SPECIFICATION # | 3 |

* See NFPORS Restoration & Rehabilitation module – Edit Treatment screen for applicable entries.

WORK TO BE DONE

A. General Description: Several stream crossings drain steep watersheds that are prone to flash flooding, washout, and deposition of mud. Nine (9) culverts along FS system roads within the burned area were determined during the BAER field assessment to be undersized for potential post-fire runoff events. This project will replace nine culverts with larger culverts in order to pass storm flow with minimal to no damage to the roads. B. Location/(Suitable) Sites: Three (3) culvert sites on Road #745; three (3) culvert sites on Road #751; two (2) culvert sites on Road #067; and one (1) culvert site on Road #668. For exact locations see Appendix IV, Watershed Treatments Map. C. Design/Construction Specifications: FS engineer will do design work for each of the 9 sites and will oversee project work by contractor such that the replacement culverts are properly set at the right depth and aligned with the stream channels at the inlets and outlets. FS Implementation Leader will develop the contract and review the job sites for adherence to the contract. FS Archeologist will use engineer’s design showing changes in culvert alignment, length and width and staging areas at each site to conduct archeological survey before contract work begins; and obtain clearance from SHPO. Contractor will direct the site work. Contractor will use a backhoe to remove undersized culverts from road bed. Removed culverts are not to be left on site, but carried to warehouse where they can be either reused or scrapped. D. Purpose of Treatment Specifications (relate to damage/change caused by fire): To upsize culvert capacity to handle post-fire increased flows and possible flood flows in order to protect road beds and motorists. E. Treatment consistent with Agency Land Management Plan (identify which plan): Humboldt National Forest Land Resource Management Plan. F. Treatment Effectiveness Monitoring Proposed: See Specification 5, Post-storm Road Patrol and Maintenance. These nine new culverts will be included in the road patrol specification for proper functioning and condition.

LABOR, MATERIALS AND OTHER COST:

| PERSONNEL SERVICES: (Grade @ Cost/Hours X # Hours X # Fiscal Years = Cost/Item): Do not include contract personnel costs here (see contractor services below). | COST / ITEM |
| --- | --- |
| One FS GS-12/5 Implementation Leader @ $3976/pp x 0.5 pp (includes 35% for Benefits; 17% for Admin and oversight ) | $1,988 |
| One FS GS-07/5 Engineer Tech @ $30.76/hour x 8 hours x 7 days (includes 35% for Benefits; 17% for Admin and oversight ) | $1,723 |
| One GS-11/5 Archeologist @ $61.29/hour x 8 hours x 5 days (includes 35% for Benefits; 17% for Admin and oversight) | $2,452 |
| Contract administration (15% overhead for cost of contract) | $5,082 |
| TOTAL PERSONNEL SERVICE COST | 11,245 |
| EQUIPMENT PURCHASE, LEASE AND/OR RENT (Item @ Cost/Hour X # of Hours X #Fiscal Years = Cost/Item): Note: Purchases require written justification that demonstrates cost benefits over leasing or renting. |  |
| TOTAL EQUIPMENT PURCHASE, LEASE OR RENTAL COST |  |
| MATERIALS AND SUPPLIES (Item @ Cost/Each X Quantity X #Fiscal Years = Cost/Item): |  |
| (see CONTRACT COST) |  |
| TOTAL MATERIALS AND SUPPLY COST |  |

| TRAVEL COST (Personnel or Equipment @ Rate X Round Trips X #Fiscal Years = Cost/Item): |  |
| --- | --- |
| One truck for Implementation Leader for 2 days (truck: $80; fuel: $100) | $180 |
| One truck for Engineer Tech for 7 days (truck: $280; fuel: $350) | $630 |
| One truck for Archeologist for 3 days (truck: $120; fuel: $150) | $270 |
| TOTAL TRAVEL COST | $1,080 |

| CONTRACT COST (Labor AND Equipment AND Materials @ Cost/Hour X #Hours X #Fiscal Years = Cost/Item): |  |
| --- | --- |
| Site 1 - Road #751-1 Replace 18-inch culvert with 24-inch culvert 24-feet long | $2,880 |
| Site 2 - Road #751-4 Replace 18-inch culvert with 24-inch culvert 30-feet long | $3,600 |
| Site 3 - Road #751-7 Replace 12-inch culvert with 18-inch culvert 22-feet long | $2,200 |
| Site 4 - Road #067-6 Replace 24-inch culvert with 36-inch culvert 30-feet long | $4,500 |
| Site 5 - Road #668-1 Replace 24-inch culvert with 36-inch culvert 30-feet long | $4,500 |
| Site 6 - Road #745-1 Replace 18-inch culvert with 24-inch culvert 30-feet long | $3,600 |
| Site 7 - Road #745-7 Replace 18-inch culvert with 24-inch culvert 30-feet long | $3,600 |
| Site 8 - Road #067-2 Replace 36-inch culvert with 36-inch culvert 30-feet long | $4,500 |
| Site 9 - Road #745-4 Replace 36-inch culvert with 36-inch culvert 30-feet long | $4,500 |
| TOTAL CONTRACT COST | $33,880 |
| SPECIFICATION COST SUMMARY |
| FISCAL YEAR | PLANNED INITIATION DATE (M/D/YYYY) | PLANNED COMPLETION DATE (M/D/YYYY) | WORK AGENT | UNITS | UNIT COST | PLANNED ACCOMPLISHMENTS | PLANNED COST |
| FY07 | 30 August 2007 | 30 September 2007 | F, S | sites | $5,134 | 5 sites | $25,670 |
| FY08 | 1 October 2007 | Before winter snow sets in | F, S | sites | $5,134 | 4 sites | $20,534 |
| FY08 |  |  |  |  |  |  |  |
| FY09 |  |  |  |  |  |  |  |
| TOTAL | $46,204 |

Work Agent: C=Coop Agreement, F=Force Account, G=Grantee, P=Permittees, S=Service Contract, T=Timber Sales Purchaser, V=Volunteer

SOURCE OF COST ESTIMATE

| 1. Estimate obtained from 2-3 independent contractual sources. |  |
| --- | --- |
| 2. Documented cost figures from similar project work obtained from local agency sources. | P, C, T |
| 3. Estimate supported by cost guides from independent sources or other federal agencies |  |
| 4. Estimates based upon government wage rates and material cost. |  |
| 5. No cost estimate required - cost charged to Fire Suppression Account |  |

P = Personnel Services,   E = Equipment   M = Materials/Supplies,   T = Travel,   C = Contract,   F = Suppression

RELEVANT DETAILS, MAPS AND DOCUMENTATION INCLUDED IN THIS PLAN:

See Appendix I, Soil and Water Resources Assessment; See Appendix IV, Watershed Treatments Map.

TOTAL COST BY JURSIDICTION

| JURISDICTION | UNITS TREATED | COST |
| --- | --- | --- |
| USFS, Humboldt-Toiyabe National Forest |  | $46,204 |
|  | TOTAL COST | $46,204 |