PHOTOS – SOIL AND WATERSHED

High soil burn severity along riparian corridor and low soil              Riparian condition and sheet erosion resulting

burn severity with greenup on floodplain in Bruneau Canyon          from  first post-fire storm in upper Bruneau Canyon

Four-inch depth of erosion on debris cone during                 Road #067 wash out and channel scour on debris cone

first post-fire storm.                                                                at Little Cottonwood Creek

Ash and mud deposition on floodplain from first post-fire       Plugged culvert outlet on Road #751

storm