PART F - INDIVIDUAL TREATMENT SPECIFICATION

| TREATMENT/ACTIVITY NAME | Protective Fencing | PART E BLM Spec- S 7 | #8_Protective Fence |
| --- | --- | --- | --- |
| NFPORS TREATMENT CATEGORY* | Facility & Infrastructure | FISCAL YEAR(S) (list each year): | 2008 |
| NFPORS TREATMENT TYPE * | Fence Replacement/Repair | WUI? Y / N | Y |
| IMPACTED COMMUNITIES AT RISK | N/A | IMPACTED T&E SPECIES | Quino checkerspot butterfly |

* See NFPORS Restoration & Rehabilitation module - Edit Treatment screen for applicable entries.

WORK TO BE DONE (describe or attach exact specifications of work to be done):

A. General Description: Construct new permanent fences or repair existing fences to protect recovery of known habitat for the Quino Checkerspot butterfly, a listed T&E species, and prevent access to recovering areas by Off Highway Vehicles (OHV’s). The 2.00 miles of fence proposed for replacement are located along the Marron Valley Road (1.5 miles) and along Highway 94 (.5 miles). The fences are necessary to insure public safety for travelers along or within public lands, by preventing access back and forth from BLM lands to the roads by unauthorized OHV’s. An additional 150 feet of fence will be repaired and a gate installed on the Donohoe Spur Road. The fences will be re-constructed or repaired at the same site where previously located. Burned fence materials will be removed from the site before re-construction begins. B. Location/(Suitable) Sites: Fences will be constructed where damaged and where the need exists to insure public safety by keeping OHV’s from running onto roadways, from Bureau of Land Management (BLM) lands adjacent to the roadways, or to prevent access by OHV’s on recovering known habitat critical to listed T&E species, on BLM lands within the perimeter of the Harris Fire in southern San Diego County. Miles of fence to be constructed or repaired are approximate and located either along Highway 94 or the Marron Valley Road, which heads south from the intersection with Highway 94. This fencing is proposed to protect known habitat for the Quino Checkerspot butterfly, a listed T&E species, and to protect areas recovering from the fire, which may be impacted by OHV’s, a potentially significant public safety hazard. See the Vegetation Map in Appendix IV for actual fence location. C. Design/Construction Specifications: Fence construction shall be in accordance with standard BLM design specifications. This fence will protect critical habitat for listed T&E species and to provide public safety by preventing access to recovering areas, the minimum fence specification needed to meet objectives in this area is a 4-strand wire fence, with 3 strands of barbed wire and 1 strand of smooth wire. A 4-strand wire fence is justified based on the critical habitat and public safety issues involved. New fence materials shall be utilized. Construct 4-strand wire fence along Marron Valley Road and at repair points along Highway 94 consisting of 3 strands of 12 ½ gauge twisted barbed wire and a bottom or top strand, depending on needs, of 12 ½ gauge twisted smooth wire. Steel 6 foot T-posts shall be driven 1 ½ feet in the ground and spaced at 16 ½ feet apart. Wood posts shall be placed at all corners or at a maximum of 1/8 mile spacing or as necessary to compensate for topographical undulations. Posts are to be secured using 12 ½ gauge smooth twisted steel wire with a minimum breaking strength of 950 pounds of force. Install gate on the Donohue Spur Road at previous gate location. Additional specifications regarding fence replacement will be provided at time of reconstruction initiation. Remove all pre-existing burned and unburned fence materials, including wire, posts, staples and nails. D. Purpose of Treatment Specifications (relate to damage/change caused by fire): Protective fences may be constructed using emergency stabilization funds to protect burned areas (from impacts from wildlife, domestic livestock, wild horses, or humans and for the health and safety of agency personnel and the public) during the recovery period for burned vegetation or the establishment period for new seedlings. Fences can also be used to protect recovering designated critical habitat for listed T&E species. E. Treatment consistent with Agency Land Management Plan (identify which plan): Interagency Burned Area Emergency Response Guidebook, Part 4.2.6, Federal Field Unit Infrastructure; Fencing; DOI Manual, DM Part 620, Chapter 3; and BLM Handbook H-1742-1, Burned Area Emergency Stabilization and Rehabilitation Handbook, Part III B 10, Fences, Cattleguards, and Gates. South Coast Management Plan, 1994 F. Treatment Effectiveness Monitoring Proposed: The treatment will be considered successful if OHV’s encursion is prevented from the burned area during the 3-year prescribed recovery period, and designated critical habitat for the Quino Checkerspot butterfly, a listed T&E species, is allowed to recover without disturbance. (See Vegetation Resources Assessment for details)

LABOR, MATERIALS AND OTHER COST:

|  | COST / ITEM |
| --- | --- |
| Natural Resource Specialist: GS-09/5 @ $34.40/hr. X 8 hrs./day X 10 days X 1 year | $2,752 |
| Archeologist: GS-09/5 @ $34.40/hr. X 8 hrs./day 3 days X 1 year | $826 |
| Project Manager: GS-12/6 @ $51.30/hr. X 8 hrs./day X 1 day X 1 year | $411 |
| TOTAL PERSONNEL SERVICE COST | $3,989 |
| EQUIPMENT PURCHASE, LEASE AND/OR RENT (Item @ Cost/Hour X # of Hours X #Fiscal Years = Cost/Item): Note: Purchases require written justification that demonstrates cost benefits over leasing or renting. |  |
| Vehicle for Natural Resource Specialist @ $200/week X 3 weeks X 1 year | $600 |
| Vehicle for Archeologist @ $200/week X 1 week X 1 year | $200 |
| TOTAL EQUIPMENT PURCHASE, LEASE OR RENTAL COST | $800 |
| MATERIALS AND SUPPLIES (Item @ Cost/Each X Quantity X #Fiscal Years = Cost/Item): |  |
| 12 ½ gauge galvanized twisted two-point barbed wire: $65.63/roll X 12 rolls/mile X 2.00 miles X 1 year | $1,576 |
| 12 ½ gauge galvanized twisted smooth wire: $54.00/roll X 4 rolls/mile X 2.00 miles X 1 year | $432 |
| 6 foot steel painted T-posts: $3.71/post X 320 posts/mile X 2.00 miles X 1 year | $2,375 |
| 36” wire fence stays: $21.90/bundle X 6.4 bundles/mile X 2.00 miles X 1 year | $281 |
| Wire fence clips (50/pk): $1.69/pk X 26 pks/mile X 2.00 miles X 1 year | $88 |
| 6 foot X 6” diameter wooden brace posts: $6.97/post X 27 posts/mile X 2.00 miles X 1 year | $377 |
| Pre-fabricated Gate: 1 gate @ $900/gate X 1 year | $900 |
| Fence repair at Donohoe Spur Road (materials): | $500 |
| TOTAL MATERIALS AND SUPPLY COST | $6,529 |
| TRAVEL COST (Personnel or Equipment @ Rate X Round Trips X #Fiscal Years = Cost/Item): |  |
| Per Diem: Natural Resource Specialist: 2 weeks X $848/week X 1 year | $1,696 |
| Per Diem: Archeologist: .5 week X $848/week X 1 year | $424 |
| TOTAL TRAVEL COST | $2,120 |
| CONTRACT COST (Labor or Equipment @ Cost/Hour X #Hours X #Fiscal Years = Cost/Item): |  |
| Fencing Cost for Installation: $7,000/mile X 2.00 miles X 1 year | $14,000 |
| Fencing Cost for Removal: $2,000/mile X 2.00 miles X 1 year | $4,000 |
| TOTAL CONTRACT COST | $18,000 |

| SPECIFICATION COST SUMMARY |
| --- |
| FISCAL YEAR | PLANNED INITIATION DATE (M/D/YYYY) | PLANNED COMPLETION DATE (M/D/YYYY) | WORK AGENT | UNITS | UNIT COST | PLANNED ACCOMPLISHMENTS | PLANNED COST |
| FY 08 | 12/01/2007 | 09/30/2008 | S | Miles | $15,490 | 2.03 | $31,438 |
| TOTAL | $31,438 |

Work Agent: C=Coop Agreement, F=Force Account, G=Grantee, P=Permittees, S=Service Contract, T=Timber Sales Purchaser, V=Volunteer

SOURCE OF COST ESTIMATE

| 1. Estimate obtained from 2-3 independent contractual sources. |  |
| --- | --- |
| 2. Documented cost figures from similar project work obtained from local agency sources. | M, C |
| 3. Estimate supported by cost guides from independent sources or other federal agencies | E |
| 4. Estimates based upon government wage rates and material cost. | P |
| 5. No cost estimate required - cost charged to Fire Suppression Account |  |

P = Personnel Services,   E = Equipment   M = Materials/Supplies,   T = Travel,   C = Contract,   F = Suppression

RELEVANT DETAILS, MAPS AND DOCUMENTATION INCLUDED IN THIS REPORT:

See Appendix I, Vegetation Resource Assessment; See Appendix IV, Vegetation Treatment Map.

TOTAL COST BY JURSIDICTION

| JURISDICTION | Poomacha | Harris | Witch | UNITS TREATED | COST |
| --- | --- | --- | --- | --- | --- |
| BLM (Mi) |  | 2.03 |  | 2.03 | $31,438 |
| TOTAL COST |  | $31,438 |  | 2.03 | $31,438 |