PART F - INDIVIDUAL TREATMENT SPECIFICATION

| TREATMENT/ACTIVITY NAME | Install Drain Outlets | PART E FWS Spec-# | 14 FWS Place Road Drain Outlets |
| --- | --- | --- | --- |
| NFPORS TREATMENT CATEGORY* | Roads | FISCAL YEAR(S) (list each year): | 2008 |
| NFPORS TREATMENT TYPE * | Culverts | WUI? Y / N | N |
| IMPACTED COMMUNITIES AT RISK | San Diego National Wildlife Refuge | IMPACTED T&E SPECIES | NA |

* See NFPORS Restoration & Rehabilitation module - Edit Treatment screen for applicable entries.

WORK TO BE DONE (describe or attach exact specifications of work to be done):

A. General Description: Drain outlets are placed in locations in places where sheet flow from the road is concentrated on the embankments (fill slopes) that need protection. Drain outlets are constructed from a sheet metal headwall with a 24 inch sheet metal transition attached to an 18 inch CMP cut in half longwise. See page 118, Figure 70 of BAER Treatments Catalog (Dec. 2006) B. Location/(Suitable) Sites: Three sites on Millar Ranch Road, the nearest cross street is Campo Road, south of Jamacha Junction. See Values-at-Risk table, treatment maps and GPS reference coordinates. C. Design/Construction Specifications: Headwall dimensions to be 24 inches tall and 66 inches wide with a 3 inch 90 degree flange (opposite side from CMP). Invert of transition to be centered and 18 inches from the top edge of the headwall. Earth to be well compacted against headwall when installed. Compacted asphalt shall smoothly transition from the roadway to invert in the headwall. Outlet of the CMP should discharge in a 3 ft square area of hand placed 6 inch average diameter rocks to dissipate flows. CMP to be 10 ft long and field cut to fit the length of the embankment slope. CMP shall be continuously supported on the embankment slope D. Purpose of Treatment Specifications (relate to damage/change caused by fire): The drain outlets will prevent erosion on fill slopes of the road. The burned area will contribute additional water laden with ash and sediment. Water bars concentrate the flow which increases the risk of erosion on the embankment slope. E. Treatment consistent with Agency Land Management Plan (identify which plan): Environmental Assessment and Land Protection Plan for Otay-Sweetwater Unit of San Diego National Wildlife Refuge, San Diego County, California. F. Treatment Effectiveness Monitoring Proposed: Inspect drain outlets and repair soil erosion after major storm events.

LABOR, MATERIALS AND OTHER COST:

| PERSONNEL SERVICES: (Grade @ Cost/Hours X # Hours X # Fiscal Years = Cost/Item): Do not include contract personnel costs here (see contractor services below). | COST / ITEM |
| --- | --- |
| F&WS engineering review and contract administration (18%) | $694 |
| TOTAL PERSONNEL SERVICE COST | $694 |
| EQUIPMENT PURCHASE, LEASE AND/OR RENT (Item @ Cost/Hour X # of Hours X #Fiscal Years = Cost/Item): Note: Purchases require written justification that demonstrates cost benefits over leasing or renting. |  |
| TOTAL EQUIPMENT PURCHASE, LEASE OR RENTAL COST |  |
| MATERIALS AND SUPPLIES (Item @ Cost/Each X Quantity X #Fiscal Years = Cost/Item): |  |
| Drain outlet @ $600 / Drain outlet X 3 Num of Drain outlets | $1,800 |
| TOTAL MATERIALS AND SUPPLY COST | $1,800 |
| TRAVEL COST (Personnel or Equipment @ Rate X Round Trips X #Fiscal Years = Cost/Item): |  |
| Mob and De-mob @$1,000 x 1 once x 1 FY | $400 |
| TOTAL TRAVEL COST | $400 |
| CONTRACT COST (Labor or Equipment @ Cost/Hour X #Hours X #Fiscal Years = Cost/Item): |  |
| Contract Labor Installation @ $260 / Drain outlet X 3 Num of Drain outlets | $780 |
| Contract rock placement @ $60 / Drain outlet X 3 Num of Drain outlets | $180 |
| TOTAL CONTRACT COST | $960 |

| SPECIFICATION COST SUMMARY |
| --- |
| FISCAL YEAR | PLANNED INITIATION DATE (M/D/YYYY) | PLANNED COMPLETION DATE (M/D/YYYY) | WORK AGENT | UNITS | UNIT COST | PLANNED ACCOMPLISHMENTS | PLANNED COST |
| FY 2008 | 12/2007 | 02/2008 | S | each | $1151 | 3 | $3,454 |
| FY 2008 | 12/2007 | 02/2008 | S | each | $400 | 1 | $400 |
| TOTAL | $3,840 |

Work Agent: C=Coop Agreement, F=Force Account, G=Grantee, P=Permittees, S=Service Contract, T=Timber Sales Purchaser, V=Volunteer

SOURCE OF COST ESTIMATE

| 1. Estimate obtained from 2-3 independent contractual sources. |  |
| --- | --- |
| 2. Documented cost figures from similar project work obtained from local agency sources. | M, T, C |
| 3. Estimate supported by cost guides from independent sources or other federal agencies |  |
| 4. Estimates based upon government wage rates and material cost. |  |
| 5. No cost estimate required - cost charged to Fire Suppression Account |  |

P = Personnel Services,   E = Equipment   M = Materials/Supplies,   T = Travel,   C = Contract,   F = Suppression

RELEVANT DETAILS, MAPS AND DOCUMENTATION INCLUDED IN THIS REPORT:

See Watershed Assessment, Appendix I. See Watershed Treatment Map, Appendix IV

TOTAL COST BY JURSIDICTION

| JURISDICTION | Poomacha | Harris | Witch | UNITS TREATED | COST |
| --- | --- | --- | --- | --- | --- |
| FWS |  | $3,840 |  | 3 | $3,840 |
| TOTAL COST |  | $3,840 |  | 3 | $3,840 |

Metal Overside Drain. Page 118, Figure 70 of BAER Treatments Catalog (Dec. 2006)