PART F - INDIVIDUAL TREATMENT SPECIFICATION

| TREATMENT/ACTIVITY NAME | Road Maintenance/Debris Removal | PART E FWS Spec-# | 18 FWS Road Debris Removal |
| --- | --- | --- | --- |
| NFPORS TREATMENT CATEGORY* | Roads | FISCAL YEAR(S) (list each year): | 2008 |
| NFPORS TREATMENT TYPE * | Hazard/Debris Removal | WUI? Y / N | N |
| IMPACTED COMMUNITIES AT RISK | San Diego National Wildlife Refuge | IMPACTED T&E SPECIES | NA |

* See NFPORS Restoration & Rehabilitation module - Edit Treatment screen for applicable entries.

WORK TO BE DONE (describe or attach exact specifications of work to be done):

A. General Description: During major storm events low water crossings, culverts, and other sections of roadways can be expected to flood or experience significant surface erosion as a result of the effects to watershed conditions from the fires. Flood events will erode and/or deposit sediment, organic debris, and boulders on roadways and making them impassable and unsafe. This specification provides for maintenance and removal of sediment and debris from USFWS Refuge roadways. B. Location/(Suitable) Sites: See Watershed Treatment Map, Appendix IV. C. Design/Construction Specifications: Use front end load and/or tracked excavator with dump truck to clear sediment and debris removal from roadways after major storm events. Deposit removed material out of the floodplain on to higher ground to prevent any transport of material back into channels which could eventually move back onto roadways. D. Purpose of Treatment Specifications (relate to damage/change caused by fire): Increased runoff and sediment debris delivery to refuge transportation infrastructure. E. Treatment consistent with Agency Land Management Plan (identify which plan): Environmental Assessment and Land Protection Plan for Otay-Sweetwater Unit of San Diego National Wildlife Refuge, San Diego County, California. F. Treatment Effectiveness Monitoring Proposed: Inspect roadways after major storm events to determine if additional treatment is required.

LABOR, MATERIALS AND OTHER COST:

| PERSONNEL SERVICES: (Grade @ Cost/Hours X # Hours X # Fiscal Years = Cost/Item): Do not include contract personnel costs here (see contractor services below). | COST / ITEM |
| --- | --- |
| WG-10 or equivalent, Equipment Operators: 2 @ $33.50/hour x 10 hours x 4 flood events = | $2,680 |
| Backhoe @ $85/hour x 10 hours x 4 flood events = | $3,400 |
| Dump truck @ $65/hour x 10 hours x 4 flood events = | $2,600 |
| Move in/out @ $150/hour x 4 hours x 4 flood events = | $2,400 |
| TOTAL PERSONNEL SERVICE COST | $11,080 |
| EQUIPMENT PURCHASE, LEASE AND/OR RENT (Item @ Cost/Hour X # of Hours X #Fiscal Years = Cost/Item): Note: Purchases require written justification that demonstrates cost benefits over leasing or renting. |  |
| TOTAL EQUIPMENT PURCHASE, LEASE OR RENTAL COST |  |
| MATERIALS AND SUPPLIES (Item @ Cost/Each X Quantity X #Fiscal Years = Cost/Item): |  |
| TOTAL MATERIALS AND SUPPLY COST |  |
| TRAVEL COST (Personnel or Equipment @ Rate X Round Trips X #Fiscal Years = Cost/Item): |  |
| TOTAL TRAVEL COST |  |
| CONTRACT COST (Labor or Equipment @ Cost/Hour X #Hours X #Fiscal Years = Cost/Item): |  |
| TOTAL CONTRACT COST |  |

| SPECIFICATION COST SUMMARY |
| --- |
| FISCAL YEAR | PLANNED INITIATION DATE (M/D/YYYY) | PLANNED COMPLETION DATE (M/D/YYYY) | WORK AGENT | UNITS | UNIT COST | PLANNED ACCOMPLISHMENTS | PLANNED COST |
| 2008 | 12/1/2007 | 9/30/2008 | F | Job | $2,667 | 4 | $11,080 |
| TOTAL | $11,080 |

Work Agent: C=Coop Agreement, F=Force Account, G=Grantee, P=Permittees, S=Service Contract, T=Timber Sales Purchaser, V=Volunteer

SOURCE OF COST ESTIMATE

| 1. Estimate obtained from 2-3 independent contractual sources. |  |
| --- | --- |
| 2. Documented cost figures from similar project work obtained from local agency sources. |  |
| 3. Estimate supported by cost guides from independent sources or other federal agencies |  |
| 4. Estimates based upon government wage rates and material cost. | P, E |
| 5. No cost estimate required - cost charged to Fire Suppression Account |  |

P = Personnel Services,   E = Equipment   M = Materials/Supplies,   T = Travel,   C = Contract,   F = Suppression

RELEVANT DETAILS, MAPS AND DOCUMENTATION INCLUDED IN THIS REPORT:

See Watershed Assessment, Appendix I. See Watershed Treatment Map, Appendix IV

TOTAL COST BY JURSIDICTION

| JURISDICTION | Poomacha | Harris | Witch | UNITS TREATED | COST |
| --- | --- | --- | --- | --- | --- |
| FWS |  | $11,080 |  | 4 | $11,080 |
| TOTAL COST |  | $11,080 |  | 4 | $11,080 |