USGS National Flood Frequency (NFF) Program Results for Peak Discharges with Return Intervals of 2, 5, 10, 25, 50, 100, and 500-years for selected watersheds within the Poomacha Fire, San Diego County, California.  Post-fire peak discharges presented reflect a 5-fold increase over unburned conditions.

Refer to the Runoff Analysis Watershed Map located in Appendix IV for locations of watersheds listed in the table below.

| Watershed / Value-at-Risk | Drainage Area (Sq. Miles) | Mean Annual Precip* (inches) | Pre-fire 2-yr Discharge (cfs) | Post-fire 2-yr Discharge (cfs) | Pre-fire 5-yr Discharge (cfs) | Post-fire 5-yr Discharge (cfs) | Pre-fire 10-yr Discharge (cfs) | Post-fire 10-yr Discharge (cfs) | Pre-fire 25-yr Discharge (cfs) | Post-fire 25-yr Discharge (cfs) | Pre-fire 50-yr Discharge (cfs) | Post-fire 50-yr Discharge (cfs) | Pre-fire 100-yr Discharge (cfs) | Post-fire 100-yr Discharge (cfs) | Pre-fire 500-yr Discharge (cfs) | Post-fire 500-yr Discharge (cfs) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Adams / PA01 | 0.3 | 22.5 | 9 | 46 | 31 | 153 | 57 | 283 | 116 | 580 | 177 | 885 | 242 | 1,210 | 534 | 2,670 |
| Aqua Tibia / Wilderness Gardens | 4.92 | 25.2 | 82 | 411 | 319 | 1,595 | 629 | 3,145 | 1,380 | 6,900 | 2,170 | 10,850 | 3,050 | 15,250 | 7,070 | 35,350 |
| Cedar Creek / La Jolla Campground | 2.96 | 37.6 | 109 | 545 | 424 | 2,120 | 848 | 1,880 | 1,880 | 9,400 | 3,000 | 15,000 | 4,230 | 21,150 | 10,100 | 50,500 |
| East Amago Canyon / Hwy 76 bridge | 1.65 | 40 | 79 | 396 | 300 | 1,500 | 595 | 2,975 | 1,310 | 6,550 | 2,080 | 10,400 | 2,930 | 14,650 | 6,940 | 34,700 |
| Frey Creek / Wilderness Gardens | 4 | 25.5 | 72 | 361 | 277 | 1,385 | 545 | 2,725 | 1,190 | 5,950 | 1,870 | 9,350 | 2,630 | 13,150 | 6,070 | 30,350 |
| Jaybird Creek / RP52 | 0.51 | 24.5 | 15 | 77 | 53 | 265 | 100 | 500 | 208 | 1,040 | 321 | 1,605 | 442 | 2,210 | 988 | 4,940 |
| Paradise Creek / JH16 | 8.97 | 22.5 | 105 | 525 | 418 | 2,090 | 829 | 4,145 | 1,820 | 9,100 | 2,880 | 14,400 | 4,070 | 20,350 | 9,400 | 47,000 |
| Pauma Creek / Community of Pauma | 10.9 | 28.1 | 174 | 870 | 707 | 3,535 | 1,430 | 7,150 | 3,190 | 15,950 | 5,090 | 25,450 | 7,250 | 36,250 | 17,100 | 85,500 |
| Upper Potrero / RP21 | 0.77 | 37.8 | 42 | 209 | 152 | 760 | 295 | 1,475 | 638 | 3,190 | 1,000 | 5,000 | 1,400 | 7,000 | 3,260 | 16,300 |
| Reservoir Channel / BR01 with tire dump site | 0.45 | 24.2 | 14 | 69 | 47 | 236 | 89 | 443 | 184 | 920 | 283 | 1,415 | 389 | 1,945 | 868 | 4,340 |
| West Amago Canyon / Hwy 76 bridge | 0.55 | 37.2 | 32 | 160 | 114 | 570 | 220 | 1,100 | 472 | 2,360 | 739 | 3,695 | 1,030 | 5,150 | 2,380 | 11,900 |
| Yuimo Creek / Community of Rincon | 4.34 | 29.2 | 95 | 477 | 371 | 1,855 | 737 | 3,685 | 1,620 | 8,100 | 2,570 | 12,850 | 3,630 | 18,150 | 8,480 | 42,400 |
| San Luis Rey River / Casino and bridge on Valley Center Road** | 246 | 23.5 | 1,230 | 6,150 | 5,760 | 28,800 | 12,200 | 61,000 | 28,900 | 144,500 | 47,200 | 236,000 | 69,000 | 345,000 | 168,000 | 840,000 |

* Mean Annual Precipitation as specified in Rantz (1969)

** Drainage area upstream of Henshaw Reservoir included.