Tip Sheet

Quick tips for working with BARC data.  These are in no particular order.

- To view .tif or .img files in ArcView, turn on the Imagine and Tiff extensions.

- Landsat image files are best viewed using bands RGB = 6,4,3. ASTER image files are best viewed using bands RGB = 6,3,2.  AWiFS files should be viewed RGB = 4,3,2.

- The BARC raster files are color coded as follows:  dark green for unburned / very low, aquamarine for low, yellow for moderate, and red for high.

- The BARC (Burned Area Reflectance Classification) is based on satellite reflectance values.  Any correlation to soil burn severity requires field validation.

- The image files and preliminary severity classifications are generally georeferenced to UTM NAD 83, USGS Albers, or other projections as specified.

- The BARC classifications should be reviewed and edited by BAER teams during the course of the initial assessment.

- Image resolution is typically 30 meters when Landsat imagery is used. If alternative imagery sources such as AWiFS, ASTER, SPOT, or many other commercial and public sensor systems are used spatial resolution can vary from sub meter to 56 meters and larger.

- More information about BARC data can be obtained from the joint USFS RSAC/USGS EROS BAER Imagery Support website.

http://www.fs.fed.us/eng/rsac/baer/

If you have questions that remain unanswered after consulting these documents, please call Jess Clark (801-975-3769) at the Forest Service Remote Sensing Applications Center or Randy McKinley (605-594-2745) at USGS EROS.