## Slide 1
Unit 9
Infrared Product Generation

## Slide 2: Objectives
Discuss exercises
Identify nightly workflow for IRIN
Discuss IR imagery packet
Identify correct symbology
Interpret infrared imagery

## Slide 3: Class Exercises
Cold Springs, CO 2016 (hardcopy)
Berry, WY 2016 (hardcopy & digital)
Dog Head, NM 2016
Rock Mountain, GA/NC 2016
Camp, CA 2018
Assayii Lake, NM 2014
Final, ? 2018
Notes: Exercises provide a range of vegetation types and topographic settings

## Slide 4: Exercises
Raise hand as you have questions
“Solution” is provided for checking
  May be more than one solution
  Key is to map all valid heat sources
Scale for digitizing should be in the range of 1:10,000 to 1:20,000
  Will vary with size of fire and how much time you have
  Digitize areas or points of heat, not pixels

## Slide 5
The Work Cycle of an IRIN:
Scanner Request Submitted
By SITL or IRIN using
Online Ordering
Go to bed
(ROSS A# assigned)
ZZZZZZZZZZZ
Wake up
Check on flight
Expanded dispatch,
AFF, IRCN, IRCR
Imagery Delivered:
Upload to FTP site
Interpretation:
Create Products
Accurate Shapefiles / Maps/Log/KMZ
Delivered to IMT Before
Morning Briefing
IRIN Determines
w/ SITL
Additional Flight
Eat, get ready
FLIGHT
Your schedule will change nightly.
Notes: The work cycle makes it problematic for anyone to do IRIN work (given our standard period of operations) in addition to daytime work whether it be GIS, aerial detection and mapping, etc.
Your schedule will change nightly.

## Slide 6: IRIN work – before getting imagery
  AM – brief SITL and submit order for next night
  Get end of day briefing from SITL
    Areas of concern/perimeter growth
    Acquire additional base imagery?
    Arrange to get most recent perimeter
  Track plane and techs twitter feed to know when/what to expect
    Inform incident of general flight time
    Fire not flown, # and orientation of runs
  Prepare new shapefiles/folders using naming conventions
    Blank for intense/scattered/isolated heat
    Copy previous perimeter into new perimeter shapefile
    Set/copy projections, leave time/date as xxxx
    Or use Create IR shapefile tool
  Get map layout ready to go

## Slide 7: IRIN work – after getting imagery
Enter correct date/time stamp for shapefile names and map legend
Bring in *ortho.tifs to *.mxd and check for coverage, image quality, alignment with base imagery – every night, every run
  Color.tifs are created from ortho tifs so if ortho tif lines up, the color will as well
Get overall sense of how much heat there is to map and what your timeframe is
If time is tight, digitize priority areas/products first
Raw heat data shapefile useful for
  Ensuring you’ve covered everything especially outside perimeter
When done digitizing - clear all selections, calculate acres, turn off layers not needed in map
Produce pdf file, kmz, fill out log, zip shapefiles and post to NIFC ftp site

## Slide 8: Getting Your Imagery
Imagery is posted at ftp://ftp.nifc.gov/nirops
  Password protected
  Access via secure ftp client (WinSCP, Filezilla etc.)
  Posted as FreeArc self-extracting file *.exe
    Example 130902_2216_CORRAL_COMPLEX.exe
  Each run posted individually
  Wait until tech tweets that imagery is posted!

## Slide 9: Image Packet
Orthocorrected tifs “*_ortho.tif”
Color tifs “*_color.tif”
  Also orthocorrected
Mosaic .jpg
  Good for quick view, no geo information
Raw Heat Data Shapefile – contains triggered pixels from all runs
Metadata file

## Slide 10: Example Image Packet

## Slide 11: Ortho vs Color tif
Two channel thermal IR line scanner
  3-5 μm band for intense heat/fire detection
  8-12 μm band for background terrain
Ortho tif (gray-scale image)
  8-12 μm shown along with red pixels represented trips from fire detection algorithm and post processing
Color tif
  8-12 μm background terrain assigned to green
  3-5 μm assigned to red
  Non-fire/cooler areas appear green
  Hotter/fire areas appear orange/yellow

## Slide 12
Notes: 180609_2059_416_fire_b2_1_ortho.tif

## Slide 13: Image Orientation
Ortho.tif and color.tif will line up correctly in ArcMap
Not the case in other software like Windows PhotoViewer
  Don’t rotate in other viewers

## Slide 14: IR Shapefile Symbology
Symbology is in the GSTOP
Make perimeter outline thicker than intense and scattered heat
Rename shapefiles in
layout

## Slide 15: IR GIS Products– in order of priority
Heat Perimeter (polygon)
Isolated Heat Sources Outside Perimeter (points)*
Intense Heat (polygon)
Isolated Heat Sources Inside Perimeter (points)*
Scattered Heat (polygon)
*Should be in same file
Notes: Every data layer will be produced, if applicable, regardless of what is requested by an individual SITL.

## Slide 16: Projections
Use whatever the incident is using
  e.g. NAD83 Calif Teale Albers,
When in doubt use UTM NAD83
  First night of a fire, no previous perimeter, no GISS support, etc.
Never calculate acres in Web Mercator Auxiliary Sphere (doubles UTM acres)
Notes: CalFire uses NAD83 California Teale Albers

## Slide 17: Projections (cont.)
NIFS* perimeters are GCS WGS84
Not a projection so can’t calculate acres
Calculate acres from data frame projection
Do not reproject – leads to “sliver” issues
*National Incident Feature Service

## Slide 18: Late Flights
Inform SITL/GISS of schedule
Discuss strategy
Post rough perimeter first, focused on areas of greatest growth and concern
Follow up with more detailed products
On Type 1 & 2 fires, looking for the IR products by 0430

## Slide 19: Interpretation
Scattered/intense/isolated?
  Geographic concentration of heat
  Polygon or point?
  Consider scale of map
  How much time you have
Greater detail at leading edge
Remember priorities
Notes: This what we will work with you on during the exercises. Only so much you can show in a powerpoint.

## Slide 20: Image Only

## Slide 21: Perimeter Added
Notes: If it’s a polygon, it should be part of the perimeter

## Slide 22: Isolated, Intense, and Scattered
Notes: IRIN uses best, “closest to nadir”, run for mapping so mapped heat may not match up exactly with what you see in this one run

## Slide 23: Map

## Slide 24
Notes: Thompson Ridge fire 20130605_0038. Fire grew 5,000 acres on this night to just under 10,000 acres. This shows just a portion of the fire.

## Slide 25
Notes: Thompson Ridge fire 20130605_0038. Fire grew 5,000 acres on this night to just under 10,000 acres. This shows just a portion of the fire.

## Slide 26
Notes: Assayii Lake fire NM 2014

## Slide 27
Notes: Perimeter at lower left is from previous incident provided perimeter

## Slide 31
Notes: Isolated heat sources outside western edge not mapped because they were not in the color tiff.

## Slide 32
Note: Any polygon should be included in perimeter file
Need to be in perimeter file
Notes: Add a grid with latitude and longitude use ticks or lines.

## Slide 33: Objectives
Discuss exercises
Identify nightly workflow for IRIN
Discuss IR imagery packet
Identify correct symbology
Interpret infrared imagery

## Slide 34: QUESTIONS?